The VPLOT Combination User's, Installation, and Reference Manual

                                for Version 2.0

                                       by
                                   M. Gooley
                      Millikin University Computer Center
                              Millikin University
                            Decatur, Illinois 62522










        Copyright (C) 1981 by M.  Gooley.  This manual and the  software
        it describes are distributed without cost, and may be reproduced
        only with the inclusion of this copyright statement.  The author
        assumes no responsibility for the accuracy of this manual or the
        performance of the software.

VPLOT Guide                                                       Page 2


        I.  What is VPLOT?


             VPLOT is a package  of  VAX-11  FORTRAN  and  VAX-11  MACRO
        routines  that  enables a PRINTRONIX 300 printer to mimic a drum
        plotter (the Calcomp Model  565,  according  to  my  circa  1969
        information).  VPLOT includes these files:

            VPLOT.FOR:    Imitations of CalComp's Basic Software:
                Subroutines and Entries:
                    PLOTS - initialisation and output
                    PLOT - single lines, pen motions, output
                    FACTOR - changes scale of plot
                    WHERE - tells user's program the current "pen"
                    location and scaling-factor
                    SYMBOL - draws single symbols or character strings
                    NUMBER - draws numbers of given precision
                    SCALE - scales data arrays to axes
                    AXIS - draws numbered, titled axes
                    LINE - draws line between data points given in two
                    arrays
                    [plus sundry sub-subroutines and functions]

            Copies of bits of Calcomp's Functional Software:
                Subroutines:
                    CIRCL - draws circles, Archimedean spirals, and
                    circular arcs
                    ELIPS - draws ellipses and elliptical arcs
                    GRID - draws rectangular grids which are guaranteed
                    to cause eyestrain
                    POLY - draws regular polygons and stars
                    DASHP - resembles PLOT but draws dashed lines
                    DASHL - resembles LINE but draws dashed lines
                    RECT - draws rectangles
                    POLAR - resembles LINE but works in polar
                    coordinates
                    [plus sundry sub-subroutines and functions]

            MACPLOT.MAR: Three VAX-11 MACRO routines:
                    INITIAL - INITIALisation; also sets up a table to
                    store addresses of parts of a huge phantom matrix.
                    LOAD - loads data into the phantom matrix bit by
                    bit, enlarging the matrix when necessary.
                    DUMP - converts matrix data to the characters that
                    the PRINTRONIX understands.
                    [More about the "phantom matrix" later in part II.]

            CHARGEN.DAT:   A  data  file,  about   five   blocks   long,
                    containing CHARacter GENerator DATa for SYMBOL.

            Other assorted VAX-11 FORTRAN, BASIC,  and  PASCAL  programs
                    and  subroutines:   illustrations  for  this manual,
                    demonstrations of  how  to  call  VPLOT  from  other
                    languages, useless pictures.

            VPLOT.DOC:  This manual.

VPLOT Guide                                                       Page 3


        II.  How does it work?


             A PRINTRONIX P300 can print 132 columns, each consisting of
        six dots, over 13.2 inches--792 dots across the width of 14-inch
        paper at a density of 60 dots per inch.  Dot density parallel to
        the  length of the paper is higher:  72 dots per inch.  Dots are
        printed in horizontal rows;  each such  row  is  produced  by  a
        string  of  characters sent to the printer in the usual way, but
        followed by the ASCII character of value 5 [ENQ].  This puts the
        printer into "Plot Mode";  each character is then interpreted as
        six dots corresponding  to  its  least  significant  bits;   the
        seventh  bit  must  be a one.  For example, the character "A" is
        01000001, or five "blanks" followed by a dot;  "C" is  01000011,
        four  blanks  followed  by  two  dots;   and "P" is 01010000:  a
        blank, a dot, then four more blanks.  Note  that  the  bits  are
        interpreted  in  order  from  most-  to least- significant.  The
        "legal" characters in Plot Mode, then, have decimal values  from
        64  (or  "@",  which  serves  as  a  blank) to 127 (the <DELETE>
        character,  which  draws  a  six-dot  horizontal  line   [DELETE
        presents  a  problem.   More  on  that later.]).  See PRINTRONIX
        Application Note No.  102370, a booklet entitled "Using the Plot
        Mode", for general information.

             How are the proper character strings produced?  A record of
        pen  movements  must  be  kept,  and, when the plot is complete,
        translated into a series of strings.  One method is to store the
        starting  and  ending  coordinates  of  each  line "drawn" by an
        imaginary "pen", putting them into an array or data file;   this
        saves  memory  (eight bytes can represent one line) but is slow:
        essentially, the entire record must be searched to  create  just
        one character string.  At the other extreme, a huge matrix could
        provide an electronic simulacrum of a sheet of paper.  with  one
        bit  representing  one  dot  (or  one character six dots).  This
        seems wasteful, even with the "unlimited" virtual memory of  the
        VAX.

             VPLOT uses neither method.  It divides the plot  area  into
        small  blocks, 24 dots wide and 40 long (120 bytes apiece), each
        representing a 2/5" by 5/9" area of paper.  The user's  call  to
        the  initialisation  routine  PLOTS  gives  VPLOT the length and
        width of the proposed plot and thereby  the  maximum  number  of
        blocks  needed.   The  MACRO  routine INITIAL calls the run-time
        procedure  LIB$GET VM  (GET  Virtual  Memory.   See  the  VAX-11                          _
        Run-Time  Library  Reference  Manual  for details) and obtains a
        longword (four bytes, the amount of memory a VAX needs to  store
        an address) of virtual memory for each block.  Later in the run,
        various subroutines call LOAD, asking it  to  load  a  bit  into
        what,  as  far  as  they  are  concerned,  is  a giant matrix of
        individually addressable bits.  LOAD determines what  block  the
        bit  would be in and checks its corresponding longword;  if this
        longword has the value zero, the block does not yet  exist,  and
        to  create  it, LOAD calls LIB$GET VM for another 120-byte block                                          _
        of memory, storing the lowest address of this new block  in  the
        longword.   Then LOAD writes a one into the appropriate bit.  In
        this way, sections of the matrix that are  not  used  are  never
        created.   Finally,  DUMP  translates  the blocks into character
        strings;  each three-byte row of  a  block,  then,  yields  four
        characters,  and each block contributes to forty dot-rows.  When

VPLOT Guide                                                       Page 4


        DUMP is finished with a block, it returns  it  to  the  bank  of
        virtual  memory  using LIB$FREE VM.  In this way, virtual memory                                       _
        is used for as short a time as possible.


        III.  Necessities, Conventions, &c.


             The device handler for your  PRINTRONIX  must  not  convert
        lower- to uppercase letters, as this erases the first dot of the
        six each character represents;  it must also  consider  <DELETE>
        (decimal  127)  a symbol and not a command to erase the previous
        character.  Millikin's handler doesn't do  the  latter,  but  is
        tricked  into  passing  <DELETE>  by a set eighth bit.  In other
        words, DUMP outputs the character as decimal 255, or a  byte  of
        all  ones  (11111111),  rather  than 127 (or 01111111).  If your
        handler works properly without this subterfuge,  you  can  speed
        the  program  by  removing several clearly marked lines in DUMP;
        if the trick fails, check your handler board  and  its  manuals.
        The  board  should  have  wire  jumpers  or  DIP  switches whose
        resetting will enable it to pass <DELETE>.

             The maximum width of a VPLOT plot is 13.2 inches;  however,
        plotting in the last tenth of an inch is not recommended, making
        the actual width 13.1 inches.  The maximum length depends on the
        sparseness of the plot, your VAX's memory and disk space, and so
        on.  A far-from-sparse plot 13 inches  wide  and  100  long  ran
        without  incident  on  Millikin's  VAX-11/780, which is equipped
        with 2 MB of memory and two RMO3 disks.   Plotting  outside  the
        space  you have declared will not result in run-time errors, or,
        for that matter, lines--it's merely a waste of time.

             In the following descriptions of the subroutines, parameter
        names  starting  with  the  letters I through N denote INTEGER*4
        variables;  all other parameters  are  REAL*4.   Use  conversion
        functions  such  as  JNINT  and  SNGL when necessary.  Also note
        that, by convention, the Y-axis of a plot  is  parallel  to  the
        width  of  the paper and the X-axis to its length;  zero degrees
        points along the X-axis into the paper box.

VPLOT Guide                                                       Page 5


        IV.  The "Basic Software" Routines


             PLOTS:

             Since PLOTS initializes the  entire  package,  it  must  be
        called before any other VPLOT routine, and after the output call
        to PLOT if plotting is to continue in a new field.  PLOTS clears
        certain variables and calls INITIAL to set up the phantom matrix
        and the MACRO routines.  The call is:

             CALL PLOTS (XLONG, YWIDE, LDEV)

                         XLONG is the length of the plot in inches.  The
                    complexity  of your plot and the memory size of your
                    VAX will place limits on it (see part III.).

                         YWIDE is the width of the plot in inches.   The
                    maximum  value  is  13.2;   anything  larger will be
                    truncated.

                         LDEV is the number  of  the  output  device  or
                    file,  generally  a file named FORnnn.DAT, where nnn
                    is a number between 2 and 999, with certain  numbers
                    reserved (5,6, etc.) for system files and 1 reserved
                    for the data file CHARGEN.DAT.  For example, an LDEV
                    of 3 would yield the file FOR003.DAT.



             PLOT:

             PLOT gives the  calling  program  direct  control  over  an
        imaginary  pen;   it lets the program "move" the pen, "raise" or
        "lower" it (a raised pen draws no lines), change the location of
        the  origin  (the point from which all pen motions are defined),
        and ask to stop plotting and output a data file.   The  call  to
        PLOT has three arguments:

             CALL PLOTS (XPAGE, YPAGE, IPEN)

                         XPAGE and YPAGE are the X-  and  Y-coordinates,
                    in  inches from the current origin, to which the pen
                    is to be moved.  Initially, the  origin  is  in  the
                    upper  left-hand  corner  of  the  paper, but may be
                    moved to any point in or outside of the plot area.

                         IPEN:  If IPEN is 2 or  -2,  the  pen  is  down
                    during  movement  and draws a line.  If IPEN is 3 or
                    -3, the pen is  up  during  movement.   If  IPEN  is
                    negative,  the  end-position given by (XPAGE, YPAGE)
                    becomes the new origin:  its coordinates are set  to
                    (0.0, 0.0) and it is the reference point for further
                    pen motions.  If IPEN equals 999, the output file is
                    loaded  with  the  results  of the plot so far.  The
                    "999" call must be  either  the  last  call  of  the
                    program or be followed by a new call to PLOTS.  Note
                    that this new call may ask for a  plotting  area  of
                    different size or for a new output file.

VPLOT Guide                                                       Page 6


             FACTOR:

             FACTOR changes the size of the  plot;   all  pen  movements
        after  a  call  to  it are multiplied by its argument.  Repeated
        calls are cumulative;  for instance, a call with "2.0"  followed
        by  one  with  "3.0" will result in a magnification of six.  The
        FACTOR call:

             CALL FACTOR (FACT)

                         If FACT is 2.0, all subsequent pen motions will
                    be  twice  as  large  as  before;   if  FACT is 3.0,
                    thrice, &c.  A FACT of 1.0 returns plotting  to  its
                    normal  size.   While  a  program is being debugged,
                    much time and paper can be saved  by  following  the
                    initial PLOTS call with a FACTOR call with FACT less
                    than 1.0, which can be removed later.



             WHERE:

             The WHERE entry sets the arguments in the call to the pen's
        current X, Y coordinates and the present scaling-factor:

             CALL WHERE (RXPAGE, RYPAGE, RFACT)

                         RXPAGE and RYPAGE are variables  that  will  be
                    set to the pen's present coordinates.

                         RFACT is set to the current scaling factor (1.0
                    if FACTOR has not been called).

                               NOTE:  a call to WHERE made after a  call
                          to  SYMBOL  might  not indicate where the next
                          character  should   be   plotted.    Use   the
                          "continuation feature" of SYMBOL (which see).

VPLOT Guide                                                       Page 7


             SYMBOL:

             This routine writes symbols  of  almost  any  size  at  any
        angle.  The call looks like this:

             CALL SYMBOL (XPAGE, YPAGE, HEIGHT, IBCD, ANGLE, NCHAR)

                         XPAGE and YPAGE are the coordinates, in inches,
                    of  the centre of the first character to be plotted.
                    To continue annotation from the  position  at  which
                    the  last  annotation ended, give XPAGE and/or YPAGE
                    as  999.0;   this  may  be  done   with   X   or   Y
                    independently.  (Calling WHERE and then using RXPAGE
                    and RYPAGE in another call to SYMBOL might not yield
                    the  same  results as using 999.0, especially if the
                    previous call to SYMBOL had a  negative  NCHAR  [see
                    below].)

                         HEIGHT  is  the  height,  in  inches,  of   the
                    characters  to  be  plotted.   For  best results, it
                    should be at least 0.1, and a multiple of 0.1  (0.1,
                    0.2,   0.3,   &c.),  but  any  number  over  0.1  is
                    acceptable.   Character  width  (including  spacing)
                    equals character height;  therefore, a ten-character
                    string of 0.2" letters should be about 2.0" wide.

                               NOTE:    Plotting   small   (under   .2")
                          characters  at  angles which are not multiples
                          of  90  degrees   is   not   suggested:    the
                          dot-matrix   of   the   PRINTRONIX  lacks  the
                          resolution  needed  for  legibility   at   odd
                          angles.  Even symbols as large as 0.3" or 0.4"
                          may have a rather shaky appearance.  Use  your
                          own discretion.

                         IBCD is the text to be plotted.  This should be
                    a character string, such as 'ECCLES', or a character
                    string variable;  in the latter  case,  a  substring
                    such  as  CSTRNG(2:7)  may  be  used rather than the
                    whole of CSTRNG (see  the  VAX-11  FORTRAN  Language
                    Reference   Manual   for   more  about  substrings).
                    Hollerith constants are not allowed.

                         There are a number  of  centred  plot  symbols,
                    numbered  from  0  to  17,  that may be used to mark
                    points of a  graph;   to  plot  one  of  these,  use
                    CHAR(n)  for  IBCD,  where  n is the symbol's number
                    (see the text on NCHAR, below).

                         ANGLE is the angle, in degrees from the X-axis,
                    at  which  the string is to be plotted.  If ANGLE is
                    0.0, the character(s) will be drawn  right  side  up
                    and parallel to the X-axis.

VPLOT Guide                                                       Page 8


                         NCHAR is, in CalComp software,  the  number  of
                    characters  of  IBCD  that  are  to be plotted;  for
                    instance,  an  NCHAR  of  5  would  plot  only  five
                    characters  of  a  ten character string.  VPLOT uses
                    VAX-11 FORTRAN's implicit passing of string lengths;
                    therefore,  for  drawing strings, NCHAR need only be
                    positive.  For one  of  the  special  numbered  plot
                    symbols  (or any symbol being used to mark a point),
                    NCHAR must be negative.  If NCHAR  is  -1,  the  pen
                    moves  to  the  given location and draws the symbol;
                    if NCHAR is -2, the pen is down during the move  and
                    draws a line to the point as well.

                               NOTE:  After a call  in  which  NCHAR  is
                          negative,  the  pen is at XPAGE, YPAGE;  after
                          one with a positive NCHAR, it's in the  centre
                          of a nonexistent "next character."

             NUMBER:

             NUMBER converts a floating point  ("REAL*4")  number  to  a
        form  that  is  plotted in what resembles FORTRAN F-format.  The
        calling sequence:

             CALL NUMBER (XPAGE, YPAGE, HEIGHT, FPN, ANGLE, NDEC)

                         XPAGE, YPAGE, HEIGHT, & ANGLE are the  same  as
                    in  SYMBOL;  the "999" continuation feature may also
                    be used.

                         FPN is the floating point number to be plotted;
                    it  must be REAL*4.  If it isn't, use functions such
                    as SNGL, FLOATI, and FLOATJ to convert it.

                         NDEC controls  the  precision  of  the  plotted
                    number.  If NDEC > 0, NDEC digits will be plotted to
                    the right of the decimal point--rounded, of  course.
                    For  example,  the  number  -0.12345678 E03, with an
                    NDEC of 2, would be plotted as -123.46.

                         If NDEC = 0, only the number's integer  portion
                    (rounded) and a decimal point are plotted;  the same
                    holds for NDEC = 1, except that there's  no  decimal
                    point.   If  NDEC  < -1, |NDEC|-1 (absolute value of
                    NDEC, minus  one)  digits  are  truncated  from  the
                    integer portion (still rounded).

                               NOTE:  |NDEC| should not exceed  9;   the
                          maximum  number  of  plotted  characters  in a
                          number will not  exceed  20.   REAL*4  numbers
                          which  cannot  be  plotted  in  the  requested
                          format will cause overflow:  the  plotting  of
                          ten asterisks.  The call is roughly equivalent
                          to an F20.<NDEC> format, with  leading  blanks
                          suppressed;   in  fact,  NUMBER  uses the same
                          Run-Time Library routine as does FORTRAN.

VPLOT Guide                                                       Page 9


             SCALE:

             Data to be plotted on a pair of axes can be  stored  as  as
        two  arrays,  one  of X-values and one of Y-values.  Rarely will
        these X and Y values correspond to the length of  an  axis,  and
        the user may find it troublesome (or impossible, if the range of
        his data isn't known beforehand) to provide conversion factors.

             Enter SCALE, which scans  data  in  arrays,  determining  a
        starting  value  for  the  axis  (a  minimum  or  maximum) and a
        units-per-inch scaling factor  (positive  or  negative).   These
        ensure  that  each  labeled mark on an axis is correctly placed,
        and that the data points, when plotted by the LINE routine, will
        fit  in  a given area.  SCALE stores these two values at the end
        of an array.

             DELTAV, the scaling factor, is in units/inch of  axis,  but
        is adjusted so that it is 1, 2, 4, 5, or 8 x10^n.  For instance,
        given an array with values ranging from 1250 to 3800 which is to
        be  plotted over a ten-inch axis, SCALE would first calculate an
        "unadjusted" factor of (3800-1250)/10 = 255 units per inch;   it
        would  then  assign the largest even value to DELTAV:  400 units
        per inch.

             FIRSTV, the starting value, is a multiple of DELTAV that is
        equal to or outside the limits of the data in the array.  In the
        example above, a minimum FIRSTV would be 1200;   a  maximum  one
        would be 4000.  (Note that with a FIRSTV of 1200, the far end of
        the axis would be 5200, and the last 3.5" of the axis  would  be
        wasted.   SCALE excels at such paper-wasting, and this behaviour
        probably is not peculiar to its VPLOT version.   Often  all  the
        data  points of a graph will be crammed into the first fourth of
        an axis.  You have been warned!)   The calling sequence:

             CALL SCALE (ARRAY, AXLEN, NPTS, INC)

                         ARRAY  is  the  array  of  data  points  to  be
                    examined.

                         AXLEN is the length of the axis  to  which  the
                    data is being scaled;  it must be greater than 1.0.

                         NPTS is the number of data points which are  to
                    be  examined.  This is not necessarily the number of
                    points in the array;  the array will generally  have
                    NPTS*|INC| points in it, plus several more locations
                    for scaling-factors (see below).

                         INC's  magnitude  is  used  by  SCALE  as   the
                    increment with which to select values from the array
                    for scanning.  Usually INC = 1;  if  it  is  2,  for
                    instance,  every  other  location  of  the  array is
                    examined.

                         If  INC  is  positive,  FIRSTV  approximates  a
                    minimum and DELTAV is positive;  if INC is negative,
                    FIRSTV is a maximum and DELTAV is also negative.

VPLOT Guide                                                      Page 10


                         If INC = 1 or -1, the array must  be  at  least
                    two elements larger than it would need to be for the
                    data alone.  In general, FIRSTV is stored  at  ARRAY
                    (NPTS*INC+1) and DELTAV at ARRAY (NPTS*INC+INC+1).

                         Generally, SCALE  is  called  to  examine  each
                    array whose data will be plotted;  if the user knows
                    the range of his data values he need not call  SCALE
                    for  an array, so long as he supplies an appropriate
                    FIRSTV and DELTAV for AXIS and LINE.



             AXIS:

             Most graphs require labelled axes;  this  routine  draws  a
        line  at  any angle, divides it into inch-long segments with tic
        marks, labels the marks, and writes a centred title.  When  both
        X-  and  Y-axes  are  needed, AXIS is called separately for each
        one.  The call has eight arguments:

             CALL AXIS (XPAGE, YPAGE, IBCD, NCHAR, AXLEN, ANGLE, FIRSTV,
        DELTAV)

                         XPAGE and YPAGE are the coordinates, in inches,
                    of  the axis line's starting point.  The entire line
                    and its terminal ends should be  at  least  one-half
                    inch  from  any edge of the paper to allow space for
                    labels and titles.  Usually the X-  and  Y-axes  are
                    joined  at the origin of the graph (0.0,0.0), though
                    other points may be used instead.  (See note at  end
                    of LINE for the correct use with that routine.)

                         IBCD is the title, which is centred and  placed
                    parallel  to  the  axis line.  The characters have a
                    fixed height of  about  0.2"  (five  characters  per
                    inch).  See SYMBOL for more about IBCD.

                         NCHAR, in Calcomp software, gives the number of
                    characters in the axis title, but its exact value is
                    not important to VPLOT.  If NCHAR is  positive,  all
                    axis  labels  (tic  marks, numbers, title) appear on
                    the positive (counterclockwise) side  of  the  axis,
                    which  is  usual  for the Y-axis;  if it's negative,
                    the labels will be on the negative side (X-axis).

                         AXLEN is  the  length  of  the  axis  line,  in
                    inches.

                         ANGLE is the angle at which the axis is  to  be
                    drawn,  normally  zero degrees for the X-axis and 90
                    degrees for the Y-axis.

                               NOTE:  Plotting axes at angles which  are
                          not  multiples  of  90  degrees  may result in
                          illegible tic-mark numbers.

VPLOT Guide                                                      Page 11


                         FIRSTV  is  the  starting  value  (minimum   or
                    maximum)  which  will  appear at (XPAGE, YPAGE).  It
                    may   be   computed   by   SCALE   and   stored   at
                    ARRAY(NPTS*INC+1),  or may be determined by the user
                    and stored anywhere.  This number  and  every  scale
                    value along the axis is drawn with two digits to the
                    right of the decimal point.  Since the digit size is
                    fixed  at about 0.1" (about ten characters per inch)
                    and one scale value appears every inch, no more than
                    six  digits  and a sign should appear to the left of
                    the decimal point.

                         DELTAV represents the number of data units  per
                    inch  of axis.  This value (increment or decrement),
                    which  is  added  to  FIRSTV  for  each   succeeding
                    one-inch  division  of  the axis, may be computed by
                    SCALE    and     stored     beyond     FIRSTV     at
                    ARRAY(NPTS*INC+INC+1), or determined by the user and
                    stored anywhere.  In order to use a standard format,
                    the size of DELTAV is adjusted to be between 100 and
                    0.01.  As a result, the decimal point may be shifted
                    left  or  right  in  the scale values as drawn;  the
                    axis title will then be followed by "10^n," where  n
                    is a power-of-ten adjustment factor.

             LINE:

             The LINE subroutine produces a line plot of pairs  of  data
        points  given  in  two arrays (X and Y).  LINE computes the page
        coordinates of each point according to its X- and  Y-values  and
        scaling  factors;  the data points may be represented by centred
        symbols, and/or lines which connect them.

             The scaling factors FIRSTV and DELTAV must be at the end of
        each  array;   if they have not been computed by SCALE they must
        be supplied by the user.

             CALL LINE (XARRAY,YARRAY,NPTS,INC,LINTYP,INTEQ)

                         XARRAY and YARRAY contain abscissa and ordinate
                    values, respectively, and the X and Y scaling values
                    (FIRSTV and DELTAV for each dimension).   These  two
                    arrays  must  be  one-dimensional  and have the same
                    number of elements.

                         NPTS is the number of data points to  be  taken
                    from   each  of  the  above  arrays;   this  is  not
                    necessarily the number of data points in each  array
                    (see  SCALE).   NPTS  should be the same as the NPTS
                    used for any previous call to SCALE.

                         INC is the increment that LINE is  to  use  for
                    gathering  data  from  the  two arrays, as described
                    earlier for SCALE.

                               NOTE:  For most applications, INC  is  1;
                          i.e.,  every  point  in  the  arrays is a data
                          point, and each array has (NPTS+2)  locations,
                          the last two containing FIRSTV and DELTAV.

VPLOT Guide                                                      Page 12


                         LINTYP determines what sort of a line  will  be
                    drawn  through  the  data  points.  The magnitude of
                    LINTYP  determines  the  frequency  of  the  plotted
                    symbols;   for  instance,  if  LINTYP=+4  or  -4,  a
                    special symbol  is  plotted  at  every  fourth  data
                    point.

                         If  LINTYP=0,  the  points  are  connected   by
                    straight lines but no symbols are plotted.

                         If LINTYP>0, a  straight  line  connects  every
                    data point gathered using INC (there will be NPTS of
                    them).  The pen is up while moving to the first data
                    point.

                         If LINTYP<0, no  connecting  lines  are  drawn;
                    only symbols are plotted.

                         INTEQ is the integer equivalent of the  special
                    plotting  symbol  which  is to be drawn (centred) at
                    each data point.   INTEQ  is  usually  zero  through
                    eighteen,  but  may be any other value corresponding
                    to a symbol (64 through 127);  however,  the  latter
                    symbols are not always centred about the data point.
                    One sample program included  with  VPLOT  plots  its
                    complete character set;  refer to its output.

                               NOTE:  When plotting lines on a  pair  of
                          axes,  be  certain  that the starting point of
                          both axes  (the  "XPAGE,YPAGE"  given  in  the
                          calls  to  AXIS)  is  set to (0.0,0.0);  if it
                          isn't, the axis labels will  not  reflect  the
                          actual  values  of  the  points.  For a single
                          X-axis, the starting point's X-coordinate must
                          be  0.0;   for a single Y, the Y- must be 0.0.
                          The starting-point may be reset  to  (0.0,0.0)
                          by  this  call:    CALL PLOT (X,Y,-3), where X
                          and Y are the coordinates of the point.

VPLOT Guide                                                      Page 13


        V.  The "Functional Software" Routines


             (The descriptions of these routines are rather sketchy.   I
        assume  that  you are already familiar with the "Basic Software"
        set.)

             CIRCL:

             CIRCL draws circular arcs  from  a  given  starting  point.
        These arcs may form circles and Archimedean spirals.

             CALL CIRCL (XPAGE,YPAGE,THO,THF,RO,RF,DI)

                         XPAGE and YPAGE are the coordinates, in inches,
                    of the starting point.

                         THO is the angle from the X-axis,  measured  in
                    degrees along a circle of radius RO, of the start of
                    the arc.

                         THF is the angle from the X-axis,  measured  in
                    degrees  along  a circle of radius RF, of the end of
                    the arc.

                         RO and RF are the starting  and  ending  radii,
                    respectively, of the arc.

                         DI:  If DI is 0.0, a solid arc is drawn;  if DI
                    is 0.5, a dashed arc is drawn.

             To draw a circle, set both RO and RF equal to the radius in
        inches,  and  make THO 360 degrees smaller (or larger) than THF.
        To draw an Archimedean spiral, set RO=0.0, RF=the final  radius,
        THO=0.0,  and THF=some large number of degrees.  THO and THF may
        be  positive  or  negative;   if  THO<THF,  the  arc  is   drawn
        counterclockwise,  else  clockwise.   If  THO=THF, or nearly so,
        errors may  occur.   Since  each  dot  of  an  arc  is  computed
        separately,  CIRCL  is  rather wasteful of CPU time;  also, some
        dots of a circle may seem superfluous.

             DASHL:

             DASHL is much like LINE except that it draws a dashed  line
        (the  dashes  are  about  0.1"  long)  instead  of a unbroken or
        nonexistent one and it does not plot centred symbols at  points.
        Consequently, its call is shorter:

             CALL DASHL (XARRAY,YARRAY,NPTS,INC)

                         XARRAY and YARRAY are the abscissa and ordinate
                    arrays for the points to be plotted.

                         NPTS is the number of data points to be plotted
                    (normally,  this  is  the same as the number of data
                    points in the array.  See SCALE and LINE).

VPLOT Guide                                                      Page 14


                         INC is the increment between the  point  values
                    in the arrays;  usually INC=1.

             DASHP:

             This routine draws a dashed line from the  "pen's"  current
        position  to a specified one.  If the line is not at least twice
        as long as the given dash length, dashes half the length of  the
        line result.  DASHP is rather like PLOT:

             CALL DASHP (XPAGE,YPAGE,DASH)

                         XPAGE,YPAGE are the coordinates of the point to
                    which the dashedline will be drawn.

                         DASH is the length of each dash and  the  space
                    between  dashes.   It should be greater than 1/60 of
                    an inch.

             ELIPS:

             ELIPS draws ellipses  or  elliptical  arcs.   It  resembles
        CIRCL,  but  is  even slower.  Large plots containing many large
        ellipses will consume vast amounts of CPU time;  several library
        functions  (SIN,  COS,  etc.),  must be called for each dot (the
        mathematical theory behind the method is correct, but  not  very
        practical).  Nevertheless:

             CALL ELIPS (XPAGE,YPAGE,RMAJ,RMIN,ANGLE,THO,THF,IPEN)

                         XPAGE and YPAGE  are  the  coordinates  of  the
                    starting point of the ellipse or arc.

                         RMAJ and RMIN are the lengths  (as  always,  in
                    inches)   of   the  semimajor  and  semiminor  axes,                                        ____            ____
                    respectively.

                         ANGLE is  the  angle  of  the  major  axis,  in
                    degrees.

                         THO and THF are the angles, in degrees from the
                    major  axis,  of  the  arc's  initial  and  terminal
                    points.

                               NOTE:  THO and THF are NOT measured  with                                                      ___
                          respect to the centre of the ellipse, but from
                          the  focus  on  the  "positive"  side  of  the
                          ellipse.   Imagine  plotting an entire ellipse
                          with ANGLE=0.0;  the focus about which  angles
                          are measured would be the one nearer the paper
                          box.  This is not the  same  as  the  original
                          CalComp routine, unfortunately.

                         IPEN is the same as in PLOT.

VPLOT Guide                                                      Page 15


             GRID:

             GRID draws linear grids--customized "graph paper" which  is
        guaranteed  to cause eyestrain.  It may be used with SCALE, AXIS
        and LINE to make graphs.

             CALL GRID (XPAGE,YPAGE,DELTAX,DELTAY,NXSP,NYSP)

                         XPAGE and YPAGE are the coordinates, in inches,
                    of the grid's lower left corner.

                         DELTAX is the distance between  grid  lines  in
                    the X direction.

                         DELTAY is the distance between  gris  lines  in
                    the Y direction.

                         NXSP and NYSP are the numbers of spaces between
                    lines in the X and Y directions, respectively.

                               NOTE:  NXSP+1 lines are drawn  in  the  X
                          direction, NYSP+1 in the Y.

             POLY:

             This routine draws equilateral polygons and stars.

             CALL POLY (XPAGE,YPAGE,SLEN,SN,ANGLE)

                         XPAGE and YPAGE  are  the  coordinates  of  the
                    starting point.

                         SLEN is the length of each side of the polygon.

                         SN is the number of sides in the  polygon;   if
                    SN  is  negative,  a  star  of  SN  points  is drawn
                    instead.

                         ANGLE is the angle, in degrees,  of  the  first
                    side of the polygon.

             RECT:

             RECT draws rectangles of any reasonable length and width at
        any angle.  The call is:

             CALL RECT (XPAGE,YPAGE,HEIGHT,WIDTH,ANGLE,IPEN)

                         XPAGE  and  YPAGE  give  the  position  of  the
                    rectangle's lower left corner (before rotation).

                         HEIGHT and WIDTH are self-explanatory.

                         ANGLE  is  the  angle,  in  degrees,   of   the
                    rectangle's  base  (the  rectangle is rotated around
                    XPAGE, YPAGE).

VPLOT Guide                                                      Page 16


                         IPEN is the same as for PLOT.

             POLAR:

             POLAR is much like LINE, except  that  it  works  in  polar
        coordinates,  plotting  a radial variable against an angular one
        (given in radians), and can do its own scaling.  The call is:

             CALL POLAR (RADAR,ANGAR,NPTS,INC,LINTYP,INTEQ,RMAX,DR)

                         RADAR and ANGAR are the arrays  containing  the
                    radial and angular values, respectively.

                         NPTS is the number of data points to be plotted
                    (recall the information given in SCALE and LINE).

                         INC is the increment between data values in the
                    arrays, as in LINE.

                         LINTYP is also the same as in LINE.

                         INTEQ:  See LINE.

                         RMAX is the maximum  radius  for  the  plotting
                    area that the polar plot will occupy.  If RMAX<=0.0,
                    DR is used as a scale factor.

                               NOTE:  In the original CalComp version of
                          POLAR,  RMAX  was  in  page inches:  inches of                                                 ____ ______
                          paper, which are not influenced  by  calls  to
                          FACTOR.   In VPLOT, RMAX is in inches, and its
                          value will  be  multiplied  by  FACTOR  before
                          being  used.   The  same  holds for DR:  it is
                          units of data per inch rather  than  per  page
                          inch.

                         DR is the scale factor;  POLAR computes  it  if
                    RMAX>0.0;  otherwise the user must supply it.

VPLOT Guide                                                      Page 17


        VI.  How to compile, link and  run  VPLOT  with  VAX-11  FORTRAN
        programs:

                $ FORTRAN MAIN1
                $ FORTRAN VPLOT
                $ MACRO MACPLOT
                $ LINK MAIN1+VPLOT+MACPLOT
                $ RUN MAIN1


             VPLOT and MACPLOT may be compiled beforehand and placed  in
        a  system  directory  as object files;  a short command language
        program could be used to link them with the main program and run
        the result.  The file CHARGEN.DAT is the character-generator for
        SYMBOL;  if it is also placed in a directory such  as  [SYSEXE],
        the  OPEN  statement  in  the SYMBOL subroutine of VPLOT must be
        modified.  At present it looks like this:

                OPEN (UNIT=1,NAME='CHARGEN.DAT',TYPE='OLD',READONLY)

             Replace 'CHARGEN.DAT' with  'DRA0:[SYSEXE]CHARGEN.DAT'  (or
        whatever directory and device names are appropriate).

        VII.    Printing the output file:
        On the Millikin system, the command is:
                PRINT/NOFEED/DEV=LPB0: FORnnn.DAT
        where nnn is the number of the output file as  given  to  PLOTS.
        An  ASSIGN  statement may be used to associate some such FORTRAN
        data file with the PRINTRONIX (which, as you can tell  from  the
        above,  is LPB0:  on Millikin's VAX);  in this way, no permanent
        data file is created and the information is sent directly to the
        printer.  It's all a matter of taste and convenience.

             Printing VPLOT output files on  the  screen  using  a  TYPE
        command  allows one to see the approximate length and width of a
        plot.  These files  contain  some  of  the  most  moronic  prose
        imaginable:
        @@@@@@@@@@@@@@@@@@@@@qiOc@jxfF@shI@aAy@@qMpGg@a@O@p
        @@@@@@@@@@@@@@@@@@@f@a@AuP@bjIe@sqFFf@mN@@@Ggiarx@zl@k
        @@@@@@@@@@@@@@@@gT@@@@@@fgPz@@@@@@GiMq@@@@eCc@@@@@@@@@h@@fgT
        @@@@@@@@@@@@@@@yi@@@@whUSSjkOap@@F@x
        @
        @
        @

             Those single "@" characters usually represent blank  lines;
        if  these  occur  at the beginning or end of a plot, they may be
        edited out using EDT or SOS to make the plot shorter.  Text  may
        be  edited  in with plot files, but may not occupy the same line
        as plot data.  Be certain to  leave  at  least  one  blank  line
        between  data  and  text, or the adjacent lines of text may have
        broken letters.

VPLOT Guide                                                      Page 18


        VIII.  Some final words:

        O, tish ill done, tish ill done!  By my hand, tish ill done!

                        --(Henry the Fifth, Act III, Sc. II, line 91)


             The VPLOT package has become an albatross around  my  neck.
        I  have  been  working  on  it sporadically for something over a
        year, with most programming being done in early August 1980  and
        January  1981.   At  other  times  I  have  tried to improve the
        plotter's performance, test for bugs (some were turning up  only
        days  ago  and I'm certain that there are a few left), and write
        documentation.   This  manual  is  based  on  the  same  CalComp
        literature that I used in designing my routines;  in places this
        Guide  reads  depressingly  (and  plagiaristically!)  like   the
        CalComp material.  Peccavi.

             Although I thought up the matrix-storage method  for  VPLOT
        independently,  it seems that I was anticipated;  Hoare mentions
        it in Structured Programming, and gives credit for the invention              __________ ___________
        to  Dijkstra.  While I'm on the subject of acknowledgements, I'd
        like to thank the Mathematics faculty at Millikin for much  help
        and  encouragement,  especially  Dr.   Thomas Wallgren, who gave
        valuable suggestions for CIRCL, ELIPS, and POLY;  the  staff  of
        the  Computer  Center,  especially  center  director  Dr.   John
        Arrison and programmer/analyst Mr.   Alan  Smith;   the  student
        operators,  notably  Mr.   Jon  Westcot, who found a way to call
        VPLOT from BASIC and who has contributed a short manual and some
        BASIC programs to this package;  and of course my parents.

             If (when?) you  find  errors  in  VPLOT,  need  help,  have
        suggestions  or  needs  for  improvements, modified versions for
        other printers or the PDP-11, etc., write:
                M. Gooley
                c/o Millikin University Computer Center
                1184 West Main Street
                Decatur, Illinois 62522
        The Center's 'phone numbers, at present, are (217)-424-6333  and
        -6334, but I can't conceive an emergency grave enough to warrant
        a call;  besides, I probably would be in  class  when  the  call
        arrived.