HEXADECIMAL/ASCII DUMP SUBROUTINE

AUTHOR: J.A.Johnson
        Jet Propulsion Laboratory
        Pasadena, California
        15-JAN-1982

PURPOSE: This subroutine provides a HEXADECIMAL and ASCII dump of selected
         parameters.

CALLING PARAMETERS: HEXDMP is invoked in the following manner:

                    CALL HEXDMP(INPBUF,NBYTES,UNIT,TITLE)

         where:
               INPBUF is the starting location of the memory area to be 
               formatted and printed.
               NBYTES is a variable containing the number of bytes to be
               printed.
               UNIT is a variable containing the unit number of an open
               output file.
               TITLE is a character string which will be printed on the
               header line for the particular output block.

OUTPUT FORMAT: HEXDMP takes each successive 32 bytes from INPBUF and formats
         it in the following manner:

         1) a 64 character hexadecimal representation as eight double words.
         2) a 32 character ASCII translation bracketed by asterisks (*).
            Untranslatable bytes are represented as periods (.).
         3) complete lines which duplicate previous lines will be not be
            replaced by the message: LINES xxxx THRU yyyy SAME AS ABOVE

EXAMPLE: The following is an example of use in a FORTRAN program:

                   INTEGER ALPHA, BRAVO(2), CHARLIE
                     .
                     .
                     .
                   CALL HEXDMP(ALPHA,16,6,'ALPHA et.al.AFTER START')
                   etc.

         HEXDMP will format and print the 3 INTEGER values above (16 bytes)
         and output same to unit 6:

 BLOCK NUMBER=     1, RECORD SIZE=    16 (10), TITLE=ALPHA et.al.AFTER START

 0000  01000000 0F002200 69500044 204F4F50  /etc/ *......". P..POOP*

         The first four characters give the relative byte address in the 
         block, followed by the 16 bytes in question.  The right hand side
         shows the ASCII representation with dots replacing the unprintable
         characters.  In actual practice, each line is approximately 120
         characters in length but has been foreshortened here to get it 
         on an 80 character line.

                                          mahalo,
                                           jo4hn