;+++
;
; FACILITY
;	OAK RIDGE NATIONAL LABORATORY
;	FUSION ENERGY DIVISION
;	TOKAMAK SECTION
;
; ABSTRACT
;
;	This library contains a collection of procedures
;	designed to support access to the VAX CAMAC system
;	developed for the ORNL Fusion Energy Division VAX-11/780
;	computer system(s). These procedures are designed to 
;	conform to VAX linkage conventions and as such should
;	be callable from any VAX supported high-level language.
;	Specifically, this library contains the following procedures:
;
;	CAM$CSTATE
;	-Alter default CAMAC system states for the
;	 on an image by image basis,
;	CAM$ASSIGN
;	-Assign a key value to a specific CAMAC module,
;	CAM$DASSGN
;	-Release a CAMAC module key assignment,
;	CAM$PIO(W)
;	-Perform a single-action CAMAC request(programmed I/O),
;	CAM$QSCAN(W)
;	-Perform a CAMAC Q-Scan mode transaction,
;	CAM$QSTOP(W)
;	-Perform a CAMAC Q-Stop mode transaction,
;	CAM$STOP(W)
;	-Perform a CAMAC Stop mode transaction.
;
;
;	A brief synopsis of each access procedure is included
;	in the preamble for that procedure.
;
; AUTHOR
;	E. T. Blair
;
; REVISION HISTORY
;	V02-000, E.T. Blair,12-AUG-1982
;	Modified CAMAC access procedures performing QIO(W) system services
;	to provide analogous entry points,i.e. CAM$XXX and CAM$XXXW calls
;	with consistent argument lists for both calls. In V01 the determination
;	as to whether a call was wait/proceed mode was based on the argument
;	list parameters specified, however, this approach posed some problems
;	when attempting to perform CAMAC calls from PASCAL.
;
;	V02-001,E.T. Blair,12-AUG-1982
;	Made changes to documentation in several procedure preambles
;	to correct errors and clarify intent. Also, changed argument
;	format for CAM$CSTATE(arguments XSTATE and QSTATE) from
;	bytes to words to accomodate use of existing mask definitions
;	in the CAMAC macro library.
;
;
;	V02-002,E.T. Blair,25-AUG-1982
;	Made change to CAM$CSTATE to force update of the process information
;	maintained in the CIB for each call to CAM$CSTATE. This provides a
;	simple means of updating this information if the process happens to
;	change some privilege, etc. without creating a separate access call
;	to perform the update.
;
;	V02-003, E.T. Blair,8-SEP-1982
;	Incorporated changes to optimize the access procedures. An internal
;	routine was added to generate the CAMAC RTB. Also, modifications to
;	support the parallel highway were added.
;---


;+++
;
;	Procedure:
;	CAM$CSTATE(EFN[,XSTATE][,QSTATE][,MEM])
;
;	Description:
;	This procedure provides a means to define the default
;	values for the parameters specified in the procedure
;	argument list. A description of each parameter, it's
;	function and permissible values is given below:
;
;	Parameter: EFN
;
;	Function:
;	Allows the user to define the default process local event flag to be
;	utilized by the CAMAC access procedures for synchronizing I/O 
;	completion on all non-proceed I/O calls(i.e. any call to a CAMAC access
;	procedure that does not include the optional 'proceed I/O' parameters).
;	This value initially defaults to local event flag 0.
;
;	Value:
;	Any legal process local event flag number.
;
;	Parameter: XSTATE
;
;	Function:
;	Allows the user to influence the logic equation used by the
;	CAMAC branch driver in the determination of 'ERROR'/'NORMAL'
;	termination of a programmed I/O(PIO) or a list PIO operation.
;	This value initially defaults to 'CAM$_XI'.
;
;	Values:
;	CAM$XI-Ignores CAMAC X response in the determination of
;		ERROR status from the CAMAC branch driver.
;	CAM$_XE-Opposite of CAM$_XI.
;
;	Parameter: QSTATE
;
;	Function:
;	Allows the user to influence the logic equation used by the
;	CAMAC branch driver in the determination of 'ERROR'/
;	'NORMAL' termination of a programmed I/O(PIO) or a list
;	PIO operation. This value initially defaults to 'CAM$_QDC'.
;
;	Values:
;	CAM$_QDC-Ignores CAMAC Q response in the determination of
;		ERROR status from the CAMAC interface.
;	CAM$_QNE-CAMAC Q response not expected. If received, the CAMAC
;		interface terminates with ERROR status on PIO and list PIO
;		operations.
;	CAM$_QE-CAMAC Q response expected. If not received, the CAMAC
;		interface terminates with ERROR status on PIO and list PIO
;		operations.
;
;	Parameter: MEM
;
;	Function:
;	Allows the user to change the default memory format state for
;	a given image. The memory format used determines whether 16 or
;	24 bit CAMAC data transfer operations are performed. This value 
;	initially defaults to '16' bit mode.
;
;	Values:
;	16-Sets default memory format to '16' bit format(1 CAMAC transfer =
;		1 word).
;	24-Sets default memory format to '24' bit format(1 CAMAC transfer =
;		2 words).
;
;	Parameters:
;	EFN- value of the process local event flag to be used by CAMAC
;		access procedures as default,
;	XSTATE- address of a word containing one of the symbolic values
;		CAM$_XI,CAM$_XE,
;	QSTATE- address of a word containing one of the symbolic values
;		CAM$_QDC, CAM$_QE, CAM$_QNE,
;	MEM- address of a byte containing one of the values 16 or 24.
;
;	Return Status:
;	SS$_NORMAL
;		Successful completion of item request.
;	SS$_INSFARG
;		Not enough arguments supplied.
;	SS$_BADPARAM
;		Invalid parameter specified.
;
;---


;+++
;
;	Procedure:
;	CAM$ASSIGN(%DESCR(MODULE_NAME),KEY)
;
;	Description:
;	This procedure performs a CAMAC key(I/O channel)
;	assignment to the specified CAMAC logical module.
;	The logical module name is translated recursively
;	and must eventually translate to a physical module
;	name from the SYSTEM logical name table unless the
;	calling process has SYSNAM privilege. Upon verification
;	of physical module name syntax and UIC access to the
;	module, a VAX I/O channel is assigned to the CAMAC 
;	unit specified in the physical module name and the
;	key is encoded for return to the caller.
;
;	Parameters:
;	MODULE_NAME- address of a CHARACTER variable containing an ASCII 
;		character string identifying the CAMAC module to be referenced,
;	KEY- address of a longword to receive the encoded key value
;		to be used for subsequent CAMAC I/O calls,
;
;	Return Status:
;	SS$_NORMAL
;		Service normally completed. Key value is valid.
;	SS$_BADPARAM
;		Invalid/illegal parameter was passed on the call.
;	(See SYS$ASSIGN system service for additional status return).
;
;---


;+++
;
;	Procedure:
;	CAM$DASSGN(KEY)
;
;	Description:
;	This procedure releases a CAMAC key assignment previously
;	assigned via the CAM$ASSIGN function call. The VAX I/O
;	channel associated with the specified key value is
;	deassigned when the reference count associated with the
;	CAMAC Support Unit becomes 0.
;
;	Parameters:
;	KEY- address of a longword integer containing the encoded
;		key value.
;
;	Return Status:
;	SS$_NORMAL
;		Request successfully completed.
;	SS$_BADPARAM
;		Illegal/invalid parameter passed on call.
;	See SYS$DEASSGN system service for additional status).
;
;---


;+++
;
;	Procedure:
;
;	CAM$PIO(W)(%DESCR(MODULE_NAME),A,F[,DATA][,MEM]][,IOSB]
;			[,EFN][,AST][,ASTPRM])
;		Or
;
;	CAM$PIO(W)(%DESCR(KEY),A,F,[,DATA][,MEM][,IOSB]
;			[,EFN][,AST][,ASTPRM])
;
;	Description:
;	This procedure performs a single-action CAMAC I/O request.
;	The specified CAMAC module name is translated into the
;	appropriate controller, crate and station addresses.
;	If the keyed access format is used, the key must correspond
;	to a CAMAC module previously connected via the CAM$ASSIGN
;	function call. The CAMAC data buffer is not required for
;	calls performing CAMAC control functions(8 <= F <= 15 or
;	24 <= F <= 31. If the I/O status block parameter is specified,
;	it is used to receive the status from the CAMAC I/O request.
;	If the memory format control parameter is specified,
;	the value determines whether 16 bits of data is transferred
;	(MEM=16) or 24 bits of data is transferred(MEM=24). If
;	not specified, the CIB memory format specifier is used.
;
;	If the proceed mode call(CAM$PIO) is used, control returns
;	 to the caller as soon as the CAMAC request is queued to 
;	the system. If the wait mode call(CAM$PIOW) is used, control 
;	is returned to the calling program only when the CAMAC I/O 
;	is complete. 
;
;	The I/O synchronization parameters(EFN, AST and ASTP) are used
;	in the same manner as their counterparts in the QIO and QIOW
;	system services. See the VAX System Services Reference Manual
;	for further discussion if needed.
;
;
;	Parameters:
;	MODULE_NAME- address of a CHARACTER variable containing an ASCII 
;		character string identifying the CAMAC module to be referenced,
;	KEY- address of a longword descriptor for the key value
;		previously computed for the CAMAC module via
;		calling the procedure CAM$ASSIGN,
;	A- address of a byte containing CAMAC subaddress,
;	F- address of a byte containing CAMAC function code,
;	DATA- address of a long word containing CAMAC write
;		data or that will receive CAMAC read data. Not 
;		required for CAMAC control functions,
;	MEM- address of a byte containing the memory format for
;		the CAMAC transaction(MEM=16; MEM=24). If not
;		specified, the current CIB memory format specifier
;		is used.
;	IOSB- address of a quadword buffer to receive I/O completion
;		status from the CAMAC request.
;
;	Optional I/O Synchronization Parameters:
;	EFN- value specifying the number of a local event flag
;		to be set upon I/O completion. If not specified, the
;		default process event flag from the CAMAC image block
;		is used,
;	AST- address of an AST procedure to receive an I/O completion
;		AST,
;	ASTPRM- address of a longword containing a parameter to
;		be passed to the specified AST procedure.
;
;	Return Status:
;
;---


;+++
;
;	Procedure:
;	CAM$QSCAN(W)(%DESCR(MODULE_NAME),A,F,COUNT,DATA[,MEM][,IOSB]
;		[,EFN],[,AST][,ASTPRM])
;		Or
;	CAM$QSCAN(W)(%DESCR(KEY),A,F,COUNT,DATA[,MEM][,IOSB]
;		[,EFN],[,AST][,ASTPRM])
;
;	Description:
;	This procedure performs a CAMAC subaddress/address
;	scan utilizing the Q-scan technique to control the
;	incrementing of the CAMAC subaddress and address
;	utilized on successive repetitions of the specified
;	CAMAC function code. The scan starts initially at the
;	specified subaddress(A). The initial station number
;	is determined from the specified module name(for direct
;	module reference calls) or from the key value(for keyed
;	access calls). To utilize the keyed access mode, the
;	key value must first be generated by a call to the
;	CAM$ASSIGN function. In all cases, the transaction
;	terminates when the transfer count(COUNT) is exhausted
;	or when an anomolous condition is detected. If the I/O
;	status block parameter is specified, the status of the
;	CAMAC I/O request is returned in specified quadword buffer.
;	If not, a quadword buffer in the CAMAC image block is used.
;
;	If the proceed mode call(CAM$QSCAN) is used, control returns
;	 to the caller as soon as the CAMAC request is queued to 
;	the system. If the wait mode call(CAM$QSCANW) is used, control 
;	is returned to the calling program only when the CAMAC I/O 
;	is complete. 
;
;	The I/O synchronization parameters(EFN, AST and ASTP) are used
;	in the same manner as their counterparts in the QIO and QIOW
;	system services. See the VAX System Services Reference Manual
;	for further discussion if needed.
;
;	Parameters:
;	MODULE_NAME- address of a CHARACTER variable containing an ASCII 
;		character string identifying the CAMAC module to be referenced,
;	KEY- address of a longword descriptor for the key value
;		previously computed for the CAMAC module via
;		calling the procedure CAM$ASSIGN,
;	A- address of a byte containing CAMAC subaddress,
;	F- address of a byte containing CAMAC function code,
;	DATA- address of data buffer that contains CAMAC write data
;		or that will receive CAMAC read data.
;	COUNT- address of a word containing the CAMAC transfer
;		count(in units of the memory format).
;	MEM- address of a byte containing memory format for the
;		CAMAC transaction(MEM=16; MEM=24). If not specified,
;		the current CIB memory format specifier is used,
;	IOSB- address of a quadword buffer to receive I/O completion
;		status from the CAMAC request.
;
;	Optional I/O Synchronization Parameters:
;	EFN- value specifying the number of a local event flag
;		to be set upon I/O completion. If not specified, the
;		default process event flag from the CAMAC image block
;		is used,
;	AST- address of an AST procedure to receive an I/O completion
;		AST,
;	ASTPRM- address of a longword containing a parameter to
;		be passed to the specified AST procedure.
;
;
;	Return Status:
;
;---


;+++
;
;	Procedure:
;	CAM$QSTOP(W)(%DESCR(MODULE_NAME),A,F,COUNT,DATA[,MEM][,IOSB]
;		[,EFN][,AST][,ASTPRM])
;		Or
;	CAM$QSTOP(W)(%DESCR(KEY),A,F,COUNT,DATA[,MEM][,IOSB]
;		[,EFN][,AST][,ASTPRM])
;
;	Description:
;	This procedure performs a CAMAC block transfer utilizing
;	the Q-stop technique for controlling successive references
;	to a given CAMAC module using a fixed subaddress and
;	function code. A Q-stop transaction terminates when
;	the referenced module returns a Q=0 response or the
;	specified transfer count(COUNT) is exhausted or an
;	anomolous condition is detected. If the I/O status block parameter
;	is specified, the status of the CAMAC I/O operation is
;	returned in that quadword buffer. If not, a quadword 
;	in the CAMAC image block is used to receive the status.
;
;	If the proceed mode call(CAM$QSTOP) is used, control returns
;	 to the caller as soon as the CAMAC request is queued to 
;	the system. If the wait mode call(CAM$QSTOPW) is used, control 
;	is returned to the calling program only when the CAMAC I/O 
;	is complete. 
;
;	The I/O synchronization parameters(EFN, AST and ASTP) are used
;	in the same manner as their counterparts in the QIO and QIOW
;	system services. See the VAX System Services Reference Manual
;	for further discussion if needed.
;
;	Parameters:
;	MODULE_NAME- address of a CHARACTER variable containing an ASCII 
;	character string identifying the CAMAC module to be referenced,
;	KEY- address of a longword descriptor for the key value
;		previously computed for the CAMAC module via
;		calling the procedure CAM$ASSIGN,
;	A- address of a byte containing CAMAC subaddress,
;	F- address of a byte containing CAMAC function code,
;	DATA- address of data buffer that contains CAMAC write data
;		or that will receive CAMAC read data.
;	COUNT- address of a word containing the CAMAC transfer
;		count(in units of the memory format).
;	MEM- address of a byte containing memory format for the
;		CAMAC transaction(MEM=16; MEM=24). If not specified,
;		the current CIB memory format specifier is used.
;	IOSB- address of a quadword buffer to receive I/O completion
;		status from the CAMAC request.
;
;	Optional I/O Synchronization Parameters:
;	EFN- value specifying the number of a local event flag
;		to be set upon I/O completion. If not specified, the
;		default process event flag from the CAMAC image block
;		is used,
;	AST- address of an AST procedure to receive an I/O completion
;		AST,
;	ASTPRM- address of a longword containing a parameter to
;		be passed to the specified AST procedure.
;
;
;	Return Status:
;
;---


;+++
;
;	Procedure:
;	CAM$STOP(W)(%DESCR(MODULE_NAME),A,F,COUNT,DATA[,MEM][,IOSB]
;		[,EFN][,AST][,ASTPRM])
;
;		Or
;	CAM$STOP(W)(%DESCR(KEY),A,F,COUNT,DATA,[,MEM][,IOSB]
;		[,EFN][,AST][,ASTPRM])
;
;	Description:
;	This procedure performs a CAMAC block transfer utilizing
;	only the specified transfer count(COUNT) to control the
;	number of times the specified CAMAC module is referenced
;	using a fixed subaddress(A) and function code(F). The
;	transaction terminates when either the transfer count is
;	exhausted or an anomolous condition is detected.
;	If the I/O status block parameter is specified, the
;	status of the CAMAC I/O operation is returned to that
;	quadword buffer. If not, the status is returned to a
;	quadword buffer in the CAMAC image block.
;
;	If the proceed mode call(CAM$STOP) is used, control returns
;	 to the caller as soon as the CAMAC request is queued to 
;	the system. If the wait mode call(CAM$STOPW) is used, control 
;	is returned to the calling program only when the CAMAC I/O 
;	is complete. 
;
;	The I/O synchronization parameters(EFN, AST and ASTP) are used
;	in the same manner as their counterparts in the QIO and QIOW
;	system services. See the VAX System Services Reference Manual
;	for further discussion if needed.
;
;
;	Parameters:
;	MODULE_NAME- address of a CHARACTER variable containing an ASCII 
;		character string identifying the CAMAC module to be referenced,
;	KEY- address of a longword descriptor for the key value
;		previously computed for the CAMAC module via
;		calling the procedure CAM$ASSIGN,
;	A- address of a byte containing CAMAC subaddress,
;	F- address of a byte containing CAMAC function code,
;	DATA- address of data buffer that contains CAMAC write data
;		or that will receive CAMAC read data.
;	COUNT- address of a word containing the CAMAC transfer
;		count(in units of the memory format).
;	MEM- address of a byte containing memory format for the
;		CAMAC transaction(MEM=16; MEM=24). If not specified,
;		the current CIB memory format specifier is used,
;	IOSB- address of a quadword buffer to receive I/O completion
;		status from the CAMAC request.
;
;	Optional I/O Synchronization Parameters:
;	EFN- value specifying the number of a local event flag
;		to be set upon I/O completion. If not specified, the
;		default process event flag from the CAMAC image block
;		is used,
;	AST- address of an AST procedure to receive an I/O completion
;		AST,
;	ASTPRM- address of a longword containing a parameter to
;		be passed to the specified AST procedure.
;
;
;	Return Status:
;
;---


;---