Supplement to the "Kermit User's Guide"



3.x. CYBER 170/750 KERMIT

Kermit is written for the Cyber 170/750 in FTN5, CDC's FORTRAN 77
compiler.   It  mimics  the DEC-20 style command parser in that a
question mark followed by a carriage return will display the pos-
sible  inputs  for  a given field. This version of Kermit must be
watched since it has no timeout capabilities.

Kermit only uses local files.  To send a file, it must  first  be
copied  to  a local file.  Kermit may then be run to send it from
the Cyber to another Kermit.  To  receive  a  file,  Kermit  will
write  it  to  a  local file.  This file must be copied to a per-
manent file before logging out if it is to be saved.

A Cyber filename is restricted to 7 alphanumeric characters  with
the  first character being an alpha.  Kermit will use the first 7
valid characters of any file being sent to the Cyber.  If a  file
under  that  name already exists, an Error packet stating so will
be sent back and Cyber Kermit will abort the transfer.

Kermit can only deal with "8 in 12" ASCII files.  At the  Univer-
sity  of Texas, an "8 in 12" ASCII file is defined to be an 8 bit
ASCII character stored in a 12 bit byte.  There are 60 bits in  a
word so that is 5 bytes per word.  A null character is represent-
ed as an octal 4000 and the CR/LF pair is mapped into the  single
character  NEL  (octal 205).  This is the same character set that
Cyber C uses.  Unfortunately, CDC hasn't officially defined  it's
"8  in  12"  character  set yet, but it is likely that the end of
line convention will be the similar to the current one  which  is
one or more 0000 bytes in the low order portion of a word.

You can run Kermit interactively by typing repeated  commands  in
response  to its "Kermit-170>" prompt, or you can run it as a re-
mote server.  Here are the Kermit-170 commands:

EXIT    Exit from Kermit-170.  You may also  stop  Kermit-170  in
        the  midst  of  a transfer or during server operations by
        aborting the program (CTRL-C or CTRL-G ABORT);  the  pro-
        gram  traps them and puts yor terminal back to normal be-
        fore halting.

HELP [<topic>]
        Give Help.  There's a general help  text,  plus  seperate
        help texts for each Kermit-170 command.

QUIT    Synonym for EXIT.

RECEIVE Receive a file or group of files from the other host.  If
        the  name  in the header packet is not a legal Cyber file
        name, the first 7 legal characters will be used.

        If the file already exits as a local  file,  Kermit  will
        abort  the transfer.  If an error occurs during transfer,
        the file being received will be removed  from  the  local
        file  list  to  allow  the  transfer  to be retried.  You
        should escape back to your local  Kermit  after  entering
        RECEIVE mode and give the SEND command.

SEND filename
        Send a file to the other host.  The name of the  file  is
        passed to the other host in a file header packet, so that
        the file can be stored there with  the  same  name.   You
        should  escape back to your local Kermit and give the RE-
        CEIVE command.  If you don't  do  this  fast  enough  the
        "send-init"  packet  may  arrive prematurely.  To prevent
        this, use SET DELAY or hit the RETURN key on your  micro-
        computer if it does not timeout.

SERVER  Act as a server for  another  Kermit.   Whatever  options
        were previously SET will be used.  The server may be shut
        down from the local Kermit by using  the  BYE  or  FINISH
        commands,  or by connecting back to the Cyber, and typing
        Control-C or Control-G ABORT.

SET     Establish system-dependent parameters.  You  can  examine
        their  values  with the SHOW command.  Numeric values may
        be decimal, octal (postfixed with a  B),  or  hexadecimal
        (postfixed by an H).  The following may be SET:

        DEBUG <option>
                Show packet traffic explicitly.  Options are:

                ALL     Set all debug options.

                LOG-FILE filename
                        Log states and packets to  the  specified
                        file.  The default log-file is file KERM-
                        LOG.

                OFF     Don't display debugging information (this
                        is the default).  If debugging was in ef-
                        fect, turn it off and close any log file.

                PACKETS Display each incoming and outgoing packet
                        (lengthy).

                STATES  Show kermit state transitions and  packet
                        numbers (brief).

        DELAY <decimal-number>
                How many seconds to wait before sending the first
                packet.  This gives you time to "escape" back and
                issue a RECEIVE command.

        DUPLEX <keyword>
                Changes the method of echoing characters when be-
                ing  prompted for commands.  The choices are FULL
                and HALF.  Full means the  Cyber  will  echo  the
                characters  you  type.  Half means the local sys-
                tems echos them.  Full is  the  default,  and  is
                used by most hosts.

        INIT-RETRY <decimal-number>
                Set the maximum number of retries allowed for the
                initial connection before giving up.

        PARITY <keyword>
                Allows you to adjust  the  parity  on  characters
                send  by  Kermit-170 to another system's require-
                ments.  The possibilities are  NONE,  EVEN,  ODD,
                SPACE, or MARK.  If NONE, then the 8th bit can be
                used for data when sending and  receiving  binary
                files.  If other than NONE, the 8th bit on outgo-
                ing characters will be set to achieve the desired
                parity,  and  the  8th bit on incoming characters
                will be discarded.  The default is NONE.

        RECEIVE <parameter> <value>
                These commands allow you to specify to the  other
                Kermit  what  the  packets  it  sends should look
                like, or to inform this Kermit what to expect.

                EOLCHR <octal-number>
                        The octal value of the ASCII character to
                        be  used as a line terminator or packets,
                        if one is required by the  other  system.
                        Carriage return (15B) is the default.

                PACKLEN <decimal-number>
                        Maximum packet length  to  send,  decimal
                        number, between 20 and 94, 94 by default.

                PADCHR <octal-number>
                        Character to use for padding.  Default is
                        NUL.

                PADLEN <decimal-number>
                        How much padding to send before a packet.
                        Default is no padding.

                QUOTECHR <octal-number>
                        What printable character to use for quot-
                        ing of control characters.

                SYNCCHR <octal-number>
                        The control character that marks the  be-
                        ginning  of  the  packet.   Normally  SOH
                        (Control-A, ASCII 1).  There should be no
                        reason to change this.

                TIMEOUT <decimal-number>
                        How many seconds the other Kermit  should
                        wait  for  a packet before asking for re-
                        transmission.

        RETRY <decimal-number>
                Set the maximum number of  retries  for  a  given
                packet before giving up.

        SEND <parameter> <value>
                These commands allow you to specify how  outgoing
                packets should look, in case the other Kermit has
                nonstandard requirements.

                EOLCHR <octal-number>
                        The octal value of the ASCII character to
                        be used as a line terminator for packets,
                        if one is required by the  other  system.
                        Carriage return (15B) by default.

                PACKLEN <decimal-number>
                        Maximum packet length  to  send,  decimal
                        number, between 20 and 94, 94 by default.

                PADCHR <octal-number>
                        Character to use for padding.  Default is
                        NUL.

                PADLEN <decimal-number>
                        How much padding to send before a packet.
                        Default is no padding.

                QUOTECHR <octal-number>
                        What printable character to use for quot-
                        ing  of  control characters.  The default
                        is "#" (43B).  there should be no  reason
                        to change this.

                SYNCCHR <octal-number>
                        The control character that marks the  be-
                        ginning  of  the  packet.   Normally  SOH
                        (Control-A, ASCII 1).  There should be no
                        reason to change this.

                TIMEOUT <decimal-number>
                        How many seconds the other Kermit  should
                        wants  before being asked for retransmis-
                        sion.  Unfortunately, the  Cyber  has  no
                        way  of  timing  out so this parameter is
                        ignored.

SHOW    Display current SET parameters,  version  of  Kermit-170,
        and other information.

STATUS  Give statistics about the most recent file transfer.

Planned further enhancements to  Kermit-170  being  done  at  the
University of Texas include:

   - Addition of new server functions: directory,  type,  delete,
     etc.

   - Host commands -- pass a command string to the system for ex-
     ecution.   This  may be a problem when implementing at other
     NOS sites.

   - Two and Three character checksums.

   - 8th-bit quoting, to allow transfer of binary files with sys-
     tems that can't use the parity bit for data.

   - Temporary escaping back to control command level.

   - Badly needed performance tuning.  Currently we have been ex-
     periencing  500-900 baud effective data throughput on a 2400
     baud line.