Command? R CPMUG-PROTOCOL

<CPMUG-PROTOCOL>   27-AUG-82
Parent: PROTOCOLS
MODEM PROTOCOL OVERVIEW  178 lines, 7.5K

1/1/82 by Ward Christensen.  I will maintain a master copy of
this.  Please pass on changes or suggestions via CBBS/Chicago
at (312) 545-8086, or by voice at (312) 849-6279.

NOTE this does not include things which I am not familiar with,
such as the CRC option implemented by John Mahr.

Last Rev: (none)

At the request of Rick Mallinak on behalf of the guys at
Standard Oil with IBM P.C.s, as well as several previous
requests, I finally decided to put my modem protocol into
writing.  It had been previously formally published only in the
AMRAD newsletter.

        Table of Contents
1. DEFINITIONS
2. TRANSMISSION MEDIUM LEVEL PROTOCOL
3. MESSAGE BLOCK LEVEL PROTOCOL
4. FILE LEVEL PROTOCOL
5. DATA FLOW EXAMPLE INCLUDING ERROR RECOVERY
6. PROGRAMMING TIPS.

-------- 1. DEFINITIONS.
<soh>   01H
<eot>   04H
<ack>   05H
<nak>   15H
<can>   18H

-------- 2. TRANSMISSION MEDIUM LEVEL PROTOCOL
Asynchronous, 8 data bits, no parity, one stop bit.

    The protocol imposes no restrictions on the contents of the
data being transmitted.  No control characters are looked for
in the 128-byte data messages.  Absolutely any kind of data may
be sent - binary, ASCII, etc.  The protocol has not formally
been adopted to a 7-bit environment for the transmission of
ASCII-only (or unpacked-hex) data , although it could be simply
by having both ends agree to AND the protocol-dependent data
with 7F hex before validating it.  I specifically am referring
to the checksum, and the block numbers and their ones-
complement.
.cp 16

    Those wishing to maintain compatibility of the CP/M file
structure, i.e. to allow modemming ASCII files to or from CP/M
systems should follow this data format:
  * ASCII tabs used (09H); tabs set every 8.
  * Lines terminated by CR/LF (0DH 0AH)
  * End-of-file indicated by ^Z, 1AH.  (one or more)
  * Data is variable length, i.e. should be considered a
    continuous stream of data bytes, broken into 128-byte
    chunks purely for the purpose of transmission. 
  * A CP/M "peculiarity": If the data ends exactly on a
    128-byte boundary, i.e. CR in 127, and LF in 128, a
    subsequent sector containing the ^Z EOF character(s)
    is optional, but is preferred.  Some utilities or
    user programs still do not handle EOF without ^Zs.
  * The last block sent is no different from others, i.e.
    there is no "short block".  

-------- 3. MESSAGE BLOCK LEVEL PROTOCOL
 Each block of the transfer looks like:
<SOH><blk #><255-blk #><--128 data bytes--><cksum>
    in which:
<SOH>       = 01 hex
<blk #>     = binary number, starts at 01 increments by 1, and
              wraps 0FFH to 00H (not to 01)
<255-blk #> = blk # after going thru 8080 "CMA" instr, i.e.
              each bit complemented in the 8-bit block number.
              Formally, this is the "ones complement".
<cksum>     = the sum of the data bytes only.  Toss any carry.

-------- 4. FILE LEVEL PROTOCOL

---- 4A. COMMON TO BOTH SENDER AND RECEIVER:

    All errors are retried 10 times.  For versions running with
an operator (i.e. NOT with XMODEM), a message is typed after 10
errors asking the operator whether to "retry or quit".
    Some versions of the protocol use <can>, ASCII ^X, to
cancel transmission.  This was never adopted as a standard, as
having a single "abort" character makes the transmission
susceptible to false termination due to an <ack> <nak> or <soh>
being corrupted into a <can> and canceling transmission.
    The protocol may be considered "receiver driven", that is,
the sender need not automatically re-transmit, although it does
in the current implementations.
.cp 13

---- 4B. RECEIVE PROGRAM CONSIDERATIONS:
    The receiver has a 10-second timeout.  It sends a <nak>
every time it times out.  The receiver's first timeout, which
sends a <nak>, signals the transmitter to start.  Optionally,
the receiver could send a <nak> immediately, in case the sender
was ready.  This would save the initial 10 second timeout. 
However, the receiver MUST continue to timeout every 10 seconds
in case the sender wasn't ready.
    Once into a receiving a block, the receiver goes into a
one-second timeout for each character and the checksum.  If the
receiver wishes to <nak> a block for any reason (invalid
header, timeout receiving data), it must wait for the line to
clear.  See "programming tips" for ideas
    Synchronizing:  If a valid block number is received, it
will be: 1) the expected one, in which case everything is fine;
or 2) a repeat of the previously received block.  This should
be considered OK, and only indicates that the receivers <ack>
got glitched, and the sender re-transmitted; 3) any other block
number indicates a fatal loss of synchronization, such as the
rare case of the sender getting a line-glitch that looked like
an <ack>.  Abort the transmission, sending a <can>

---- 4C. SENDING PROGRAM CONSIDERATIONS.

    While waiting for transmission to begin, the sender has
only a single very long timeout, say one minute.  In the
current protocol, the sender has a 10 second timeout before
retrying.  I suggest NOT doing this, and letting the protocol
be completely receiver-driven.  This will be compatible with
existing programs.
    When the sender has no more data, it sends an <eot>, and
awaits an <ack>, resending the <eot> if it doesn't get one. 
Again, the protocol could be receiver-driven, with the sender
only having the high-level 1-minute timeout to abort.

.cp24

-------- 5. DATA FLOW EXAMPLE INCLUDING ERROR RECOVERY

Here is a sample of the data flow, sending a 3-block message.
It includes the two most common line hits - a garbaged block,
and an <ack> reply getting garbaged.  <xx> represents the
checksum byte.

SENDER                                  RECEIVER
                                times out after 10 seconds,
                        <---            <nak>
<soh> 01 FE -data- <xx> --->
                        <---            <ack>
<soh> 02 FD -data- xx   --->    (data gets line hit)
                        <---            <nak>
<soh> 02 FD -data- xx   --->
                        <---            <ack>
<soh> 03 FC -data- xx   --->
   (ack gets garbaged)  <---            <ack>
<soh> 03 FC -data- xx   --->            <ack>
<eot>                   --->
                        <---            <ack>

-------- 6. PROGRAMMING TIPS.

* The character-receive subroutine should be called with a
parameter specifying the number of seconds to wait.  The
receiver should first call it with a time of 10, then <nak> and
try again, 10 times.
  After receiving the <soh>, the receiver should call the
character receive subroutine with a 1-second timeout, for the
remainder of the message and the <cksum>.  Since they are sent
as a continuous stream, timing out of this implies a serious
like glitch that caused, say, 127 characters to be seen instead
of 128.

* When the receiver wishes to <nak>, it should call a "PURGE"
subroutine, to wait for the line to clear.  Recall the sender
tosses any characters in its UART buffer immediately upon
completing sending a block, to ensure no glitches were mis-
interpreted.
  The most common technique is for "PURGE" to call the
character receive subroutine, specifying a 1-second timeout,
and looping back to PURGE until a timeout occurs.  The <nak> is
then sent, ensuring the other end will see it.

* You may wish to add code recommended by Jonh Mahr to your
character receive routine - to set an error flag if the UART
shows framing error, or overrun.  This will help catch a few
more glitches - the most common of which is a hit in the high
bits of the byte in two consecutive bytes.  The <cksum> comes
out OK since counting in 1-byte produces the same result of
adding 80H + 80H as with adding 00H + 00H.
-- No child messages --

Command? CPM
Type BINEX after the A0> prompt to return to BIN-EX
Type CHAT to chat with the system operator; BYE to quit
BIN-EX message texts are on USER 1, A: and B: drives
Files for downloading are on USER 0, both drives; DIR for directory


A0>USER 0

A0>DIR A:

ALIENS11.DOC   4k | ALIENS11.OBJ  14k | BACKUP  .ASM  28k | BACKUP  .DOC   8k
BINEX   .COM   2k | BY2-8250.ASM   8k | BY2-8251.ASM   8k | BY2-MMII.ASM   8k
BY2-SIO .ASM   8k | BYE     .COM   2k | BYEII   .ASM  52k | CAL     .OBJ   6k
CATALOG .      4k | CHAT    .COM   2k | CHESS   .OBJ   8k | DISK    .OBJ   4k
DISK74A .DOC   6k | DISK76  .ASM  48k | DOWNLOAD.HLP   6k | DU      .OBJ   6k
DU-V77  .DOC   6k | FIND    .COM   2k | FIND    .DOC   2k | FIND    .OBJ   2k
FIXTEX  .ASM  22k | HELP    .OBJ   4k | MBOOT   .ASM   8k | MBOOTVT .ASM   6k
MDM705  .DOC  34k | MDM705  .OBJ  18k | MDM705  .SET   8k | MDM705CF.ASM  14k
MDM705NM.ASM   4k | MDM705VT.DOC   4k | MDM705VT.OBJ  16k | MDMEQU02.DOC  12k
PACMAN  .DOC   2k | PACMAN  .OBJ  18k | PIPMODEM.ASM   4k | PIPMODEM.DOC   8k
PROT    .OBJ   4k | RCPM-038.LST  22k | SD      .OBJ   2k | SSUB    .OBJ   4k
USQ     .OBJ  10k | XMODEM  .COM   4k | XMODEM  .HLP   2k | Z2CON   .WQ   78k
Z80CHESS.DOC   6k | Z80CHESS.OBJ   8k | ZZERR   .DAT   2k | ZZMUMPS .DOC   2k
ZZMUMPS .OBJ  42k | ZZSETGLB.OBJ   2k | ZZSETMPS.OBJ   2k
        Drive A, user 0 contains 616K in 55 files with 144K free
A0>TYP XMODEM.HLP
TYP?
A0>TYPE A:XMODEM.HLP
Ctrl-S pauses, Ctrl-C Aborts, Ctrl-X skips to next file

Listing file A:XMODEM.HLP

   XMODEM is the downloading program on this system. It transfers binary
files block by block with error checking using either a CHECKSUM
or CRC. The protocol is known as the CPMUG or Christensen protocol.
It is compatible with several communications programs. 
 
   The syntax for its use is:

                XMODEM S filename.typ    (to send a file from here to you)

or

                XMODEM R filename.typ    (to receive a file from you) 


Programs which are compatible include:

MDM705    PUBLIC DOMAIN     (available from this system)  CP/M
MODEM7      "      "        
MODEM2      "      "
MODEM etc   "      "

MODEMIBM  PUBLIC DOMAIN     (available from this system) PCDOS
AMODEM    PUBLIC DOMAIN     (available from this system) ATARI
UMODEM    PUBLIC DOMAIN     (available from this suytem) UNIX

AMCALL    MicroCALL Services 9655-M Homestead Court, Laurel MD 20707

ASCOM     DMA or Westico  25 Van Zant Street, Norwalk CT 06855 
          CP/M-80, CP/M-86, PCDOS, MSDOS  

M.I.T.E.  Mycroft Labs  PO Box 6045 Tallahassee, FL 32301      
          CP/M-80       

COMMX     Hawkeye Grafix  23914 Mobile, Canoga Park, CA 91307
          CP/M-80  $150 or $900 source (also available in
          FORTRAN for use on mainframe) (213) 348-7909

PC-TALK III  The Headlands Press, PO BOX 862, Tiburon, CA 94920
             for IBM-PC  suggested donation $35.00 (or freeware)

MODEM80   The Alternate Source, 705 N. Pennsylvania, Lansing, MI 48906
          $39.85 TRS-80 MOD 1 & III Reviewed in May 1983 Creative Computing

ZTERM Professional    Southwestern Data Systems, PO Box 582, Santee CA 92071
          $149   Apple softcard CP/M Review May 1983 Creative Computing

ASCII Express Professional Southwestern Data Systems - APPLE II 48K

LMODEM    (DEC-10)
UMODEM    (UNIX)     Written in C (available on this system)
VMODEM    (VAX-VMS)  a VAX version of UMODEM (available on this system)
XCHANGE-11 (PDP-11 RSTS-E)
A0>DIR B:

AMODEM42.ATR  10k | APMBOOT .ASM   8k | CAT     .OBJ   2k | CIS-DOW .MAC  14k
CIS-EXEC.AQM  20k | CIS-EXEC.DOC   4k | CIS-MNET.PRO  14k | CISINFO .DOC   2k
CISPROTO.DOC  18k | CRCK8   .OBJ   6k | DBASE   .NTS   6k | ELIZA   .BAS   8k
HELP    .HQP   2k | HELP2   .HQP  14k | HELP20  .AQM  24k | INDEX   .OBJ  10k
INTNET  .TXT   4k | LDIR    .OBJ   6k | LRUN    .OBJ   2k | LU      .DOC  24k
LU      .OBJ  18k | LUDEF1  .DOC   8k | MASTHEAD.ASM   6k | MDM705  .INF   6k
MDM705  .MSG   2k | MDM705AP.ASM  10k | MDM705DP.ASM   8k | MDM705HZ.ASM   8k
MDM705OS.ASM  14k | MDM705XE.ASM  10k | MENU    .DQC   4k | MENU    .OQJ  10k
MFT     .ASM  18k | MMDF    .PQO  22k | MNETCMD .TRS   2k | MODEM80 .TRS  12k
MODEMIBM.ASM  56k | NAPLPS  .DOC  22k | NCAT    .OBJ   8k | PC-APRG .DOC  12k
PCSERPRO.DQC  16k | PRLMOV  .ASM   4k | RAMDSK  .ASM  24k | RAMDSK  .DOC   4k
RAMDSK  .OBJ   2k | RESOURCE.OBJ   8k | REZ     .DOC  30k | SCRAMBLE.ASM   6k
SCRAMBLE.DOC   2k | SORTV   .DOC   2k | SORTV-12.MAC  14k | SYNONYM .ASM   6k
SYNONYM .DOC   4k | UMODEM  .DOC   4k | UMODEM28.C    38k | UMODEM28.HLP   8k
UNSPOOL .DOC  10k | UNSPOOL .MAC  18k | UNSPOOL .OBJ   2k | VMODEM28.C     8k
VMODEM28.H     2k | XREF    .BAS   6k
        Drive B, user 0 contains 672K in 62 files with 28K free