INCBK.COM (or NEVER FORGET YOUR BACKUPS AGAIN)


	by	HARVEY EDWARDS
		CODE 8321
		U.S. NAVAL OCEANOGRAPHIC OFFICE
		NSTL STATION, MS 39522

	INCBK.COM is a general purpose system backup routine.  It can be 
self-submitting or a "one-shot" deal where a particular disk is backed up.
INCBK is  capable of incremental or full backups.
	INCBK runs in a batch environment fairly well, especially since 
it has a few privs that it can throw around to increase its priority.
(This was necessary on our system because batch jobs normally run at 
a priority of 1 and INCBK would sit idle with a tape drive for long 
periods, just waiting for its turn to compute.)
	If your backup requires more than one tape, the system will
tell you to mount the next volume.  This step will require oper privs
from an operator's terminal (ie. REPLY/TO=##). 

HOW TO USE INCBK.COM
	
	1)  Decide whether you want a self-submitting routine or a 
	    one-shot.  If you desire, the self-submitting routine
	    can control several one-shotters.  

	2)  Submit INCBK.COM (what could be easier?) To start the self-
	    submitting ritual, submit INCBK with no parameters.
	    For one-shots, submit with the desired disk as the parameter
	    (eg: submit/param=dja2 INCBK.COM).  To do a full backup
	    on the targetted disk, p2=full (eg: submit/param=(dja2,full) 
	    INCBK.COM). (-- You might want to try using START.COM)
	
	INCBK will look for a free tape drive to do the backup on.  If it
finds one, fine.  If it doesn't, then it rusubmits itself to check again
in 15 minutes.  It will continue trying until quitting time and if
it still hasn't grabbed a drive by then, it will resubmit itself to
become active the next morning.  
	Once INCBK finds a tape drive it will ask to have a tape
mounted for backup on the drive.  A request is sent to the operator
console every 5 minutes for 25 minutes.  After that, INCBK assumes
that the operator is asleep and will make a plea to the commoners
every 5 minutes for 10 minutes.  If there is still no response, then
INCBK assumes that it must be a federal holiday and its wasting its
time.  It then resubmits itself for what should be the next working
day.
	After the tape is successfully initialized and mounted, INCBK
does the appropriate backup (incremental or full) on the selected disk.
When the backup is complete, the drive is dismounted, the operator
notified that the backup is complete and a listing is queued to print at 11:00
(a slow time around here).  
	Finally (if in the self-submitting mode), INCBK calculates 
when the next incremental backup should be and submits itself for the 
appropriate time.