USING FPAINT SCREENS: AN EXAMPLE APPLICATION




                                 John Sinclair
                                   Mark Geib
                              Inland Steel Company
                                  10-Oct-1986

                                                                Page 1


     Using FPaint Screens - general considerations


          FPaint builds a  package  of  FORTRAN  subroutines  that  may  be
     considered  the  abstraction  of a data entry screen.  Each screen has
     the following characteristics:

          - A five character name ( referred to below as <NAME> )

          - A specific height (in rows) and width (in columns)

          - A number of fixed text fields

          - A number of data fields of varying characteristics

          - A screen help line



     In addition, the following operations may be performed on a screen:

          - Clear        - clear the area occupied by the screen

          - Display Text - display screen text

          - Display Data - display screen data field contents

          - Edit         - begin edit of screen data fields

          - Validate     - validate all screen data fields


          Using an FPaint screen successfully therefore depends on invoking
     the  above routines properly and in the correct order.  The first task
     is thus to examine each routine in detail.


     FPaint Screen Operations - A Detailed Description


     Clear

     The Clear operation is invoked as

     call <NAME>Clear( Row, Col )

          where Row and Col give the origin of the upper left of the screen
          in rows and cloumns on the CRT relative to the upper left corner.

     Clear causes the rectangular area of the CRT occupied by the screen to
     be erased.  The given area extends from rows "Row" to "Row"+Height and
     from columns "Col" to "Col"+Width.

                                                                Page 2


     Text Display

     The Text Display operation is invoked as

     call <NAME>TextDsp( Row, Col )

          where Row and Col give the origin of the upper left of the screen
          in rows and cloumns on the CRT relative to the upper left corner.

     Text Display causes all screen text fields to be displayed on the  CRT
     relative the the screen origin.


     Data Display

     The Data Display operation is invoked as

     call <NAME>DataDsp( Row, Col, First, Last, {Data} )

          where Row and Col give the origin of the upper left of the screen
          in rows and cloumns on the CRT relative to the upper left corner,
          First is the first field to be displayed, Last is the last  field
          to  be  displayed  and  {Data}  is  the  list  of  variables that
          correspond to the FPaint data fields.

     Data Display causes the current value of  all  specified  screen  data
     fields  to  be  displayed  on  the CRT relative the the screen origin.
     Note that all data  should  be  initialized  prior  to  invoking  this
     routine.


     Edit

     The Edit operation is invoked as

     call <NAME>Edit( Row, Col, First, Last, CurrentField, TermKeys,
                      {Data}, Next, Previous, Refresh, Exit, LastKey )

          where,

          Row and Col give the origin of the upper left of  the  screen  in
          rows and cloumns on the CRT relative to the upper left corner;

          First is the first field to be edited and Last is the last  field
          to be edited;

          CurrentField is, on input, the field at which editing is to begin
          and, on output, the last field edited;

          TermKeys is a 30 element integer*2 array to be discussed later;

          {Data} is the list of variables that  correspond  to  the  FPaint

                                                                Page 3


          data fields;

          Next is a termination flag that indicates a  carraige  return  or
          down arrow was pressed during edit of the last field;

          Previous is a termination flag that indicates  an  up  arrow  was
          pressed during edit of the first field;

          Refresh       is a termination flag  that  indicates  the  screen
          image should be refreshed;

          Exit is a termination flag that indicates the edit is complete;

          LastKey is the last key typed by the operator.

     The Edit operation initiates data entry or edit of all specified  data
     fields  beginning  with  the  current field.  This operation continues
     until terminated by the operator.

     Edit is terminated by any one of the following events:

        - The operator presses a carriage return  or  a  down  arrow  while
          editing the last field of the screen.  In this case, Next is set,
          which, for multi screen  applications,  means  "go  to  the  next
          screen".

        - The operator presses an up arrow while editing the first field of
          the  screen.   In  this  case,  Previous is set, which, for multi
          screen applications, means "go to the previous screen".

        - The operator presses control R.  In this case,  Refresh  is  set,
          which  means  "refresh  the  entire  screen  image".  This may be
          necessary if, during data entry, a system message  covers  up  an
          area of the screen.

        - The operator presses control Z.  In this case, Exit is set, which
          means "data entry/edit is complete".

        - The operator presses a programmer defined termination key ( named
          TermKeys  in  the  Edit  parameter  list ).  No flags are set but
          LastKey holds the ASCII value of the pressed key.


          Validate

          The validate operation is invoked as

          call <NAME>Validate( First, Last, {Data}, Valid, FieldNumber )

          where First is the first field to be displayed, Last is the  last
          field  to  be  displayed and {Data} is the list of variables that
          correspond to the FPaint data fields.

                                                                Page 4


     Validate performs a validation check on all specified data fields.  If
     any  field  is invalid, Valid is set to .false.  and FieldNumber holds
     the index of the offending data field.  If all fields are valid, Valid
     is set to .true.  and FieldNumber is undefined.


     Programmer Defined Termination Keys


          As mentioned above, a special set  of  keys,  called  termination
     keys,  may  be  defined  by the programmer.  During an edit operation,
     pressing one of these keys causes the edit  to  terminate.   A  thirty
     element integer array contains the termination key information.

          As if to complicate things, two types  of  termination  keys  may
     reside in the array simultaneously as separate lists.  These two types
     will be refered to as edit termination keys and immediate  termination
     keys.

          When an edit  termination  key  is  pressed,  FPaint  checks  the
     validity  of  the  current  field  being  edited.   If valid, the edit
     terminates, otherwise an error message is issued and edit continues.

          An immediate termination key, as  its  name  implies,  causes  an
     immediate  and  unconditional termination of the edit.  A possible use
     for such a device might be that of popping up a help screen to give an
     operator  additional  assistance  upon  demand.   Another  obvious use
     includes the aborting of an operation.

          The  result  of  immediate  termination  is  slightly   different
     depending  on whether or not the current field is numeric.  If, during
     the edit of a numeric data field,  an  immediate  termination  key  is
     pressed,  the  edit  is,  in  effect, aborted and the partially edited
     value lost.  A non-numeric data field  retains  the  partially  edited
     value.

     Important:  It is the programmers responsibility to reenter  the  edit
     routine after processing an immediate termination key without changing
     the edit state.

          The structure of the termination key array is best  described  by
     example.   Figure  1 shows the logical contents of the termination key
     array.  In addition, an example is given below.


     Example 1  A possible array of termination keys

     TermKeys(1) = 4           { 4 edit termination keys }
     TermKeys(2) = 1           { ^A }
     TermKeys(3) = 141         { PF1 }
     TermKeys(4) = ichar('?')  { ? }
     TermKeys(5) = 4           { ^D }

                                                                Page 5


     TermKeys(6) = 2           { 2 immediate termination keys }
     TermKeys(7) = 142         { PF2 }
     TermKeys(8) = 143         { PF3 }

     Appendix III contains the numeric values of function and keypad keys.


     Integrating the Operations


          Having fully described each screen operation, the next  objective
     is  the  synthesis  of  a  working  FPaint  screen.   In  general, the
     following logic is employed:

          - Choose an appropriate origin for the screen.

          - Set First and Last to define the set of data fields to be
            operated upon. This provides the capability to display, edit
            or validate a single field or a specific subset of fields.
            Setting First to 1 and Last to 100 will cause all fields to
            be included in a given operation.

          - Define all termination keys.

          - Initialize all screen data fields.

          - Clear the screen.

          - Display the screen text.

          - Display the screen data.

          - Perform the edit operation starting with a given field number.
            On return from the edit, process the termination flags and
            keys.

          - Insure that all data is valid ( If not, repeat the edit
            operation starting with the invalid field ).

     Rather than elaborating on the above, a specific example will be
     considered in detail.


     Example Program Description


          Appendix I contains the listing of a  program  that  incorporates
     two FPaint screens to perform operator input.  It is based on a system
     that is used to acquire data from a device capable  of  measuring  the
     surface  roughness  of  a  steel specimen.  The example presented here
     serves  merely  to  illustrate  the  use  of  FPaint  screens  in   an
     application;  the  routine  that  would perform any useful work is, of

                                                                Page 6


     course, a stub.

          Presumably, an operator runs the program to measure the roughness
     of  a group of replicate specimens.  Data entry is made at two levels.
     First, information common to all  specimens  is  entered  through  the
     FPaint  screen  named Group.  Then, before each specimen is processed,
     the specimen ID and orientation is entered through the  FPaint  screen
     named Spec.

          The operator may enter individual specimen information repeatedly
     until all replicates of a given group have been processed.  The choice
     is then made either to exit the program or  repeat  the  process  with
     another group of specimens.

          Figure 2 outlines the program logic and processes.



     The FPaint Screens


          Before considering the details of the  FPaint  interface,  it  is
     worthwhile to examine the screens individually.

          Group, the specimen group screen, is shown in Figure 3 and  Spec,
     the individual specimen screen in figure 4.

          The final composite screen (from the operator's  point  of  view)
     includes  Group  with  the  upper left corner origin at (1,1) and Spec
     with origin at (11,39).  This is shown in figure 5.


     A Detailed Examination of the Example


          As mentioned previously, Appendix I contains the  listing  of  an
     example program, Profil.For.  The following is detailed examination of
     the FORTRAN source code.

     Section 1  contains  declarations  for  the  Group  screen  variables.
     Notice the similarity to the declarations given in the Group auxillary
     file listed in Appendix II.  Also note that "Description" is  a  three
     element array.

     Section 2 contains declarations for the Spec screen variables.  Notice
     the  similarity  to  the  declarations given in the Spec auxilary file
     listed in Appendix II.

     Section 3 contains declarations for local variables.

     Section 4 serves to initialize constants and variables.   Notice  that
     screen variables must be initialized in the application.

                                                                Page 7


     Section 5 deserves special attention.

          TTYinit must be called before any FPaint  operation  is  invoked.
     This  is especially true for a VAX hosted system.  TTYinit initializes
     both the display and a package of display routines.  It  may  also  be
     called during program exit to clean up the display state.

          EchoOff  should  be  called  in  DEC-10  environments.   It  will
     eliminate any problems associated with echoed type ahead.

          KpdOn may be called to place the terminal in  keypad  application
     mode.  Note that it is not necessary in this application.

     Section 6:  First field to edit for Group screen is 3.

     Section 7:  Clear the Group screen.

     Section 8:  Display the Group screen text ( figure  6  ).   Note  that
     "description" is an array that contains three FPaint fields.

     Section 9:  Display the Group screen data ( figure 7 ).

     Section 10:  Start of loop "repeat until no more specimen groups".

     Section 11:  Edit the Group screen ( figures 8 and 9 )  starting  with
     field three.  Process the termination state as follows:

          [A] if the operator pressed PF1 ( abort ) then turn off  the  key
          pad, clear the screen, and stop program;

          [B] if "go to next screen" ( i.e.  Next is set ) then simply wrap
          to field number three of the same screen;

          [C] if "go to previous screen" ( i.e.  Previous  is  set  )  then
          simply wrap to the last field;

          [D] if  "screen  needs  to  be  refreshed"  goto  100  to  clear,
          redisplay, and continue the edit of Group.

          [E] if "data entry/edit is not complete" goto 300 to continue the
          edit.

     Section 12:  Validate the Group screen.  If any field is invalid  then
     continue the edit at that field number.

     Section 13:  First field to edit for Spec screen is 1.

     Section 14:  Start of loop "repeat until no more specimens".

     Section 15:  Clear the Spec screen ( figure 10 ).

     Section 16:  Display the Spec screen text ( figure 11 ).

                                                                Page 8


     Section 17:  Display the Spec screen data ( figure 12 ).

     Section 18:  Edit the Spec screen ( figure 13 )  starting  with  field
     one.  Process the termination state as follows:

          [A] if "go to next screen" ( i.e.  Next is set ) then simply wrap
          to field number one of the same screen;

          [B] if "go to previous screen" ( i.e.  Previous  is  set  )  then
          simply wrap to the last field;

          [C] if "screen needs to be refreshed" then  clear  and  redisplay
          the  Group  screen  and  then  goto  400 to clear, redisplay, and
          continue the edit of Spec.

          [D] if "data entry/edit is not complete" goto 500 to continue the
          edit.

     Section 19:  This is the call to some routine that would  utilize  the
     FPaint  input  and perform some useful work.  The routine is a stub in
     this example ( see the listing of Subs.For in Appendix I ).

     Section 20:  Ask operator if more specimens are to be tested for  this
     group ( see the listing of Subs.For in Appendix I ).

     Section 21:  If more specimens for this group then clear and redisplay
     the group screen ( just for looks ).  As the loop repeats the specimen
     screen will again be overlayed on the group screen.

     Section 22:  End of loop "repeat until no more specimens".

     Section 23:  Ask operator if more groups of specimens are to be tested
     ( see the listing of Subs.For in Appendix I ).

     Section 24:  End of loop "repeat until no more specimen groups".

     Section 25:  Key pad off, clear screen, and terminate program.


     Custom Validation of FPaint Data Fields


          Appendix I contains a listing of the file Subs.For, a  collection
     of  subroutines  called  by  the example program.  Of interest to this
     discussion is the routine ValScr.

          Whenever the edit of an FPaint data field is  completed  ( either
     as  a  result  of  moving  to another field or terminating the edit ),
     validation is performed as prescribed when the field was created.   In
     addition,  if  the  data  field  passes  the  FPaint  validation,  the
     subroutine ValScr is called in order that  custom  validation  may  be
     performed by the application.

                                                                Page 9


          ValScr is present in the standard FPaint library as a  stub  that
     sets  the  Valid  flag  true,  thus  imposing no additional validation
     constraints on the data.

          If a subroutine named ValScr is included in the  application,  it
     will  supersede  the  library  stub,  enabling custom validation to be
     performed.  See the example in  Subs.For  for  a  description  of  the
     parameters.   The  logic  of  any such custom routine should always be
     similar to the pseudocode given below:

       if Name is equal to the screen to be validated then

          if Field is equal to the field to be validated then

             check the value of Intg, Rl, or Str  depending  on  the  field
             type ( which is known a priori )

             if the value is OK then
               Valid = .true.
             else
               Valid = .false.
               display some appropriate error message via
               the routine ErrMsg
             end if

          end if

       end if

     ( Note the use of  the  "<Name>Ind"  function  in  the  example,  e.g.
     GroupInd.   This  function  maps  the  field name to the field number.
     Since field numbers may change whenever fields are added to or deleted
     from  an  FPaint screen, this field index function should be used when
     refering to a particular FPaint field ).


     FPaint From the User's Viewpoint


          Up to this point, the description of FPaint has  been  programmer
     oriented.   The application user, of course, is interested in the ease
     with which data may be entered and edited.

          Editing is performed at  two  levels.   Screen  editing  involves
     moving  from one field to another.  This is accomplished with the keys
     described below.

          Up arrow        - Move to the previous data field.
          Down arrow      - Move to the next data field.
          Carriage Return - Move to the next data field.

          Editing may also occur at the individual field level.   The  keys

                                                               Page 10


     listed below perform field edit functions.

          Control B       - Move to beginning of field
          Control E       - Move to end of field
          Tab             - Move to next word
          Control X       - Move to previous word
          Control W       - Toggle insert/overwrite
          Control U       - Abort edit ( restore original value )
          Control J       - Delete to end of line
          Control K       - Delete word

          [Dec-10 or IBM PC]
          Backspace       - delete one character backward
          Delete          - delete character at cursor

          [IBM PC]
          Home            - Move to beginning of field
          End             - Move to end of field
          Shft Tab        - Move to previous word
          Insert          - Toggle insert/overwrite

          [Vax]
          Delete          - delete one character backward
          Key pad ,       - delete character at cursor
                            ( if key pad mode has been turned on )


          In addition to the editing keys, the function of  Control  R  and
     Control  Z  are worth repeating at this point.  They have the meanings
     given below.

          Control R       - Refresh screen image
          Control Z       - Data entry/edit is complete

                                                               







                                           FIGURES


                                                               


                   Array Element        Contents

                        1               Number of Edit Termination Keys, NE
                        2               Edit Termination Key 1
                        3               Edit Termination Key 2
                        .                       .
                        .                       .
                        .                       .
                       1+NE             Edit Termination Key NE

                      (NE+2)            Number of Immediate Termination Keys, NI
                      (NE+2)+1          Immediate Termination Key 1
                      (NE+2)+2          Immediate Termination Key 2
                        .
                        .
                        .
                      (NE+2)+NI         Immediate Termination Key NI


                                 Figure 1. Termination Key Array.


                   Program Profilometer

                   Initialize Terminal Routines

                   Display Specimen Group Information

                   Repeat

                     Get Specimen Group Information

                     Repeat

                       Display and Get Specimen Information

                       Collect and Plot Test Data

                       More Specimens?
                         if Yes then Display Specimen Group Information

                     Until No More Specimens

                     Another Specimen Group?

                   Until No More Specimen Groups

                   Program End


                                 Figure 2. Main program pseudo code.

                                                               






                                          APPENDIX I


                                     EXAMPLE PROGRAM LISTINGS


                                                               






                                        PROFIL.FOR





                  This is an example of a program that uses two FPaint screens.

                  An operator runs this program to measure the surface characteristics
                  of a group of replicate specimens.

                  The first screen, Group, is a data entry screen that contains
                  specimen group information, i.e., information common to all
                  specimens.

                  The second screen, Spec, contains information unique to each
                  specimen, namely the specimen ID and orientation.

                  Note that the portion of the program that would actually do
                  some useful work is, of course, a stub.


                                                               



                program Profilometer


          C     SECTION 1

          c---
          c  variable declarations  ( Group screen )

                  Integer*2 GRow, GCol, GCurField, GTermKeys(30)
                  Integer*2 GNumberOfFields, GLastKey, GFirstFld, GLastFld
                  Logical*1 GNext, GPrevious, GExit, GRefresh

                  character* 4    Version
                  character* 9    Date
                  character* 6    GroupID
                  character* 3    Operator
                  character*65    Description(3)
                  integer*2       ScanRate
                  character* 6    StageVelocity


          C     SECTION 2

          c---
          c  variable declarations  ( Specimen screen )

                  Integer*2 SRow, SCol, SCurField, STermKeys(30)
                  Integer*2 SNumberOfFields, SLastKey, SFirstFld, SLastFld
                  Logical*1 SNext, SPrevious, SExit, SRefresh

                  character* 6    SpecimenID
                  character*12    Orientation


          C     SECTION 3

          c---
          c Misc variables
                integer*2 Abort, FieldNumber
                logical*1 More, Valid

          C     SECTION 4

          c---
          c Variable initialization

                data Abort /141/

                data GRow /1/ , GCol /1/ , SRow /11/ , SCol /39/

          c---

                                                               


          c immediate termination on F1 key
                  data GTermKeys/ 0, 1, 141, 27*0 /

                  data STermKeys/ 30*0 /

                  Version = '1.00'
                  call Today( Date )
                  GroupID = ' '
                  Operator = ' '
                  Description(1) = ' '
                  Description(2) = ' '
                  Description(3) = ' '
                  ScanRate = -1
                  StageVelocity = '1.0'
                SpecimenID = ' '
                Orientation = 'Transverse'


          c---
          c Total number of screen parameters

                  GNumberOfFields = 9
                GFirstFld = 1
                GLastFld = 9

                  SNumberOfFields =   2
                SFirstFld = 1
                SLastFld = 2


          C     SECTION 5

          c--   Initialize Terminal Routines
                call TTYinit
                call EchoOff
                call KpdOn


          c--   Display Specimen Group Information

          100   continue

          C     SECTION 6
                GCurField = 3

          150   continue

          C     SECTION 7
                  call GroupClear( GRow, GCol )

          C     SECTION 8
                  call GroupTextDsp( GRow, GCol )

                                                               



          C     SECTION 9
                  call GroupDataDsp( GRow, GCol, GFirstFld, GLastFld
               1 , Version, Date, GroupID, Operator, Description, ScanRate
               1 , StageVelocity
               1   )

          C     SECTION 10

          c--   repeat
          200   continue

          c--     Get Specimen Group Information

          C     SECTION 11
          300       call GroupEdit( GRow, GCol, GFirstFld, GLastFld, GCurField
               1   , GTermKeys, Version, Date, GroupID, Operator, Description
               1   , ScanRate, StageVelocity
               1   , GNext, GPrevious, GExit, GRefresh, GLastKey )

          C     SECTION 11 [A]
                  if( GLastKey .eq. Abort ) then
                    call KpdOff
                    call ClrScr
                    stop '[Program Aborted]'

          C     SECTION 11 [B]
                  else if( GNext ) then
                    GCurField = 3

          C     SECTION 11 [C]
                  else if( GPrevious ) then
                    GCurField = GNumberOfFields

          C     SECTION 11 [D]
                  else if( GRefresh ) then
                    goto 150

                  end if

          C     SECTION 11 [E]
                  if( .not. GExit ) goto 300


          c--     Validate Specimen Group Information

          C     SECTION 12
                    call GroupValidate( GFirstFld, GLastFld
               1   , Version, Date, GroupID, Operator, Description, ScanRate
               1   , StageVelocity
               1   , Valid, FieldNumber )


                                                               


                  if( .not. Valid ) then
                    GCurField = FieldNumber
                    goto 300
                  end if


          390     continue

          C     SECTION 13
                  SCurField = 1

          C     SECTION 14
          c--     repeat
          400     continue

          c--       Display and get Specimen Information

          C     SECTION 15
                      call SpecClear( SRow, SCol )

          C     SECTION 16
                      call SpecTextDsp( SRow, SCol )

          C     SECTION 17
                      call SpecDataDsp( SRow, SCol, SFirstFld, SLastFld
               1     , SpecimenID, Orientation
               1       )

          C     SECTION 18
          500         call SpecEdit( SRow, SCol, SFirstFld, SLastFld, SCurField
               1     , STermKeys, SpecimenID, Orientation
               1     , SNext, SPrevious, SExit, SRefresh, SLastKey )

          C     SECTION 18 [A]
                      if( SNext ) then
                      SCurField = 1

          C     SECTION 18 [B]
                    else if( SPrevious ) then
                      SCurField = SNumberOfFields

          C     SECTION 18 [C]
                    else if( SRefresh ) then
                        call GroupClear( GRow, GCol )
                        call GroupTextDsp( GRow, GCol )
                        call GroupDataDsp( GRow, GCol, GFirstFld, GLastFld
               1       , Version, Date, GroupID, Operator, Description, ScanRate
               1       , StageVelocity
               1         )
                      goto 400

                    end if

                                                               



          C     SECTION 18 [D]
                    if( .not. SExit ) goto 500

          C     SECTION 19
          c--       Collect and Plot Test Data
                    call DoTest

          C     SECTION 20
          c--       More Specimens?
                    call MoreSpecs( More )

          C     SECTION 21
          c--         if Yes then Display Specimen Group Information
                      if( More ) then
                          call GroupClear( GRow, GCol )
                          call GroupTextDsp( GRow, GCol )
                          call GroupDataDsp( GRow, GCol, GFirstFld, GLastFld
               1         , Version, Date, GroupID, Operator, Description, ScanRate
               1         , StageVelocity
               1           )
                      end if

          C     SECTION 22
          c--     until no more specimens
                  if( More ) goto 390

          C     SECTION 23
          c--     Another Specimen Group?
                  call MoreGroups( More )

          C     SECTION 24
          c--   until no more specimen groups
                if( More ) goto 100

          C     SECTION 25
                call KpdOff
                call ClrScr
                stop '[Normal Program Termination]'

          c--   program end
                end


                                                               







                                         SUBS.FOR





                    subroutine ValScr - An example of custom validation for the
                                      two FPaint screens.

                    logical function LegalFileName - Called by ValScr.

                  subroutine DoTest - A stub. If this program really did something,
                                      it would be done here.

                  subroutine MoreGroups - A routine that asks the operator if he
                                          has more specimen groups. Includes an
                                          example of the use of the routine Menu1.

                  subroutine MoreSpecs - A routine that asks the operator if he
                                         has more specimens. Includes an example
                                         of the use of the routine Menu1.


                                                               







                subroutine ValScr( Name, Field, Intg, Rl, Str, Valid )

          c--
          c This is a custom validation routine for the profilometer program.
          c
          c The program uses two Fpaint screens, GROUP and SPEC. The following
          c validation will be performed:
          c
          c
          c     For the screen GROUP ( i.e. Name = 'GROUP' )
          c
          c       The "GroupID" field (character) must be a
          c       valid file name.
          c
          c
          c     For the screen SPEC ( i.e. Name = 'SPEC' )
          c
          c       The "SpecimenID" field (character) must be a
          c       valid file name.
          c
          c--

                character*(*) Name
                integer*2 Field, Intg
                real Rl
                character*(*) Str
                logical*1 Valid


          c-- functions
                logical*1 LegalFileName
                integer*2 GroupInd, SpecInd


                Valid = .true.

                if( Name .eq. 'GROUP' ) then

                  if( Field .eq. GroupInd( 'GroupID' ) ) then

                    if( .not. LegalFileName(Str) ) then
                      Valid = .false.
                      call ErrMsg( 'Group ID must be a valid file name!' )
                    end if

                  end if


                                                               



                else if( Name .eq. 'SPEC' ) then

                  if( Field .eq. SpecInd( 'SpecimenID' ) ) then

                    if( .not. LegalFileName(Str) ) then
                      Valid = .false.
                      call ErrMsg( 'Specimen ID must be a valid file name!' )
                    end if

                  end if

                end if


                end


                logical*1 function LegalFileName( String )

                character*(*) String
                character*1 C
                integer*2 I, Length

                do 10 I = 1 , length( String )

                  C = String(I:I)

                  if(  ( C .lt. '0' .or. C .gt. '9' ) .and.
               1               ( C .lt. 'A' .or. C .gt. 'Z' ) .and.
               1               ( C .lt. 'a' .or. C .gt. 'z' )  ) then

                    LegalFileName = .false.
                    return

                  end if

          10    continue

                LegalFileName = .true.

                end


                subroutine DoTest

                integer*2 Key

                call ClrScr
                call CsrPos( 3, 20 )
                call OutString( 'The test would be performed at this point' )


                                                               


                call DspMessage( 'Press a key', 'to continue' )
                call FPGetChar( Key )

                end


                subroutine MoreGroups( More )

                logical*1 More, Abort
                integer*2 Item, Selection, Intense

                data Intense /2/, Normal /0/

                call EraseRegion( 23,1, 24,80 )
                call DspAttribute( Intense )
                call CsrPos( 23, 1 )
                call OutString( 'Another Specimen Group?' )
                Item = 1
          10    call Menu1( 24, 'Yes   No', 'YN', Item, Selection, Abort )

                if( Abort ) goto 10

                call DspAttribute( Normal )
                call EraseRegion( 23,1, 24,80 )

                if( Selection .eq. ichar('Y') ) then
                  More = .true.
                else
                  More = .false.
                end if

                end


                subroutine MoreSpecs( More )

                logical*1 More, Abort
                integer*2 Item, Selection, Intense

                data Intense /2/, Normal /0/

                call EraseRegion( 23,1, 24,80 )
                call DspAttribute( Intense )
                call CsrPos( 23, 1 )
                call OutString( 'Another Specimen?' )
                Item = 1
          10    call Menu1( 24, 'Yes   No', 'YN', Item, Selection, Abort )

                if( Abort ) goto 10

                call DspAttribute( Normal )
                call EraseRegion( 23,1, 24,80 )

                                                               



                if( Selection .eq. ichar('Y') ) then
                  More = .true.
                else
                  More = .false.
                end if

                end

                                                               








                                         APPENDIX II


                                  FPAINT AUXILIARY FILE LISTINGS

                                                               




          Group.aux



          c---
          c  variable declarations

                integer*2 FirstFld, LastFld
                integer*2 Row, Col, CurField, TermKeys(30)
                integer*2 NumberOfFields
                integer*2 LastKey, FieldNumber
                logical*1 Next, Previous, Exit, Refresh, Valid

                character*  4 Version
                character*  9 Date
                character*  6 GroupID
                character*  3 Operator
                character* 65 Description(  3)
                integer*2 ScanRate
                character*  6 StageVelocity

          c---
          c Normal termination on F1 key
          c immediate termination on F2 key
                data TermKeys/ 1, 141, 1, 142, 26*0 /

          c---
          c Default variable initialization
                data Version /' '/
                data Date /' '/
                data GroupID /' '/
                data Operator /' '/
                data Description(1) /' '/
                data Description(2) /' '/
                data Description(3) /' '/
                data ScanRate /0/
                data StageVelocity /' '/

          c---
          c Screen origin
                data Row, Col / 1, 1 /

          c---
          c TTY initialization
                call TTYinit
                call EchoOff
                call KpdOn

          c---
          c Starting edit field

                                                               


                CurField = 1

          c---
          c Total number of screen parameters

                NumberOfFields =   9

          c---
          c Default limits

                FirstFld = 1
                LastFld = NumberOfFields


          c---
          c Clear the screen region

           10     call GROUPClear( Row, Col )

          c---
          c Display the Text fields

                call GROUPTextDsp( Row, Col )

          c---
          c Display the Data fields

                call GROUPDataDsp( Row, Col, FirstFld, LastFld
               1, Version, Date, GroupID, Operator, Description, ScanRate
               1, StageVelocity
               1 )


          c---
          c Edit the Data fields

           20     call GROUPEdit( Row, Col, FirstFld, LastFld, CurField, TermKeys
               1, Version, Date, GroupID, Operator, Description, ScanRate
               1, StageVelocity
               1, Next, Previous, Exit, Refresh, LastKey )



                if( Refresh ) then
                    goto 10
                else if( Next ) then
                    CurField = 1
                    goto 20
                else if( Previous ) then
                    CurField = NumberOfFields
                    goto 20
                else if( .not. Exit ) then

                                                               


                    goto 20
                end if


          c---
          c Validate the Data fields

                call GROUPValidate( FirstFld, LastFld
               1, Version, Date, GroupID, Operator, Description, ScanRate
               1, StageVelocity
               1, Valid, FieldNumber )

                if( .not. Valid ) then
                    CurField = FieldNumber
                    goto 20
                end if

                call TTYinit
                call EchoOn
                call KpdOff

                End

                                                               



          Spec.aux




          c---
          c  variable declarations

                integer*2 FirstFld, LastFld
                integer*2 Row, Col, CurField, TermKeys(30)
                integer*2 NumberOfFields
                integer*2 LastKey, FieldNumber
                logical*1 Next, Previous, Exit, Refresh, Valid

                character*  6 SpecimenID
                character* 12 Orientation

          c---
          c Normal termination on F1 key
          c immediate termination on F2 key
                data TermKeys/ 1, 141, 1, 142, 26*0 /

          c---
          c Default variable initialization
                data SpecimenID /' '/
                data Orientation /' '/

          c---
          c Screen origin
                data Row, Col / 1, 1 /

          c---
          c TTY initialization
                call TTYinit
                call EchoOff
                call KpdOn

          c---
          c Starting edit field
                CurField = 1

          c---
          c Total number of screen parameters

                NumberOfFields =   2

          c---
          c Default limits

                FirstFld = 1
                LastFld = NumberOfFields

                                                               




          c---
          c Clear the screen region

           10     call SpecClear( Row, Col )

          c---
          c Display the Text fields

                call SpecTextDsp( Row, Col )

          c---
          c Display the Data fields

                call SpecDataDsp( Row, Col, FirstFld, LastFld
               1, SpecimenID, Orientation
               1 )


          c---
          c Edit the Data fields

           20     call SpecEdit( Row, Col, FirstFld, LastFld, CurField, TermKeys
               1, SpecimenID, Orientation
               1, Next, Previous, Exit, Refresh, LastKey )



                if( Refresh ) then
                    goto 10
                else if( Next ) then
                    CurField = 1
                    goto 20
                else if( Previous ) then
                    CurField = NumberOfFields
                    goto 20
                else if( .not. Exit ) then
                    goto 20
                end if


          c---
          c Validate the Data fields

                call SpecValidate( FirstFld, LastFld
               1, SpecimenID, Orientation
               1, Valid, FieldNumber )

                if( .not. Valid ) then
                    CurField = FieldNumber
                    goto 20

                                                               


                end if

                call TTYinit
                call EchoOn
                call KpdOff

                End

                                                               






                                          APPENDIX III


                            NUMERIC CODES FOR FUNCTION AND KEY PAD KEYS

                                                               






                 KEY              NUMERIC CODE

                 Up Arrow            128
                 Down Arrow          129
                 Left Arrow          130
                 Right Arrow         131

                 PF1                 141
                 PF2                 142
                 PF3                 143
                 PF4                 144

                 Key Pad 0           157
                 Key Pad 1           158
                 Key Pad 2           159
                 Key Pad 3           160
                 Key Pad 4           161
                 Key Pad 5           162
                 Key Pad 6           163
                 Key Pad 7           164
                 Key Pad 8           165
                 Key Pad 9           166
                 Key Pad -           167
                 Key Pad ,           168        ( 8 for VAX version )
                 Key Pad .           169
                 Key Pad Enter       170

                 Back Tab            132          ( generated by ^X )
                 Del Char at Cursor  127                ( generated by Del or Backspace )
                 Del Char Backward     8                ( generated by Backspace or key pad , )



                For IBM PC

                Keypad Keys

                Insert              23  (^W)
                Delete             127  (Del)
                Home                 2  (^B)
                End                  5  (^E)
                PgUp               133
                PgDn               134


                Function Keys   Un-Shifted      Shifted

                F1                 141            151

                                                               


                F2                 142            152
                F3                 143            153
                F4                 144            154
                F5                 145            155
                F6                 146            156
                F7                 147            157
                F8                 148            158
                F9                 149            159
                F10                150            160

                                                               






                                          APPENDIX IV


                                          USEFUL ROUTINES