VT3xx Font Editor











Michael N. LeVine
Code 3514
Naval Weapons Center
China Lake
Ca 93555
(619)939-3970
 avn 437-3970


	This package consists of the following parts:

FONT.FOR	Source file

SMG.FOR		Include file
FONTDEF.FOR	Include file

*.200		Font data files in VT200 format(a previous font editor I 
		submitted to the Sig tapes)

*.dat		Font data files in VT3xx format

KEYBOARD.COM	Displays keyboard with the current font key positions
WRITE.COM	Displays all printable characters in the current font

*.COM		Font down-load command files generated by FONT



	The VT3xx Font Editor is generated as follows:

$ FOR FONT	! The directory must contain all the .FOR files shown above
$ LINK FONT

NO special priv's are required to use this program.


	Running the VT3xx Font Editor


The font editor uses the screen management functions and is menu driven.
As much a possible, all commands or requests for additional data is self
explanatory and with the exception of some prompts, most commands
are one or two keystrokes with no <CR> required.


$ RUN FONT
		Brings up the main menu with the following options

1	Init Data Structures
		Initializes all internal data structures - any information
		currently stored there is lost. When selected the editor
		will ask if you really mean it-only a "Y" will cause the
		Init to be done(no <CR> required, otherwise the editor
		will just wait for the next main menu command.

2	Read font data file
		Reads in a VT3xx font data file. First prompts for the
		name of the data file (default extension is ".DAT"),
		then while reading in the data file displays at the 
		bottom of the screen the message:
		"Bell will sound on any error"
		When the message disappears- the read is complete.
		If the bell sounds-the contents are unknown.

3	Convert VT200 data file
		Reads in a VT200 font data file. First prompts for the
		name of the data file (default extension is ".200"),
		then asks if you want the file converted to an equivalent
		VT300 format (Cell width 7 pixels, cell height 20 pixels)
		and expects an answer of "Y" to do so, otherwise uses the
		VT3xx hardware emulation values for VT200 fonts,
		then while reading in the data file displays at the 
		bottom of the screen the message:
		"Bell will sound on any error"
		When the message disappears- the read is complete.
		If the bell sounds-the contents are unknown.

4	Write font data file
		Writes the current font in memory to a disk file in
		VT3xx format. The program will then as for the name of
		the file to be written (default extension is ".DAT"),
		then while writing into the data file displays at the 
		bottom of the screen the message:
		"Bell will sound on any error"
		When the message disappears- the write is complete.
		If the bell sounds-an error occurred during the write an
		no file is generated.

5	Edit font parameters
		Puts the user in to the font parameters edit sub-menu.
		See special section on this selection for a full description
		of options.
6	Edit font character
		Puts the user in to the font character edit sub-menu.
		See special section on this selection for a full description
		of options.
7	Build font download .COM file
		Writes a command file that when executed will download
		to the terminal the font currently defined in the font
		editor. The user is prompted at the bottom of the screen
		for the name of the file to be generated (default extension
		is ".COM").
		While writing into the command file displays at the 
		bottom of the screen the message:
		"Bell will sound on any error"
		When the message disappears- the write is complete.
		If the bell sounds-an error occurred during the write an
		no file is generated.

8	Exit
		Exit from the font editor (also ^Z), prompts the user
		at the bottom of the screen to be sure he really wants to.
		An answer of "Y" will cause an exit, all others will
		return back to the main menu for the next command.

9	Special Functions
		Puts the user into the special functions sub-menu.
		See special section on this selection for a full description
		of options.




	To select an action from the main menu-just enter the digit (1-9)
corresponding to the menu item you want to execute-no <CR> required.

	The user is expected to have read the Programmers Reference Manual
for his terminal with special attention to the generation of soft character
sets.


		Editing Font Parameters

	The following font wide parameters are available for the user to
modify:

Font Number
Font name
Cell width
Font Width
Text cell
Cell Height
Character Set

	The user selects the number corresponding to the parameter
to be changed (if the setting of that parameter cannot be changed because
of a dependence on another parameter, the bell will sound). A short
description of the parameter options is show on the lower half of the
screen and the user is prompted for the new setting. If the setting is
not valid due to conflict with another parameter- the bell will sound
and the change will not be made. Note that my restrictions are not quite
the same as those outlined in the PRM, for all 80 col fonts can be
up to 10 pixels wide whether text cell or full cell, and the 132 col
fonts are limited to 6 pixels wide (but in the character edit mode,
the text cells are show one pixel col narrower than selected).



		Editing Font Character

	When invoked, the character editor function will prompt form
the character number, this is 0-95 for 96 character fonts or 1-94 for
94 character fonts (character 0 is SPACE and 95 is DELETE). Note that 
a 2 character response is expected so if a single digit number is entered
then end with a <CR> or input as either <zero><digit> or <space><digit>

	The character edit sub menu comes up with the double high/wide
name at the top followed by a list showing the character number,
equivalent ascii character, equivalent ascii character value in hex
and then a list of all the editing commands. On  the right hand side
of the screen is a box the size of the character cell as defined in
the font parameters (full width if a full cell or one pixel less if
a text cell) which show the character being edited.
	If this is being run on a REGIS terminal, then the following is
also displayed-on the same line as the HIGH-WIDE title is both the 
equivalent ascii character and the character as currently defined
(also in HIGH-WIDE format). Next to the line showing the equivalent
ascii character the character being edited is also displayed at its
exact size.

	All the commands recognized by the character editor are show in
the lower left hand section of the screen and are for the most part self
explanatory. The two that might not be are the B and O commands. Both will
prompt for and read in another VT3xx font definition file and then prompt
for a character number. The B command will .OR. in the selected character
into the character being edited, and the O command will replace the
character being edited with the selected character from the selected
font definition file.


		Special Functions

	This sub-menu is used for special font manipulation that
do not fit elsewhere.

A	Convert 80 col font to 132 col font
		requires that the 80 col font be 10 pixels wide, and 
		generates a 132 (6 pixel wide) font by using every other
		pixel column form the 80 column font. The user is prompted
		as to whether to use the even or odd numbered pixel col's.

B	Create a random bit font
		Self explanatory

C	Create all bits set font
		Self explanatory

D	Reverse characters in font
		All the characters is the font are now their mirror image,
		depending on how you answer the prompt, it will be either
		top to bottom or left to right.