CONTENTS



CHAPTER 1       INTRODUCTION


CHAPTER 2       INTERACTIVE ETHERNET MONITOR

        2.1     MONITOR MODES  . . . . . . . . . . . . . . . . . . 2-1
        2.1.1     Ethernet Protocol Mode . . . . . . . . . . . . . 2-1
        2.1.2     Ethernet Map Mode  . . . . . . . . . . . . . . . 2-1
        2.1.3     Ethernet Trace Mode  . . . . . . . . . . . . . . 2-2
        2.2     INTERACTIVE ETHERNET MONITOR COMMANDS  . . . . . . 2-2


CHAPTER 3       ETHERNET MAINTENANCE MODULE

        3.1     OVERVIEW . . . . . . . . . . . . . . . . . . . . . 3-1


CHAPTER 4       ETHERNET LISTENER AND REPORTER MODULE

        4.1     OVERVIEW . . . . . . . . . . . . . . . . . . . . . 4-1


APPENDIX A      INSTALLING ETHERNET MONITOR


APPENDIX B      FILE FORMATS


APPENDIX C      CAVEAT EMPTOR


APPENDIX D      STATUS LINES




















                                      1













                              CHAPTER 1

                             INTRODUCTION



     Emonitor is a collection of ethernet  monitor  programs  used  to
identify  and  monitor ethernet devices on an ethernet network.  It is
composed of the following modules:

      *  Ethernet Monitor
         The  interactive   ethernet   monitoring   program   provides
         statistics  by protocol, displays device address and optional
         node names (when  entered  via  the  maintenance  module)  of
         devices sensed on the network, and traces packets to and from
         a selected device.  Also able to  dump  ethernet  packets  to
         EMON_DIR:ETHERNET_DUMP.DAT.

      *  Ethernet Listener
         Collects   statistics   to   EMON_DIR:ETHERNET_COUNTS.DAT for
         processing  by  report  module.   Packet counts are dumped at
         selected interval.

      *  Ethernet Reporter
         Produces reports from EMON_DIR:ETHERNET_COUNTS.DAT.

      *  Ethernet Maintenance
         Ability to list and modify contents of monitor  protocol  and
         device data files.


















                                     1-1













                              CHAPTER 2

                     INTERACTIVE ETHERNET MONITOR



2.1  MONITOR MODES

     The interactive ethernet monitor provides a means  of  monitoring
ethernet  traffic  on  the fly.  This program has three screen modes -
Protocol, Map, and Trace.



2.1.1  Ethernet Protocol Mode

     When first invoked via  the  EMONITOR  command,  the  process  is
displaying  ethernet  statistics  by  protocol.  This mode can also be
selected by typing a "P" when in any  of  the  other  modes.   As  new
protocols  are detected by the program, they are added to the protocol
data file (EMON_DIR:ETERNET$PROTOCOLS.DAT) and displayed at the bottom
of the current screen list.  When they are added they are given a name
of "Unknown Protocol", you may change this by invoking the maintenance
module  by  typing "EMON/MAINTENANCE" at the DCL command prompt.  Each
time the program is entered, these protocols are sorted into ascending
protocol id order.  If you wish to monitor a specific protocol, simply
select the desired protocol by using the up and down arrow keys.  This
will  cause  the  packet  grabber  routine to discard all packets with
protocols different than that selected.  You will also note  that  the
counters will be reset.



2.1.2  Ethernet Map Mode

     The map screen is selected by typing "M" when in the  interactive
monitor.   This  will  draw an ethernet map (schematic representation)
with the various detected ethernet devices listed.  As new devices are
sensed,  they  will  be  added  to  the  device  data  file  found  in
EMON_DIR:ETERNET$DEVICES.DAT and displayed at the bottom of the current
screen  list.   When  devices are added automagically they are given a
name equal to the ethernet address.  You should/could change  this  to





                                     2-1


                         INTERACTIVE ETHERNET MONITOR


the  node  name  by  invoking  the  maintenance module.  Each time the
program is entered known devices are  displayed  in  ascending  device
name  order.   If  you  wish  to monitor a specific device, select the
desired device by using the up and down arrow keys.  This  will  cause
the  packet  grabber  routine  to  discard  all packets with source or
target addresses not equal to the selected device.  Counters will also
be  reset.   You can have a selected device and a selected protocol at
the same time.



2.1.3  Ethernet Trace Mode

     The trace mode is selected by typing "T".  The  trace  screen  is
useful  for  determining  traffic flow by node address.  If there is a
selected device, the trace mode will only track packets  sent  between
the selected device and communicating nodes.



2.2  INTERACTIVE ETHERNET MONITOR COMMANDS

     Ethernet packets can be viewed for analysis by typeing  "D"  when
in  any  of  the  monitor  screen  modes.   This toggles the option of
dumping ethernet packets to EMON_DIR:ETHERNET_DUMP.DAT on and off. This
file is a collection of raw ethernet packets each of which is preceded
by a time stamp record.  For analyzing formatted packets use  the  VMS
dump utility on this file, i.e.:

        DUMP/RECORD EMON_DIR:ETHERNET_DUMP.DAT


























                                     2-2













                              CHAPTER 3

                     ETHERNET MAINTENANCE MODULE



3.1  OVERVIEW

     The Ethernet maintenance module  is  used  to  modify  or  delete
records  contained  in  the protocol and device files.  This module is
invoked by typing "EMONITOR/MAINTENANCE" at the dcl prompt.




































                                     3-1













                              CHAPTER 4

                ETHERNET LISTENER AND REPORTER MODULE



4.1  OVERVIEW

     The Ethernet Listener is used to collect summary statistics based
on protocol type, source address, and/or target address.  The listener
is invoked by typing "EMON/RECORD" at the dcl prompt.  Output  can  be
directed  to  a  file  of  your  choice by using the /OUTPUT qualifier
(default is EMON_DIR:ETHERNET_COUNTS.DAT).  The default interval of  5
minutes  can  be  modified  by supplying a delta time to the /INTERVAL
qualifier.  Once the data  file  has  been  created,  reports  can  be
generated by typing EMON/REPORT at the dcl prompt.































                                     4-1













                              APPENDIX A

                     INSTALLING ETHERNET MONITOR



     The ethernet monitor needs to reside in a directory pointed to by
the logical EMON_DIR. The program must be run from an account with the
PHYIO privilege and write access to the EMON_DIR directory.   Copy the
executable files into this directory along with the cld file.  Execute
the following commands and you're off!

    $ define emon_dir   disk1:[systems.source.emon]
    $ set command emon_dir:ethernet_monitor

     As the programs  execute,  the  device  and  protocol  files  are
updated as new devices and protocols are sensed.






























                                     A-1













                              APPENDIX B

                             FILE FORMATS




                        ETHERNET_PROTOCOLS.DAT

        Field           Type                    Remarks
    protocol_type       2 char                  key 0
    protocol_name       25 char                 key 1


                        ETHERNET_DEVICES.DAT

        Field           Type                    Remarks
    ethernet_address    6 char                  key 0 
    node_name           12 char                 key 1
    node_type           byte                    0 = terminal_server
                                                1 = host
                                                2 = unknown
    remarks             80 char                 Currently not used
























                                     B-1


                                 FILE FORMATS


                        ETHERNET_COUNTS.DAT

Time Stamp record:

        Field           Type                    Remarks
    record_type         byte = 0
    time_stamp          quadword system time
    active              longword integer        Active counters for current interval
    counters            longword integer        Total counters for session


Counter Record:

        Field           Type                    Remarks
    record_type         byte = 1
    destination         6 char
    source              6 char
    protocol            2 char
    packet_count        integer
    byte_count          integer




































                                     B-2













                              APPENDIX C

                            CAVEAT EMPTOR



     In order to monitor ethernet  traffic,  the  ethernet  controller
must  be  kicked  into promiscuous mode.  This makes the computer work
much harder than would ordinarily  be  necessary  since  it  must  now
handle   every   packet   going  down  the  line  instead  of  packets
specifically targeted to that controller.  Ethernet  is  a  relatively
fast  channel,  and  a  busy  ethernet  can  keep the cpu busy.  IT IS
IMPORTANT TO UNDERSTAND THE RESOURCE REQUIREMENTS OF  THIS  SYSTEM  IN
ORDER  TO  GUARANTEE  MEANINGFUL  STATISTICS.   Ethernet  packets  are
collected by an asynchronous  routine  and  stuffed  into  a  circular
buffer  list.   To  prevent  this  list  from overflowing, the list is
trimmed if the current buffer count exceeds a threshold (reflected  by
discarded  packets  on  the  status  line).   Keep an eye on discarded
buffers!  Most likely, your cpu is not able to handle traffic, process
priority is insufficient (in which case you may not even catch all the
packets) or packet dumping to disk is too costly.  To prevent the  ast
routine  effectively  locking out the program, sampling is disabled if
the discarded packets exceed a threshold.

           This software works best with a VT200 or VT300.






















                                     C-1













                              APPENDIX D

                             STATUS LINES





                         Ethernet Counters Status Line

        BRC     Bytes Received
        DBR     Packets Received
        MBY     Mulitcast Bytes Received
        MBL     Multicast Packets Received
        RFL     Packets in Error
        OVR     Lost - Internal Buffer Errors
        LBE     Lost - Local Buffer Errors
        BSN     Bytes Transmitted
        DBS     Packets Transmitted
        MSN     Multicast Bytes Transmitted
        MBS     Multicast Packets Transmitted
        BID     Packets Deferred
        SFL     Packets Aborted
        BSM     Packets with Several Errors
        BS1     Packets with Single Error
        CDC     Collision Check Errors
        UFD     Unrecognized Frame Destination




















                                     D-1