VD: and FD: Drivers - Virtual Disks for VMS

 VDDRIVER (V4)

It sometimes happens that a VMS system would like to have its online
storage broken up into disk volumes differently than the physical disks
available. This happens for a variety of reasons.
	Sometimes, it is desired to have different cluster factors for
different groups. Sometimes, volume ACLs can provide security desired
to protect some data where the alternative (ACLs on directories and all
files) is unduly slow. Sometimes, command files from a vendor will modify
a volume and it is desired to have a clean disk to turn these command
file loose on, rather than risking one's system. Again, sometimes it's
easier to turn management of a disk volume over to a group of users
rather than play political games over quotas. Finally, at times file
structures other than ODS-2 may be wanted.
	These are a few of the reasons for splitting storage.
	VMS makes an attempt to allow merging of disks (volume sets), and
the rooted directories and quotas give some ALMOST virtual volume
support. Sometimes, though, there's nothing like the real thing.
	The VD: driver is designed to be a fast, high performance driver
that allows a CONTIGUOUS file on any VMS volume to appear to the rest
of VMS to be a separate disk. The file may be created with any convenient
utility, provided only that it be contiguous. A privileged image then
"connects" a unit of the VD: device to the file and allows it to be
used. Once connected, a VD: unit can be INITed, MOUNted, read from,
written to, or whatever, exactly like a real disk hanging on a local
bus on the VAX.
	VDDRIVER operates by "editing" I/O Request Packets (IRPs) and
passing them off to a "host" driver, which is the driver of the disk
on which the contiguous file exists. It regains control by means of a
VMS hook so that split I/O's (for virtual I/O where a request spans
more than one region of disk) and the like can be handled correctly and
then terminates the IRP. As a result, VDDRIVER's overhead is very low.
	VDDRIVER has several limitations in this "initial cut" version.
First, it has a single physical structure which forces its disks to be
a multiple of 64 bytes long. Most of VDDRIVER doesn't care about disk
physical structure, but this was an adequate initial solution.

	(note: a program that assumes things about disk
	physical structure can be fooled by this
	geometry. Analyze/disk may be in this class. If
	it bothers you, edit the source and provide only
	32 sectors/track like DEC drives and use the FD1
	device type instead of RP06.)

Second, VDDRIVER's control image does not provide any ability to create
the container file and is minimal in error reporting. (For example, if
the container file is not contiguous, it silently refuses to enable the
VD: unit.) Third, VDDRIVER does NOT track files used in any continuing
way. That is, the file is not locked, and there is no online indication
of what file is connected to what VD: unit (other than the start block
number and size in the VD: UCB). If the container file is deleted and
VD: continues to be used, this can result in corruption of any part
of the host disk that is allocated over the container file's old space.
(This is similar in concept to what happens when you delete a page file
on a running system and then write onto the system disk.)

	(note: A version of VDDRIVER that keeps track of
	the filenames assigned, and of its
	assign/deassign utility, are provided.)

	Further, some possibilities of VDDRIVER are not realized. The most
obviously useful is shadowing. It is clearly fairly easy to have VDDRIVER
send the IRP to two files for writes (one after the other) before completing
it, and easy to have reads alternate between two files if so desired.
This would allow a virtual disk to shadow only the data one NEEDED to shadow,
not necessarily an entire volume. (This is essentially the sort of thing
shadowing now does, but buried inside DEC drivers. VDDRIVER would allow
it to be done controllably. (Also free.))
	VDDRIVER (use version 4 please!) is offered as a useful and
handy piece of code as is, in the hope also there will be added abilities
provided by others as needed.


	Using VD:

	To use VD:, you first assemble and link it in the standard way for
VMS drivers; the VDMAKE.COM file in fact is an outline of this procedure.
You must also assemble and link ASNVD, the privileged image that associates
VD: units with contiguous files. (It must be linked with the system symbol
table also.)
	Now you load the VDDRIVER you've built. For example, with one
unit you'd use a command to SYSGEN like
  CONNECT VDA0:/NOADAPTER/MAXUNITS=1/DRIVER=VDDRIVER3C.EXE
(assuming that the driver executable filename is sys$system:vddriver3c.exe;
alter the command if the filename is different.)

Make sure you've assembled VDDRIVER for at least as many units as you
want; there's a table internally that must be long enough. The default
max is 8 units unless you edit the source.

	Now you have one or more VD: units, but they're offline and
not yet usable. So now
	set command ASNVD
to set up the ASNVD command. Make sure the IMAGE statement in ASNVD.CLD
matches where the ASNVD.EXE image is.
	If this is the first time thru, create a contiguous file somewhere
(let's say it's DF0:[DISKCONT]MYVD.DSK for the purposes of illustration).
	Now issue the command
ADVD/ASSIGN VD0: DF0:[DISKCONT]MYVD.DSK

	Now you'll notice that VD0: is online and enabled. (If it isn't,
check the file; if it isn't contiguous, the ADVD command will NOT have
enabled the VD: unit.)

If this is the first time through, INITialize the disk:
  INIT/STRUCT=2/CLUSTER=1 VD0: VDVOL
(where you can pick structure, cluster factor and volume label to be
whatever you want, of course.)

INIT may complain there is no badblock information. This is not a problem.

  Now you can mount the device and use it

MOUNT/SYSTEM VDA0: VDVOL
   (or the like)
and VD0: will act like any other volume on your system.

NOTE: Be SURE you have enough XQP cache (Sysgen ACP* parameters)!!!
Some versions of VMS cause strange & wonderful (?) corruption errors
where they run on very low XQP cache amounts.

	FDDRV

	FDDRV is an attempt to increase the flexibility of VMS storage
and solve some remote backup problems. Like VDDRIVER, it's a virtual disk.
UNLIKE VDDRIVER, FDDRV does its' actual I/O via a complete PROCESS.
As such, it looks like a disk to its' "clients", and sends all requests
for I/O to a "host" PROCESS. This is a normal (but privileged) VMS program
able to use all VMS services. It allows things like remote virtual disks
over any network, memory virtual disks (using the process' memory),
cryptodisks, compressing disks, and other novelties.
	The remote backup problem is fairly pervasive in VMS sites
including ours. I wanted to devise a way to remote mount a disk (since the
disk problem is easier to solve than tape) but didn't want to depend on
any internal DECnet interfaces. As a result, I decided to build a virtual 
disk driver that would notify a VMS process when it had work, and send
bytes TO the process to write them or get them FROM the process to read
them, allowing the process to handle the actual storage. The idea was that
a VMS process can do things like talk DECnet fairly easily, where doing
it from a driver could be quite complex and hard to debug. Since I knew
that FDT processes are handled in the process context and don't need to
be queued to the driver's start-IO, I figured these could be used to
communicate with the "busy" driver during the time the client process was
doing "disk" I/O.
	To handle data passage, I built buffers right into the driver
and used some existing code (from John Osudar's memory driver) to move
data between the client process and the driver buffers. This was easier
than allocating nonpaged pool (and guaranteed that space was available),
and I set up the maxbytecount field of the UCB so that no transfers
would be too large for the buffer. There are some special FDT routines
provided to move data between the "host" process and the driver. These
are handled at IPL 2 (ASTDEL) and so can pagefault. The one tricky
part of the driver was where the host process terminates the client's
I/O packet (IRP). That I/O must terminate two IRPs, the client's and
the host's. I added a great deal of UCB field save/restore code there and
had to play some games with priorities to get things synchronized right.
Notifying the host process was rather easier, since there's a documented
call to write data to a mailbox. The host process creates the mailbox
and tells the driver where it is in a setup call. Alternatively I could
have used a call to set local event flag 10 in the host process, but
the mailbox call appeared cleaner. The EF 10 code is in the driver but
commented out in case anyone wants to use it. Unfortunately the mailbox
must be world writeable to be usable here; the EF 10 code is more secure
but may have undesirable side effects in a multiprocessor.

	FDDRV requires a privileged image, just as VDDRIVER does. Unlike
VDDRIVER, though, where the privileged image does some setup and goes
away, in FDDRV, the privileged image must stay around. It not only
does the setup of the device, associating it with storage, but it also
handles the storage itself. Therefore, an FDDRV unit MUST have a VMS
process in being to handle it while it is online. In fact, some code
in FDDRV will take the unit offline if communication with its' host
process fails. (It will attempt to clean out any outstanding I/O at
that time also.)

	To debug FDDRV, I used a "host" process that just had a large
internal array of memory which acted as a disk. This had the advantage
that it couldn't mess up any on-disk filestructures and left no
undesirable traces of hangs or crashes during debugging. However, I realized
that such a thing is useful in itself. It is a memory disk, but memory
is user-mode pageable memory and can be as large as the virtual address
space of a process. Therefore this host is supplied. It may be preferable
to "memory disk" drivers whose storage is all in nonpaged pool since
storage can conveniently be much larger, though performance will be less due
to the need for extra QIO requests to communicate between driver and host
process.
	Another host supplied communicates over DECnet with a "remote
host" process. This remote host must be installed as a DECnet known
object and have LOG_IO privilege. Its host process then opens a DECnet
circuit to the remote object and the two exchange data. This implements
the remote mounted virtual disk originally desired. The DECnet circuit is
opened on the host end by some Fortran subroutines, and the remote host
is entirely Fortran. Again, the failure of communications will have the
effect of taking the device offline.
	Several other host processes are supplied. These include "file"
disks, where the storage is on a container file somewhere on your
system (or on another system over DECnet if you like), "crypto" disks
which encrypt all data they store; storage is on a normal file. These
files do NOT have to be contiguous. There's code for a remote disk over
asynchronous lines (can you say SLOW? SURE you can!). There's also
something called the Bat Out of Hell disk, which is a file disk backed
by a memory disk; it's an attempt at a cheap cached disk which can be
faster than a file disk if mostly reads are done. See AAAREADME.2nd for
info on what file does what.

	These host programs all use CLI callbacks, and as a result must
be started from processes that contain DCL. Therefore, a run/detach or
equivalent should be done with the image being LOGINOUT (to get DCL into
the process) and with commands to SET COMMAND FDHOST and then an FDHOST
command to connect to a unit of FD: (e.g., FDHOST FDA0:). Some logical
names are needed for the network remote virtual disk to set up the
cross-DECnet links; the remote DECnet object number and nodename have to
be set up this way (as things are now written; other means of getting
this information could of course be used.) The remote host program also
needs a logical defined to tell it the disk name to use, though it does
not have to contain DCL in its' process. These details are due to the
history of the FDHOSTxxx programs, all being derived from ASNVD. 

	Usage:

	First, note that some tables inside FDDRV set the max.
number of units and max. buffer size permitted in the driver. These
should be no larger than needed due to the space they occupy.
  You assemble and link FDDRV as for a normal VMS driver and load it
much as you load VDDRIVER. This must be done before firing up FDHOSTxxx.

	Two hosts have been defined to date. FDHOSTMEM.MAR implements
a "memory disk" in the host's virtual memory. Size is defined by some
assembly-time parameters (defining number of "cylinders"). To run it, a
process must SET COMMAND FDHOST and then issue a command like
FDHOST FDA0:
which will start the connection up. The fd: drive will then be 
available so long as the FDHOST image is running and may be INITed,
MOUNTed, and used as a normal disk. Since the disk is created empty
every time, the INIT and MOUNT steps must be taken every time.

	Another host, FDHOSTREMOT.MAR, works with a server on a remote
system connected by DECnet. The server part of the code is FDREMSRV.FOR
here, and subroutines in FDREMSUB.FOR must be linked with FDHOSTREMOT.
This server is started like the memory server, but MUST have some
logicals defined for it before it can do anything. On the system with
FDREMSRV, the FDREMSRV image must be installed as a DECnet object first,
and the logical name FDRDSK must be defined for it to point to the disk
that will be "remoted". In addition, the logical name NOWRIT may be
defined. If it is, the FDREMSRV image will never write to the disk, but
will allow read accesses to succeed. (It will pretend writes worked, but
not actually do them.)  Then, the FDHOSTREMOT/FDREMSUB image must be
started with logical names predefined for FDNODE, the nodename of the
system running FDREMSRV, and FDOBJ, the DECnet object number of the
FDREMSRV image as installed. These are used to open a DECnet circuit to
the server, after which it obtains the physical characteristics of the
disk it is "remoting" (using $GETDVIW) and sends them to the node with
the FDDRV unit active, setting the FD: unit geometry to be the same as
that of the remote-accessed disk. The two images then enter a continuous
dialogue that accomplishes the remote data transfer.

Example setups:

ASSIGN/SYS 1 NOWRITE	! Prevents writing by FDDRV on remote
NCP SET OBJECT FDREMSRV number 0 file sys$system:fdremsrv priv log_io -
  USER username PASSWORD password  ! must be a priv'd acct or install the
				   ! image with privs.
ASSIGN/SYS FDREMSRV FDOBJ
ASSIGN/SYS MYNODE FDNODE	! note no ::
ASSIGN/SYS vda0: FDRDSK

  The DECnet object name should be a task type object (number 0) but
should have its own name in this way. You may need to create a file
FDREMSRV.COM or the analogue. Make sure the images are world readable.


	Other images are planned for remote access. In particular, at our
site we have a Pro 350 with RX50 disks and some IBM ATs. By defining an
asynchronous access protocol of fairly simple design, it should be rather
easy to concoct remote hosts that allow FD: units on our VAX to appear
to be 1.2MB RX33 type disks (the 1.2MB drive on an AT) or RX50 drives
local to the VAX, even though they are foreign mounted floppies on the
PRO 350. By "remoting" a virtual disk on our larger VAX and making it
appear to be local on our uV2000, I will also be able to back up from the
TK50 on the microvax to disks on our larger VAX system, giving access to
yet another peripheral. This technique will also allow much simpler use
of peripherals from anywhere on the internal DECnet, not requiring large
scratch storage on the systems whose peripherals I use, since their only
local needs will be for sufficient storage to run FDDRV and a remote
host program talking to my home system and a virtual disk (type VD:)
thereon. (I'd use a VD: type disk due to its efficiency.)
	Obviously, the FDDRV system is NOT a high efficiency mechanism
since data must be transferred from client to driver, from driver to
host, and from host possibly to other remote host, with several context
switches along the way. Even so, it IS very flexible. Because storage is
managed by PROCESSES, any network protocol can be added if a user mode
process can use it; no further VMS hooks are required. Nor is FDDRV
internally very sensitive to VMS modifications; most of its interfaces
are documented, and the rest have been mostly stable for many VMS
versions. A process can do a great deal that a driver alone would have
difficulty with. Consider: suppose one wants a compressing disk.
Subroutines to compress data are not hard to get. A host process that had
compress/decompress routines in it might make an ISAM file, indexed by
block, of compressed data records, allowing a slow-access but smaller
disk to hold information. In fact, it might be designed NOT to compress
the first "n" blocks of the disk, and initialized with /INDEX=BEGINNING
so that the index file would NOT be subject to compress/decompress
delays. Such a system might be quite useful for archival information.
If one wanted a crypto-disk, a host that asked for a decryption key
might be implemented which opens an ISAM file and encrypts all that is
written to it, or decrypts all that is read from it. If the host process
is a spawned process, VMS itself will have no access to the clear text
when the host is not present, and the exiting of the main process will
automatically clear out the spawned process. One assumes such a disk
would be mounted privately of course. Many other possibilities will occur
to the imaginative.

	You should notice that because FDDRV uses a host process, the host
can very easily be made to do catch-up copying of a container file to
another container file without allowing interruptions by other access.
Shadowing becomes trivial here: instead of writing data out once, write it
out twice, to two container files. There is beauty in being able to do shadowing
without having to write even one line of kernel mode code! It's not clear
that performance gains would be available by doing this, of course, but some
applications of shadowing don't have that much to do with performance.

	Commercial Comparable Code

	This system lacks much of the polish of a commercial system like
the Bear Systems MD: driver, which works VERY well. In particular, file
creation, flexible virtual device geometry control, and additional access
controls are all missing. Bear's product already has shadowing of virtual
disks also. In addition, the Bear product contains logic for driver
enforced device ACLs and mousetraps. These are much more powerful for
security enforcement than using VMS ACLs, since a privileged VMS user can
avoid VMS ACLs and generally will know how to do this. Unless he is very
familiar with the Bear product, he will not know what their ACLs do, and
there is no supplied quick way to bypass driver ACLs in their system
which would compare with the ease of setting BYPASS privs in VMS. Such a
system could be added to VD: or FD:, of course, but there is no provision
for it at present and it would require a nontrivial code addition to
implement. The VD: and FD: drivers are designed to run reliably and well
but are weak in error reporting and niceties. Thus, for example, while
ASNVD will not allow a VD: unit to be assigned to a noncontiguous file,
it will also not tell what went wrong. Nor has it any provision for
setting VD: geometry nor for creating contiguous container files. Nor has
it any provision for reporting files used as containers, or locking files
that are in use. What these devices DO have is the ability to give
virtual disk services and to perform the functions other VMS commands
dont' provide. Given reasonable care in their use (for example, as in
protecting container files for VD: units from accidental deletion) you
can use virtual disks to significantly increase system flexibility. And
of course you have complete sources, which allow you to add functions or
maintain the software indefinitely.
	The drivers here are also much more conservatively written than
the Bear driver. By splitting the VD: and FD: functions into two drivers,
and by buffering data in the FD: driver itself, I avoid many complexities
in the code. The Bear driver avoids most (possibly all) double copying of
data and multiple context switches; these are unavoidable in the FDDRV / 
FDHOST system presented here. VDDRIVER is so simple it is as efficient as
possible already, but VD: and FD: drivers do not attempt to lock their
containers. Also, the Bear driver keeps track of the host process where
FDDRV does not. (That's why fdhost/clear exists, to clean up the bit of
residual status in an FD: unit.) 
	In terms of features, the sets of drivers are comparable. Some
unique features apply to each, too. If you start using memory or file
disks, cryptodisks, or the like, you may find that the Bear product
will be easier to use than these, and occupy less CPU resources. For
sites where this doesn't matter, the VD:/FD: driver suites provide some
useful capabilities which can be readily extended.