The VT340 Mouse: An Introduction
    
This file features code previously published in the October 1989 issue of
VAX Professional magazine. It was published as part of an article written
by Kevin Crittenden and Michael Dunn titled, "The VT340 Mouse: An
Introduction.:" The article appears on page 6. The code, titled READ_BUFFER
by the authors, reads the terminal's input buffer using the system service
routine $QIOW, then passes the input back to the calling routine.
    
************************************************************************
*  Use these procedures at your own risk. Professional Press is not    *
*  liable for any damage that these utilities might do to your system. *
************************************************************************


        SUBROUTINE READ_BUFFER ( INPUT_CHANNEL,CINPUT)
C************************************************************************
C*                                                                      *
C*                              READ_BUFFER                             *
C*                                                                      *
C*              Read the terminal's input buffer using the system        *
C*      service routine $QIOW. Pass the input back to the calling       *
C*      routine.                                                        *
C*              The terminal's input channel is passed into this        *
C*      routine.                                                        *
C*                                                                      *
C************************************************************************

        INCLUDE '($IODEF)'              ! I/O definitions

        INTEGER*2 INPUT_CHANNEL         ! channel assigned to the terminal
        INTEGER*2 INPUT_BUFFER_SIZE     ! size of buffer to receive data

        INTEGER*4 STATUS                ! return status of QIOW
        INTEGER*4 OPCODE                ! modifiers for read operation
        INTEGER*4 SYS$QIOW              ! QIOW system service

        CHARACTER*(*) CINPUT            ! input buffer

        STRUCTURE /IOSTAT_BLOCK/
                INTEGER*2 IO_STATUS     ! return status I/O operation
                INTEGER*2 TERM_OFFSET   ! number of characters before the
                                        ! terminator
                INTEGER*2 TERMINATOR    ! value of terminator
                INTEGER*2 TERM_SIZE     ! size of terminator string
        END STRUCTURE

        RECORD /IOSTAT_BLOCK/ IOSTAT

C************************************************************************

C       -- length of buffer to receive data
        INPUT_BUFFER_SIZE = LEN(CINPUT)

C       -- QIOW function codes
C          IO$READVBLK - read virtual block
C          IO$M_ESCAPE - allow escape sequences to be recognized as valid
C                        delimiters

        OPCODE = IO$_READVBLK .OR. IO$M_ESCAPE

C       -- fill the input buffer with blanks. Read the terminals input
C          buffer for data.
        CINPUT = ' '
        STATUS = SYS$QIOW ( ,%VAL(INPUT_CHANNEL),
     1                       %VAL(OPCODE),
     2                       IOSTAT,,,
     3                       %REF(CINPUT),
     4                       %VAL(INPUT_BUFFER_SIZE),,,,,)

C       -- check QIOW status
        IF ( .NOT. STATUS) CALL LIB$SIGNAL ( %VAL(STATUS))
C       -- check status of I/O operation
        IF ( .NOT. IOSTAT.IO_STATUS)
     1                          CALL LIB$SIGNAL ( %VAL(IOSTAT.IO_STATUS))

        RETURN ! * from READ_BUFFER *
        END

=




        SUBROUTINE SET_MOUSE_BUTTONS ( IOPTION)
C************************************************************************
C*                                                                      *
C*                        SET_MOUSE_BUTTONS                             *
C*                                                                      *
C*      Set up mouse buttons according to the following values of       *
C*      IOPTION:                                                        *
C*              1 = Send reports only when buttons are pressed          *
C*              2 = Send reports only when buttons are released         *
C*              3 = Send reports when buttons are pressed or released   *
C*                                                                      *
C*      The DECLBD device control string looks like the following:      *
C*              ESC P Pc $ w Key1/Down1/Up1;...;Keyn/Downn/Upn ESC \    *
C*                                                                      *
C************************************************************************

        INTEGER*2 IOPTION               ! mouse button option desired

        CHARACTER*90 CPRI_REQUEST       ! holds the DECLBD device control
                                        ! string

C************************************************************************

        CPRI_REQUEST(1:1) = CHAR(27)    ! escape character
        CPRI_REQUEST(2:) = 'P1$w'       ! clear one button at a time

C       -- define for buttons pressed only
        IF ( IOPTION .EQ. 1) THEN
        CPRI_REQUEST(6:) =  '1/1B5B3234317E/;'   ! ESC[241~
        CPRI_REQUEST(22:) = '2/1B5B3234337E/;'   ! ESC[243~
        CPRI_REQUEST(38:) = '3/1B5B3234357E/ \'  ! ESC[245~
        CPRI_REQUEST(53:53) = CHAR(27)

C       -- define for buttons released only
        ELSE IF ( IOPTION .EQ. 2) THEN
        CPRI_REQUEST(6:) =  '1//1B5B3234327E;'   ! ESC[242~
        CPRI_REQUEST(22:) = '2//1B5B3234347E;'   ! ESC[244~
        CPRI_REQUEST(38:) = '3//1B5B3234367E \'  ! ESC[246~
        CPRI_REQUEST(53:53) = CHAR(27)

C       -- define for buttons pressed or released
        ELSE IF ( IOPTION .EQ. 3) THEN
        CPRI_REQUEST(6:) =  '1/1B5B3234317E/1B5B3234327E;'
        CPRI_REQUEST(34:) = '2/1B5B3234337E/1B5B3234347E;'
        CPRI_REQUEST(62:) = '3/1B5B3234357E/1B5B3234367E \'
        CPRI_REQUEST(89:89) = CHAR(27)
        END IF

C       -- if the option desired is either 1, 2, or 3 then write the DECBLD
C          device control string to the terminal
        IF ( IOPTION .GE. 1 .AND.
     1       IOPTION .LE. 3) WRITE ( 6,'(1X,A)') CPRI_REQUEST

        RETURN ! * from SET_MOUSE_BUTTONS *
        END

=




C************************************************************************
C*                                                                      *
C*                              ONESHOT_DEMO                            *
C*                                                                      *
C*            To demonstrate the use of ReGIS One-shot Graphics input   * 
C*      mode with the mouse on a VT340 terminal. The user generates a   *
C*      report by pressing any of the mouse buttons. The position of    *
C*      the cursor at that time will be shown along with the identity   *
C*      of the button pushed.                                           *
C*                                                                      *
C************************************************************************

        INTEGER*2 INPUT_CHANNEL         ! channel assigned to the terminal
        INTEGER*2 IOPTION               ! mouse button option


        INTEGER*4 DUM                   ! dummy variable
        INTEGER*4 STATUS                ! status of SYS$ASSIGN and
                                        ! SYS$DASSGN
        INTEGER*4 SYS$ASSIGN            ! assign an I/O channel
        INTEGER*4 SYS$DASSGN            ! deassign an I/O channel

        CHARACTER*1 CR                  ! carriage return
        CHARACTER*10 CINPUT             ! buffer to receive data
        CHARACTER*25 CTEXT              ! output text

C************************************************************************

C       -- assign an I/O channel to SYS$INPUT
        STATUS = SYS$ASSIGN ( 'SYS$INPUT',INPUT_CHANNEL,,)
        IF ( .NOT. STATUS) CALL LIB$SIGNAL ( %VAL(STATUS))

C       -- define the mouse buttons for both pressed and released
        IOPTION = 3
        CALL SET_MOUSE_BUTTONS ( IOPTION)

C       -- clear screen
        WRITE ( 6,*) CHAR(27)//'[2J'

C       -- enter ReGIS
        WRITE ( 6,'(''+'',A)') CHAR(27)//'P1p'

C       -- enter one-shot mode
        WRITE ( 6,'(''+'',A)') 'R(I0)'

C       -- request a cursor position report
        WRITE ( 6,'(''+'',A)') 'R(P(I))'

C       -- when a button is pressed, the button code sequence is sent to the
C          terminal's input buffer, followed by the cursor position, and then
C          by a carriage return. Since the button code sequence contains an
C          escape character, it acts as a read terminator; thus 2 reads are
C          required ( one read for the mouse button and the second for the
C          cursor position). Further note that in one-shot mode, if both
C          press and release are defined, the act of pressing the button
C          sends the position report and the terminal exits one_shot mode.
C          The subsequent release of the button by the user does not
C          therefore generate a report.

C       -- the first read captures the button sequence e.g. <ESC>[243~
        CALL READ_BUFFER ( INPUT_CHANNEL,CINPUT)

C       -- determine which button was used
        IF ( INDEX(CINPUT,'241~') .NE. 0) CTEXT = 'Left button pressed'
        IF ( INDEX(CINPUT,'243~') .NE. 0) CTEXT = 'Middle button pressed'

        IF ( INDEX(CINPUT,'245~') .NE. 0) CTEXT = 'Right button pressed'
C       -- note that the release buttons will be recognized in one-shot
C          mode if: 
C          1. The pressed buttons are not defined and the release
C             buttons are defined or
C          2. The button is already pressed by the user as one-shot mode
C             is entered.
        IF ( INDEX(CINPUT,'242~') .NE. 0) CTEXT = 'Left button released'
        IF ( INDEX(CINPUT,'244~') .NE. 0) CTEXT = 'Middle button released'
        IF ( INDEX(CINPUT,'246~') .NE. 0) CTEXT = 'Right button released'

C       -- the second read captures the absolute position of the
C          cursor e.g. [189,9]<CR>
        CALL READ_BUFFER ( INPUT_CHANNEL,CINPUT)

C       -- exit from ReGIS
        WRITE ( 6,'(''+'',A)') CHAR(27)//'\'

C       -- deassign the input channel
        STATUS = SYS$DASSGN ( %VAL(INPUT_CHANNEL))
        IF ( .NOT. STATUS) CALL LIB$SIGNAL ( %VAL(STATUS))

C       -- write the cursor position to the screen
        DUM = INDEX(CINPUT,']')
        WRITE ( 6,'(1X,A)') CTEXT
        WRITE ( 6,*) 'The cursor position is: ',CINPUT(1:DUM)

        CALL EXIT
        END



=




C************************************************************************
C*                                                                      *
C*                              MULT_DEMO                               *
C*                                                                      *
C*            To demonstrate the use of ReGIS Multiple Graphics Input   *
C*      mode with the mouse on a VT340 terminal. The user can draw on   *
C*      the screen by holding button 1 down and moving the mouse. If    *
C*      the button is released, the cursor movement does not leave a    *
C*      trace. The program is exited by pressing button 2.              *
C*                                                                      *
C************************************************************************

        INTEGER*2 IOPTION               ! mouse button option

        INTEGER*2 DUM1,DUM2             ! dummy variables
        INTEGER*2 INPUT_CHANNEL         ! channel assigned to the terminal

        INTEGER*4 STATUS                ! status of SYS$ASSIGN and
                                        ! SYS$DASSGN
        INTEGER*4 SYS$ASSIGN            ! assign an I/O channel
        INTEGER*4 SYS$DASSGN            ! deassign the I/O channel

        CHARACTER*1 CR                  ! carriage return
        CHARACTER*10 CINPUT             ! buffer to receive data
        CHARACTER*10 DRAWSTRING         ! V[xxx,yyy] Draw line to position
        CHARACTER*10 MOVESTRING         ! P[xxx,yyy] Move cursor to position
        CHARACTER*25 CTEXT              ! output text

        LOGICAL*2 LNULL                 ! true if null report is generated
        LOGICAL*2 LDRAW                 ! true if button 1 is pressed
        LOGICAL*2 LDONE                 ! true if button 2 is pressed

C************************************************************************

C       -- initialize a few variables
        LDRAW = .FALSE.
        LDONE = .FALSE.
        IOPTION = 3
        CR = CHAR(13)

C       -- clear screen
        WRITE ( 6,'(''+'',A)') CHAR(27)//'[2J'

C       -- define mouse buttons for both pressed and released.
        CALL SET_MOUSE_BUTTONS ( IOPTION)

C       -- assign an I/O channel to SYS$INPUT
        STATUS = SYS$ASSIGN ( 'SYS$INPUT',INPUT_CHANNEL,,)
        IF ( .NOT. STATUS) CALL LIB$SIGNAL ( %VAL(STATUS))

C       -- enter ReGIS
        WRITE ( 6,'(''+'',A)') CHAR(27)//'P1p'

C       -- select diamond cursor
        WRITE ( 6,'(''+'',A)') 'S(C(I1))'

C       -- enter multiple graphics mode. This sends a CR for synchronization
C          purposes. We'll read it to clear the terminal's input buffer.
        WRITE ( 6,'(''+'',A)') 'R(I1)'
        CALL READ_BUFFER ( INPUT_CHANNEL,CINPUT)

C       -- request a cursor position report
        WRITE ( 6,'(''+'',A)') 'R(P(I))'

C       -- start drawing loop. If button 1 is pressed, drawing occurs. If
C          button 1 is released, drawing stops. If button 2 is pressed, the
C          program ends.
        DO WHILE ( .NOT. LDONE)

C       -- the first read will give the null sequence or the button sequence
        CALL READ_BUFFER ( INPUT_CHANNEL,CINPUT)

        LNULL = .FALSE.
        IF ( INDEX(CINPUT,'240~') .NE. 0) LNULL = .TRUE. ! Null report
        IF ( INDEX(CINPUT,'241~') .NE. 0) LDRAW = .TRUE. ! Left is pressed
        IF ( INDEX(CINPUT,'242~') .NE. 0) LDRAW = .FALSE.! Left is released
        IF ( INDEX(CINPUT,'243~') .NE. 0) LDONE = .TRUE. ! Middle is pressed

C       -- the second read will give us position information of form
C          [xxx,yyy] with which to update our string information.
        CALL READ_BUFFER ( INPUT_CHANNEL,CINPUT)

C       -- update the string information
        IF ( CINPUT(1:1) .EQ. '[') THEN
        DUM2 = INDEX(CINPUT,']')
        MOVESTRING = 'P'//CINPUT(1:DUM2)
        DRAWSTRING = 'V'//CINPUT(1:DUM2)

C       -- if LDRAW is true then write DRAWSTRING out to the terminal.
C          if LDRAW is false then write MOVESTRING out to the terminal.
        IF ( LDRAW) THEN
        WRITE ( 6,'(''+'',A)') DRAWSTRING
        ELSE
        WRITE ( 6,'(''+'',A)') MOVESTRING
        END IF
        END IF

C       -- if the report was a null report, request another cursor position
C          report
        IF ( LNULL) WRITE ( 6,'(''+'',A)') 'R(P(I))'
        END DO

C       -- exit multiple graphics input mode back into one-shot mode. This
C          sends a CR to the terminal's input buffer which we can use for
C          synchronization. Depending on how fast the user releases the
C          button and how fast your system is, stuff may be stored in the
C          terminal's input buffer and must be purged. We read until we hit
C          the synchronizing CR.
        WRITE(6,*)'R(I0)'  ! Back to one_shot mode
        DO WHILE ( CINPUT(1:1) .NE. CR)
        CALL READ_BUFFER ( INPUT_CHANNEL,CINPUT)
        END DO


C       -- exit from ReGIS
        WRITE ( 6,'(''+'',A)') CHAR(27)//'\'

C       -- deassign the input channel
        STATUS = SYS$DASSGN ( %VAL(INPUT_CHANNEL))
        IF ( .NOT. STATUS) CALL LIB$SIGNAL ( %VAL(STATUS))

        END



=