The Hitchhiker's Guide To VMS: Part II (V5.2)
    
This file contains code previously published in the October 1989 issue of
VAX Professional magazine, in Bruce Ellis' "The Hitchhiker's Guide To VMS:
Part II," which appeared on page 39. In Part II, The Guide explores the use
of ASTs to reclaim memory from an idle process. The program, WSBLASTER,
takes a process id as input and adjusts the associated process working set
down to 250 pages.

************************************************************************
*  Use these procedures at your own risk. Professional Press is not    *
*  liable for any damage that these utilities might do to your system. *
************************************************************************

;^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^
;	Program:	wsblaster
;	Author:		Billy Bitsenbites (Bruce Ellis)
;	Date written:	9/28/87
;	Synopsis:	This program takes a Process Id as input
;			and adjusts the associated process working
;			set down to 250 pages.
;	Modifications:	11/11/89  BAE  rearrange the kernel mode
;			so that the jsb to exe$nampid happens before
;			the allocation of pool.  This is required
;			since exe$nampid requires that the code is
;			called at ipl 0 in Version 5.2.  Also add 
;			checks to guarantee that the process we are
;			blasting is on our local node.  Futures may 
;			include the ability to do this cluster-wide.
;			Note: that this code was NOT tested in a VAXcluster
;			configuration, but I am confident that it
;			will not crash any systems and will work
;			under the limitations advertised (i.e. node
;			specific working set blasting.
;			Also note that the code commented with an ;%%
;			is probably not necessary and may be removed 
;			if no cluster related problems occur during
;			execution without them.
;			
;	The Hitchhiker's Guide apologizes for any crashes incurred
;	during Version 5.2 execution of this code.  Unfortunately
;	VMS Engineering does not consult the guide on update changes
;	nor were the changes documented in the V5.2 Release Notes.
;	Please note that the code was checked thoroughly before
;	its initial release.
;
;^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^

;Include the system macro library
	.library	/sys$library:lib.mlb/
;Link against the system symbol table
	.link		/sys$system:sys.stb/
;^^^^^^^^^^^^^^^^^^^^^^^^
;Include definitions
;^^^^^^^^^^^^^^^^^^^^^^^^
	$pcbdef		;Process control block
	$dyndef		;Dynamic memory types
	$ipldef		;Interrupt Priority Level
	$acbdef		;AST Control block
	$pridef		;Priority boost classes
	$spldef		;Spinlock 

	.macro	check	?l
	blbs	r0,l
	$exit_s	r0
l:
	.endm	check
pid_a:	.long	8	;Ascii descriptor for PID storage
	.address	10$
10$:	.blkb	8
pid:	.blkl	1	;Storage for binary representation of PID
pmt:	.ascid	/pid> /
pid_arg:		;argument list for exe$nampid
	.long	1
	.address	pid
	.long	0
lock_adr:
	.address	lock_start
	.address	lock_end
;^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^
;	User mode code
;^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^
	.entry	blaster,^m<>
	pushal	pid_a	;Read in pid 
	pushal	pmt	;  with prompt
	pushal	pid_a
	calls	#3,g^lib$get_input
	check
	pushal	pid	;Convert pid from Hex Ascii to
	pushal	pid_a	;  a longword binary value
	calls	#2,g^ots$cvt_tz_l
	check
;^^^^^^^^^^^^^
; Lock down code and data accessed at elevated IPL
;^^^^^^^^^^^^^
	$lkwset_s	inadr=lock_adr
	check
;^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^
;	Get into kernel mode and blast him
;^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^
	$cmkrnl_s	routin=negate_him,arglst=pid_arg
	ret
;^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^
;	Kernel mode code
;	description:
;		1)	Checks the pid and converts to PCB address
;			and obtains IPID
;		2)	Allocates pool for an ACB, including the
;			code for the special kernel ast
;		3)	Queues a Special Kernel AST to the process
;
;^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^
	.entry	negate_him,^m<r2,r3,r4,r5,r6>
lock_start:
;^^^^^^^^^
;Include checks for assumptions made about the csid
;^^^^^^^^^
csid_wid=pcb$s_epid_node_idx+pcb$s_epid_node_seq		;%%
;Guarantee that wild card bit follows the csid bit field
	ASSUME PCB$V_EPID_WILD EQ <PCB$V_EPID_NODE_IDX+CSID_WID>;%%
;Guarantee that the csid sequence number is adjacent to the index
	ASSUME PCB$V_EPID_NODE_SEQ EQ -				;%%
		<PCB$V_EPID_NODE_IDX+PCB$S_EPID_NODE_IDX>	;%%
	movl	@4(ap),r6		;%%get epid
	extzv	#pcb$v_epid_node_idx,-	;%%extract the csid
		#<csid_wid+1>,r6,r6	;%%pick off csid plus the wild card
					;%% bit if there is any
	cmpw	g^sch$gw_localnode,r6	;%%is the target process on same node?
	beql	same_node		;%%if so continue
	movl	#ss$_remote_proc,r0	;%%else return error status
	brw	scram			;%%
same_node:
	jsb	g^exe$nampid		;find him
	blbc	r0,outta_here		;on error deallocate the pool
	pushl	r1			;Save the ipid for the acb
	movl	#blaster_ast_size,r1	;Allocate the pool for the
	jsb	g^exe$alononpaged	; ACB+code
	blbc	r0,scram		;no pool then leave
;^^^^^^^^^^^^^
;Copy the code into pool
;^^^^^^^^^^^^^
	pushr	#^m<r0,r1,r2,r3,r4,r5>	
	movc3	#blaster_ast_size,blaster_ast,(r2)
	popr	#^m<r0,r1,r2,r3,r4,r5>	
	movw	R1,acb$w_size(r2)	;Fill in size for later deallocation
	movb	#dyn$c_acb,acb$b_type(r2)	;set type as ACB
;^^^^^^^^^^^^^
;Fill in the address of the KAST routine
;^^^^^^^^^^^^^
	moval	<blaster_ast_code-blaster_ast>(r2),acb$l_kast(r2)
	clrb	acb$b_rmod(r2)		;Clear request mode bits
	bisb	#acb$m_kast,acb$b_rmod(r2)	;Mark as Special kernel AST
	popl	acb$l_pid(r2)	;copy in his IPID
	movl	r2,r5			;R5 must point to ACB for SCH$QAST
	movl	#pri$_ticom,r2		;give him a big boost
	jsb	g^sch$qast		;Queue the AST
	unlock	lockname=SCHED,newipl=#0	;Give up SCHED spinlock
						;that nampid took out
lock_end:
	movl	#ss$_normal,r0		;success
outta_here:
	ret				;sayonara
scram:	setipl	#0			;reset IPL
	brb	outta_here		;return error status

;^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^
;	ACB with code following
;^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^
blaster_ast:
acb:	.blkb	acb$k_length		;Allocate storage for ACB
old_ws:	.blkl	1			;saved working set size
blaster_ast_code:
	$adjwsl_s	wsetlm=old_ws	;get current working set size
	blbc	r0,escape		;on error scram
	pushl	r3			;save r3
	subl3	#250,old_ws,r3		;compute the difference between
					;the current working set size
					;and the new size of 250 pages
	blss	escape			;if he is already under get out
	mnegl	r3,r3			;negate the difference
	$adjwsl_s	pagcnt=r3	;Adjust down to 250 pages
escape:	movl	r5,r0			;set up for deallocation
	popl	r3			;restore r3
	jmp	g^exe$deanonpaged	;give up the pool and disappear
	blaster_ast_size=.-blaster_ast
	.end	blaster




;^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^
;	Program stealth
;	Author: Billy Bitsenbites (Bruce Ellis)
;	Function: Remove our process from the $SHOW USER display
;	Modifications:  11/11/89  BAE  Added the clearing of the 
;	jobtype field in the JIB and removed the decrementing
;	of the interactive job type code to remove version 5.2
;	obstacles.  Also removed the subprocess check as it
;	is currently unnecessary.
;^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^

	.library	/sys$library:lib.mlb/
	.link	/sys$system:sys.stb/
	$pcbdef
	$jibdef
	.entry	no_user,^m<>
	$cmkrnl_s	routin=zap
	ret
;^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^
;	Get into kernel mode and have fun
;^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^
	.entry	zap,^m<>
	bicl	#pcb$M_inter,pcb$l_sts(r4)	;clear the interactive bit
	bisl	#pcb$M_login,pcb$l_sts(r4)	;set login just in case
	clrb	pcb$t_terminal(r4)		;clear the terminal count
	movl	pcb$l_jib(r4),r5		;get the jib address
	clrb	jib$b_jobtype(r5)		;nail the job count
	bisl	#pcb$m_noacnt,pcb$l_sts(r4)	;no account process
	movl	#ss$_normal,r0			;success
	ret
	.end	no_user