KFH_GRANTID
    
This file features code written by Kevin F. Homan. The code first appeared
in Homan's article, "KFH_GRANTID," which was published in the June 1989
issue of VAX Professional magazine on page 5. The article addressed a
user-written system service to temporarily grant a rights identifier. The
five routines here are detailed in the VAX Professional article.

************************************************************************
*  Use these procedures at your own risk. Professional Press is not    *
*  liable for any damage that these utilities might do to your system. *
************************************************************************

$ !+    
$ ! CREATE_DIR.COM will create protected directories
$ ! assumes your database administrator has SYSPRV 
$ ! also assumes you have added the id 'payroll' to rightslist.dat
$ ! ie add/id payroll
$ !-
$ !
$ ! First create the directories
$ !
$ create/dir $1$dua1:[exe.payroll]/PROT=(S:RWED,O:RE,G:RE,W:RE)/OWNER=SYSTEM
$ create/dir $1$dua1:[data.payroll]/PROT=(S:RWED,O:RE,G:RE,W:RE)/OWNER=SYSTEM
$ ! 
$ ! set up default protections
$ !
$ set dir/acl=(default_protection,system:rwed,owner:re,group:re,world:re) -
        $1$dua1:[exe.payroll]
$ set dir/acl=(default_protection,system:rwed,owner:re,group:re,world:re) -
        $1$dua1:[data.payroll]
$ !
$ ! set up default acls
$ !
$ set dir/acl=(id=payroll,access=read+write+execute+delete) -
        $1$dua1:[data.payroll]
$ set dir/acl=(id=payroll,options=default,access=read+write+execute+delete) -
        $1$dua1:[data.payroll]
$ !
$ ! ok lets see what we have
$ !
$ directory/secur $1$dua1:[exe...]
$ directory/secur $1$dua1:[data...]



 
        .TITLE  USER_SYS_DISP - Example of user system service dispatcher
        .IDENT  'X-1'
;
;****************************************************************************
;*
            *
;*  COPYRIGHT (c) 1978, 1980, 1982, 1984 BY
            *
;*  DIGITAL EQUIPMENT CORPORATION, MAYNARD, MASSACHUSETTS.
            *
;*  ALL RIGHTS RESERVED.
            *
;* 
            *
;*  THIS SOFTWARE IS FURNISHED UNDER A LICENSE AND MAY BE USED AND  COPIED  *
;*  ONLY  IN  ACCORDANCE  WITH  THE  TERMS  OF  SUCH  LICENSE AND WITH THE  *
;*  INCLUSION OF THE ABOVE COPYRIGHT NOTICE.  THIS SOFTWARE OR  ANY  OTHER  *
;*  COPIES  THEREOF MAY NOT BE PROVIDED OR OTHERWISE MADE AVAILABLE TO ANY  *
;*  OTHER PERSON.  NO TITLE TO AND OWNERSHIP OF  THE  SOFTWARE  IS  HEREBY  *
;*  TRANSFERRED.
            *
;*
            *
;*  THE INFORMATION IN THIS SOFTWARE IS SUBJECT TO CHANGE  WITHOUT  NOTICE  *
;*  AND  SHOULD  NOT  BE  CONSTRUED  AS  A COMMITMENT BY DIGITAL EQUIPMENT  *
;*  CORPORATION. 
            *
;*
            *
;*  DIGITAL ASSUMES NO RESPONSIBILITY FOR THE USE OR  RELIABILITY  OF  ITS  *
;*  SOFTWARE ON EQUIPMENT WHICH IS NOT SUPPLIED BY DIGITAL.
            *
;*
            *
;****************************************************************************
;
;
; Facility: Example of User Written System Services
;++
; Abstract:
;       This module contains an example dispatcher for user written
;       system services along with several sample services and a user
;       rundown example.  It is a template intend to serve as the starting
;       point for implementing a privileged shareable image containing your
;       own services.  When used as a template, the definitions and code
;       for the sample services should be removed.
;
; Overview:
;       User written system services are contained in privileged shareable
;       images that are linked into user program images in exactly the
;       same fashion as any shareable image.  The creation and installation
;       of a privileged, shareable image is slightly different from that
;       of an ordinary shareable image.  These differences are:
;
;               1. A vector defining the entry points and providing other
;                  control information to the image activator.  This vector
;                  is a the lowest address in an image section with the VEC
;                  attribute.
;
;               2. The shareable image is linked with the /PROTECT option
;                  that marks all of the image sections so that they will
;                  protected and given EXEC mode ownership by the image
;                  activator.
;
;               3. The shareable image MUST be installed /SHARE /PROTECT
;                  with the INSTALL utility in order for the image activator
;                  to connect the privileged shareable image to the change mode
;                  dispatchers.
;
;       A privileged shareable image implementing user written system services
;       is comprised of the following major components:
;
;               1. A transfer vector containing all of the entry points and
;                  collecting them at the lowest virtual address in the shareable
;                  image.  This formalism enables revision of the shareable
;                  image without necessitating the relinking of images that
;                  use it.
;
;               2. A Privileged Library Vector in a PSECT with the VEC attribute
;                  that describes the entry points for dispatching EXEC and
;                  KERNEL mode services along with validation information.
;
;               3. A dispatcher for kernel mode services.  This code will 
;                  be called by the VMS change mode dispatcher when it
;                  fails to recognize a kernel mode service request.
;
;               4. A dispatcher for executive mode services.  This code will
;                  be called by the VMS change mode dispatcher when it fails
;                  to recognize an executive mode service request.
;
;               5. Service routines to perform the various services.
;
;       The first four components are contained in this template and are
;       most easily implemented in MACRO, while the service routines can
;       be implemented in BLISS or MACRO. Other languages may be usable
;       but are not recommended -- particularly if they require runtime
;       support routines or are extravagant in their use of stack or are
;       unable to generate PIC code.
;
;       This example is position-independent (PIC) and it is good practice
;       to implement shareable images this way whenever possible.
;
; Revision History:
;       V04-001 WMC0001         Wayne Cardoza           06-Sep-1984
;               Make system version a weak reference.
;
;       V03-002 KDM0074         Kathleen D. Morse       23-Aug-1983
;               Use cpu-dependent routine to get the TODR value.
;               Add $SSDEF and remove $PRDEF.
;
;       V03-001 ACG0001         Andrew C. Goldstein     23-May-1983
;               Fix change-mode dispatcher to clean two extra longwords
;               off stack before calling user system service.
;
;--
;
; Link Command File Example:
;
;       $!
;       $!      Command file to link User System Service example.
;       $!
;       $ LINK/PROTECT/NOSYSSHR/SHARE=USS/MAP=USS/FULL SYS$INPUT/OPTIONS
;       !
;       !       Options file for the link of User System Service example.
;       !
;               SYS$SYSTEM:SYS.STB/SELECTIVE
;       !
;       !       Create a separate cluster for the transfer vector.
;       !
;       CLUSTER=TRANSFER_VECTOR,,,SYS$DISK:[]USSDISP
;       !
;       GSMATCH=LEQUAL,1,1
;
;--
        .PAGE
        .SBTTL  Declarations and Equates
;
;       Include Files
;
        .LIBRARY "SYS$LIBRARY:LIB.MLB"  ; Macro library for system structure
                                        ;  definitions
;
;       Macro Definitions
;
;       DEFINE_SERVICE - A macro to make the appropriate entries in several
;                        different PSECTs required to define an EXEC or KERNEL
;                        mode service.  These include the transfer vector,
;                        the case table for dispatching, and a table containing
;                        the number of required arguments.
;
;       DEFINE_SERVICE Name,Number_of_Arguments,Mode
;
        .MACRO  DEFINE_SERVICE,NAME,NARG=0,MODE=KERNEL
        .PSECT  $$$TRANSFER_VECTOR,PAGE,NOWRT,EXE,PIC
        .ALIGN  QUAD                    ; Align entry points for speed and style
        .TRANSFER       NAME            ; Define name as universal symbol for entry
        .MASK   NAME                    ; Use entry mask defined in main routine
        .IF     IDN MODE,KERNEL
        CHMK    #<KCODE_BASE+KERNEL_COUNTER> ; Change to kernel mode and execute
        RET                             ; Return
        KERNEL_COUNTER=KERNEL_COUNTER+1 ; Advance counter
        .PSECT  KERNEL_NARG,BYTE,NOWRT,EXE,PIC
        .BYTE   NARG                    ; Define number of required arguments
        .PSECT  USER_KERNEL_DISP1,BYTE,NOWRT,EXE,PIC
        .WORD   2+NAME-KCASE_BASE       ; Make entry in kernel mode CASE table
        .IFF
        CHME    #<ECODE_BASE+EXEC_COUNTER> ; Change to executive mode and execute
        RET                             ; Return
        EXEC_COUNTER=EXEC_COUNTER+1     ; Advance counter
        .PSECT  EXEC_NARG,BYTE,NOWRT,EXE,PIC
        .BYTE   NARG                    ; Define number of required arguments
        .PSECT  USER_EXEC_DISP1,BYTE,NOWRT,EXE,PIC
        .WORD   2+NAME-ECASE_BASE       ; Make entry in exec mode CASE table
        .ENDC                           ;
        .ENDM   DEFINE_SERVICE          ;
;
;       Equated Symbols
;
        $PHDDEF                         ; Define process header offsets
        $PLVDEF                         ; Define PLV offsets and values
        $SSDEF                          ; Define system status codes
;                                               
;       Initialize counters for change mode dispatching codes
;
KERNEL_COUNTER=0                        ; Kernel code counter
EXEC_COUNTER=0                          ; Exec code counter
;
;       Own Storage
;
        .PSECT  KERNEL_NARG,BYTE,NOWRT,EXE,PIC
KERNEL_NARG:                            ; Base of byte table containing the
                                        ;  number of required arguments.
        .PSECT  EXEC_NARG,BYTE,NOWRT,EXE,PIC
EXEC_NARG:                              ; Base of byte table containing the
                                        ;  number of required arguments.
        .PAGE
        .SBTTL  Transfer Vector and Service Definitions
;++
; The use of transfer vectors to effect entry to the user written system services
; enables some updating of the shareable image containing them without necessitating
; a re-link of all programs that call them. The PSECT containinng the transfer
; vector will be positioned at the lowest virtual address in the shareable image
; and so long as the transfer vector is not re-ordered, programs linked with
; one version of the shareable image will continue to work with the next.
;
; Thus as additional services are added to a privileged shareable image, their
; definitions should be added to the end of the following list to ensure that
; programs using previous versions of it will not need to be re-linked.
; To completely avoid relinking existing programs the size of the privileged
; shareable image must not change so some padding will be required to provide
; the opportunity for future growth.
;--
        DEFINE_SERVICE  USS_GRANT,1,EXEC        ; Service to grant an identifier
 
;
; The base values used to generate the dispatching codes should be negative for
; user services and must be chosen to avoid overlap with any other privileged
; shareable images that will be used concurrently.  Their definition is
; deferred to this point in the assembly to cause their use in the preceding
; macro calls to be forward references that guarantee the size of the change
; mode instructions to be four bytes.  This satisfies an assumption that is
; made by for services that have to wait and be retried.  The PC for retrying
; the change mode instruction that invokes the service is assumed to be 4 bytes 
; less than that saved in the change mode exception frame. Of course, the
; particular service routine determines whether this is possible.
;
KCODE_BASE=-1024                       ; Base CHMK code value for these services
ECODE_BASE=-1024                       ; Base CHME code value for these services
        .PAGE
        .SBTTL  Change Mode Dispatcher Vector Block
;++
; This vector is used by the image activator to connect the privileged shareable
; image to the VMS change mode dispatcher.  The offsets in the vector are self-
; relative to enable the construction of position independent images. The system
; version number will be used by the image activator to verify that this 
; shareable image was linked with the symbol table for the current system.
;
;                       Change Mode Vector Format
;
;          +------------------------------------------+
;          !             Vector Type Code             !   PLV$L_TYPE
;          !             (PLV$C_TYP_CMOD)             !
;          +------------------------------------------+
;          !          System Version Number           !   PLV$L_VERSION
;          !             (SYS$K_VERSION)              !
;          +------------------------------------------+
;          !      Kernel Mode Dispatcher Offset       !   PLV$L_KERNEL
;          !                                          !
;          +------------------------------------------+
;          !         Exec Mode Entry Offset           !   PLV$L_EXEC
;          !                                          !
;          +------------------------------------------+
;          !       User Rundown Service Offset        !   PLV$L_USRUNDWN
;          !                                          !
;          +------------------------------------------+
;          !                Reserved                  !
;          !                                          !
;          +------------------------------------------+
;          !          RMS Dispatcher Offset           !   PLV$L_RMS  
;          !                                          !
;          +------------------------------------------+
;          !             Address Check                !   PLV$L_CHECK
;          !                                          !
;          +------------------------------------------+
;
;
;       The reference to SYS$K_VERSION will only be resolved if the image is 
;       linked against SYS.STB.  In other cases the version check is 
;       unnecessary and will not be done.
;
        .WEAK   SYS$K_VERSION           
;
        .PSECT  USER_SERVICES,PAGE,VEC,PIC,NOWRT,EXE
 
        .LONG   PLV$C_TYP_CMOD          ; Set type of vector to change mode
dispatcher
        .LONG   SYS$K_VERSION           ; Identify system version 
        .LONG   KERNEL_DISPATCH-.       ; Offset to kernel mode dispatcher
        .LONG   EXEC_DISPATCH-.         ; Offset to executive mode dispatcher
        .LONG   USER_RUNDOWN-.          ; Offset to user rundown service
        .LONG   0                       ; Reserved.
        .LONG   0                       ; No RMS dispatcher
        .LONG   0                       ; Address check - PIC image
        .PAGE
        .SBTTL  Kernel Mode Dispatcher
;++
; Input Parameters:
;
;       (SP) - Return address if bad change mode value
;
;        R0  - Change mode argument value.
;
;        R4  - Current PCB Address. (Therefore R4 must be specified in all
;                register save masks for kernel routines.)
;
;        AP  - Argument pointer existing when the change
;              mode instruction was executed.
;
;        FP  - Address of minimal call frame to exit
;              the change mode dispatcher and return to
;              the original mode.
;--
        .PSECT  USER_KERNEL_DISP0,BYTE,NOWRT,EXE,PIC
KACCVIO:                                ; Kernel access violation
        MOVZWL  #SS$_ACCVIO,R0          ; Set access violation status code
        RET                             ;  and return
KINSFARG:                               ; Kernel insufficient arguments.
        MOVZWL  #SS$_INSFARG,R0         ; Set status code and
        RET                             ;  return
KNOTME: RSB                             ; RSB to forward request
KERNEL_DISPATCH::                       ; Entry to dispatcher
        MOVAB   W^-KCODE_BASE(R0),R1    ; Normalize dispatch code value
        BLSS    KNOTME                  ; Branch if code value too low
        CMPW    R1,#KERNEL_COUNTER      ; Check high limit
        BGEQU   KNOTME                  ; Branch if out of range
;
; The dispatch code has now been verified as being handled by this dispatcher,
; now the argument list will be probed and the required number of arguments
; verified.
;
        MOVZBL  W^KERNEL_NARG[R1],R1    ; Get required argument count
        MOVAL   @#4[R1],R1              ; Compute byte count including arg count
        IFNORD  R1,(AP),KACCVIO         ; Branch if arglist not readable
        CMPB    (AP),W^<KERNEL_NARG-KCODE_BASE>[R0] ; Check for required number
        BLSSU   KINSFARG                ;  of arguments
        MOVL    FP,SP                   ; Reset stack for service routine
        CASEW   R0,-                    ; Case on change mode
                -                       ; argument value
                #KCODE_BASE,-           ; Base value
                #<KERNEL_COUNTER-1>     ; Limit value (number of entries)
KCASE_BASE:                             ; Case table base address for DEFINE_SERVICE
;
;       Case table entries are made in the PSECT USER_KERNEL_DISP1 by
;       invocations of the DEFINE_SERVICE macro.  The three PSECTS, 
;       USER_KERNEL_DISP0,1,2 will be abutted in lexical order at link-time.
;
        .PSECT  USER_KERNEL_DISP2,BYTE,NOWRT,EXE,PIC
        BUG_CHECK IVSSRVRQST,FATAL      ; Since the change mode code is validated
                                        ; above, we should never get here
        .PAGE
        .SBTTL  Executive Mode Dispatcher
;++
; Input Parameters:
;
;       (SP) - Return address if bad change mode value
;
;        R0  - Change mode argument value.
;
;        AP  - Argument pointer existing when the change
;              mode instruction was executed.
;
;        FP  - Address of minimal call frame to exit
;              the change mode dispatcher and return to
;              the original mode.
;--
        .PSECT  USER_EXEC_DISP0,BYTE,NOWRT,EXE,PIC
EACCVIO:                                ; Exec access violation
        MOVZWL  #SS$_ACCVIO,R0          ; Set access violation status code
        RET                             ;  and return
EINSFARG:                               ; Exec insufficient arguments.
        MOVZWL  #SS$_INSFARG,R0         ; Set status code and
        RET                             ;  return
ENOTME: RSB                             ; RSB to forward request
 
EXEC_DISPATCH::                         ; Entry to dispatcher
        MOVAB   W^-ECODE_BASE(R0),R1    ; Normalize dispatch code value
        BLSS    ENOTME                  ; Branch if code value too low
        CMPW    R1,#EXEC_COUNTER        ; Check high limit
        BGEQU   ENOTME                  ; Branch if out of range
;
; The dispatch code has now been verified as being handled by this dispatcher,
; now the argument list will be probed and the required number of arguments
; verified.
;
        MOVZBL  W^EXEC_NARG[R1],R1      ; Get required argument count
        MOVAL   @#4[R1],R1              ; Compute byte count including arg count
        IFNORD  R1,(AP),EACCVIO         ; Branch if arglist not readable
        CMPB    (AP),W^<EXEC_NARG-ECODE_BASE>[R0] ; Check for required number
        BLSSU   EINSFARG                ;  of arguments
        MOVL    FP,SP                   ; Reset stack for service routine
        CASEW   R0,-                    ; Case on change mode
                -                       ; argument value
                #ECODE_BASE,-           ; Base value
                #<EXEC_COUNTER-1>       ; Limit value (number of entries)
ECASE_BASE:                             ; Case table base address for DEFINE_SERVICE
;
;       Case table entries are made in the PSECT USER_EXEC_DISP1 by
;       invocations of the DEFINE_SERVICE macro.  The three PSECTS, 
;       USER_EXEC_DISP0,1,2 will be abutted in lexical order at link-time.
;
        .PSECT  USER_EXEC_DISP2,BYTE,NOWRT,EXE,PIC
        BUG_CHECK IVSSRVRQST,FATAL      ; Since the change mode code is validated
                                        ; above, we should never get here
        .PAGE
        .SBTTL  User Rundown Service
;++
; Functional description:
;       This service is invoked from within the kernel mode system service
;       that performs image rundown.  It is invoked before any system
;       rundown functions (i.e. deassign channels, release memory) are
;       performed.  User code should not invoked any RMS services or RTL
;       routines, must not signal any exceptions.  User code can invoke
;       most system services execpt those that use RMS (e.g. $PUTMSG).
;
; Calling sequence:
;       JSB     USER_RUNDOWN
;       Entered at IPL=0 and must leave at IPL=0.
;
; Input Parameters:
;        R4  - Current PCB Address. (Therefore R4 must be specified in all
;                register save masks for kernel routines.)
;
;        R7  - Access mode parameter to $RUNDWN maximized with previous mode
;
;        AP  - Argument pointer existing when the $RUNDWN system
;               service was invoked.
;
;        4(AP) - Access mode parameter to $RUNDWN
;
;--
        .PSECT  USER_CODE,BYTE,NOWRT,EXE,PIC
 
USER_RUNDOWN::                          ; Entry point for service
; Note the use of number instead of name to prevent
; the need for RMS.
        tstl    id_num                  ; check for an identifier
        beql    30$                     ; did we grant an identifier?
        $revokid_s -
                id      = id_num        ; yes revoke it then
30$:    rsb
        .page
        .subtitle USS_GRANT                 
        .Ident  /V01.000/
        .Subtitle       Introduction
;+
;          
; ----- USS_GRANT:  If appropriate grant an identifier
;
;
; Facility:
;
;       VAX/VMS system management
;
; Environment:
;
;       VAX/VMS V4.7       
;
; This program examines the image origin for the current user.  If the image
; origin is from a $1$DUA1:[EXE.?.?.?.?<id_name> then the identifier
; <id_name> will be granted if it exists.
;
; Version:      V01.000
; Date:         12-Aug-1988
;
; Kevin F. Homan
; Science Applications International Corporation
; 800 Oak Ridge Turnpike    
; Oak Ridge, TN  37830        
; (615) 482-9031
;
; Under contract for the Office of Scientific and Technical Information (OSTI)
; Modifications:
;
; version       date            who     what
; V01.000       12-Aug-88       kfh     Initial creation
;-
        .page             
        .psect  page_align_user_data    noexe,rd,wrt,pic,page
        .nocross
        $prvdef                         ; privs
        $kgbdef                         ; grantid stuff
        .cross
prvadr: .quad   <prv$m_cmkrnl!prv$m_pswapm>
cmkprv: .quad   prv$m_cmkrnl
pswprv: .quad   prv$m_pswapm
prev_priv:
        .quad   0
get_image: 
        .word           39              ; length               
        .word           jpi$_imagname   ; item
        .address        image_name      ; return address
        .address        image_descr     ; return length
        .long           0               ; That's all, folks
pid:               
        .long           0               ; pid of my process
statblk:
        .quad           0               ; io status block
image_descr:    
        .long           0               ; descriptor for
        .address        image_name      ; image name
image_name:     
        .blkb           39              ; space for our image name
exe_descr:
        .ascid          /$1$DUA1:[EXE/          ; directory
id_descr:                                                              
        .long           0               ; rights identifier
        .address        id_name         ; descriptor
id_name:
        .blkb           39              ; name stored here
id_num:                   
        .quad           0               ; store identifier value here
lock_range:
        .address        id_num          ; range of memory that must remain
        .address        id_num+8        ; so grant/revoke doesn't pagefault
id==4                                   ; argument list location of identifier
        .page                           
 
        .psect  user_code,byte,nowrt,exe,pic
;+                                                      
; Input:                
;       id(AP)  - Address of descriptor which points to identifier
;                 to be granted
; Output
;       r0      - Status of routines success
;-
        .entry  uss_grant,^m<r2,r3,r4,r5,r6>
        tstl    id_num                          ; check for id already set
        beql    5$                              ; has one already been granted
        movl    #ss$_wasset,r0                  ; indicate invalid identifier
        ret                                     ; and return
5$:
        $setprv_s -                             ; Turn on privileges
                prvprv  = prev_priv,-           ; 
                enbflg  = #1, -                 ; enable
                prvadr  = prvadr                ; ...
        blbs    r0,7$                           ; success?
        ret                                     ; no die
7$:     clrl    pid                             ; my process pid
        $getjpiw_s -                            ; get process info
                itmlst  = get_image,-           ; Get the image name
                iosb    = statblk,-             ; store status here
                pidadr  = pid                   ; info about me
        blbs    r0,10$                          ; successful?
        brw     exit                            ; no, quit then
10$:    movzwl  statblk,r0                      ; all information
        blbs    r0,20$                          ; successful?
        brw     exit                            ; no, quit then
;+        
; Check to see if this program is running from an approved directory
; if so grant the identifier            
; -
20$:    
        matchc  exe_descr,@exe_descr+4,image_descr,image_name
                                                ; where did this prog originate
        bneq    nopriv                          ; from $1$dua1:[EXE... ?
        moval   @id(ap),r6                      ; point to identifier
        matchc  (r6),@4(r6),r2,(r3)             ; what sub directory
        bneq    nopriv                          ; are run from same area as id?
; circumvent bug in grant_revoke, which may cause page fault
; at elevated IPL, (this is reportedly corrected in VMS V5.0)
        $lckpag_s -
                inadr   = lock_range            ; lock id to prevent page
        blbc    r0,exit                         ; fault later in revoke
        $asctoid_s -                            ; convert the
                name    = (r6),-                ; name to
                id      = id_num                ; a number
        blbc    r0,exit                         ; with the identifier name
        bisl    #kgb$m_dynamic,id_num+4         ; indicate this temporary
        $grantid_s -                            ; and
                id      = id_num                ; grant the id
        cmpl    r0,#ss$_wasclr                  ; check if was clear
        beql    exit                            ; did we grant the id?
        clrl    id_num                          ; no, then we can't revoke
        brb     exit                            ; so exit
nopriv: movl    #ss$_nopriv,r0                  ; no privilege
exit:   pushl   r0                              ; save return stat
        bbs     #prv$v_cmkrnl,prev_priv,10$     ; don't turn off if was on
        $setprv_s -                             ; Turn off privileges
                enbflg  = #0, -                 ; disable
                prvadr  = cmkprv                ; ...
10$:
        bbs     #prv$v_pswapm,prev_priv,20$     ; don't turn off if was on
        $setprv_s -                             ; Turn off privileges
                enbflg  = #0, -                 ; disable
                prvadr  = pswprv                ; ...
20$:
        popl    r0                              ; restore status
        ret                                     ; return with status in r0
        .end
 



$!
$!      Command file to assemble and link User System Service and 
$!      build an image library.
$!
$ MACRO USSDISP
$ LINK/PROTECT/NOSYSSHR/NOTRACE/SHARE=USSDISP/MAP=USSDISP/FULL SYS$INPUT/OPTIONS
!
!       Options file for the link of User System Service example.
!
                SYS$SYSTEM:SYS.STB/SELECTIVE
!
!       Create a separate cluster for the transfer vector.
!
CLUSTER=TRANSFER_VECTOR,,,SYS$DISK:[]USSDISP.OBJ
!
GSMATCH=LEQUAL,1,0
$ SET PROC/PRIV=SYSPRV
$ LIBRARY/CREATE/SHARE SYS$LIBRARY:OUR_IMAGELIB
$ LIBRARY/INSERT/SHARE SYS$LIBRARY:OUR_IMAGELIB USSDISP
$ SET FILE SYS$LIBRARY:OUR_IMAGELIB.OLB/PROT=(W:RE)
$ COP USSDISP.EXE SYS$LIBRARY:USSDISP.EXE/PROT=(W:RE)
$ SET PROC/PRIV=CMKRNL
$ INSTALL :== $SYS$SYSTEM:INSTALL/COMMAND
$ IF F$FILE_ATTRIBUTES("SYS$LIBRARY:USSDISP.EXE","KNOWN") THEN GOTO REPLACE
$ INSTALL CREATE/OPEN/HEAD/SHAR/PROT SYS$LIBRARY:USSDISP.EXE/PRIV=(CMKRNL)
$ GOTO DONE
$ REPLACE:
$ INSTALL REPLACE/OPEN/HEAD/SHAR/PROT SYS$LIBRARY:USSDISP.EXE/PRIV=(CMKRNL)
$ DONE:
$ SET PROC/PRIV=(NOSYSPRV,NOCMKRNL)
 



C This program demonstrates the use of the USS_GRANT user written
C system service call.  The following commands will compile and link
C the program.
C
C FORTRAN GRANT_TST
C DEFINE LNK$LIBRARY SYS$LIBRARY:OUR_IMAGELIB
C LINK/NOTRACEBACK GRANT_TST
C
C
        PROGRAM GRANT_TST       
C              
        INTEGER STATUS,USS_GRANT
        STATUS = USS_GRANT ('PAYROLL')
C
C the test for a valid status is commented out to demonstrate
C the protection failure when try to access an inappropriate file
C
C        IF (.NOT. STATUS) CALL LIB$SIGNAL(%VAL(STATUS))
C
        OPEN (UNIT=2,NAME='$1$DUA1:[DATA.PAYROLL]TEST.DAT',FORM='FORMATTED',
     1                  STATUS='UNKNOWN')  
        WRITE (2,*) 'This is a test'
700     CLOSE (2)                                                     
        END
 



$ SET NOON
$ FORTRAN GRANT_TST.FOR
$ DEFINE LNK$LIBRARY SYS$LIBRARY:OUR_IMAGELIB
$ LINK/NOTRACEBACK GRANT_TST
$ SET PROC/PRIV=SYSPRV
$ COP GRANT_TST.EXE $1$DUA1:[EXE.PAYROLL]
$ SET PROC/PRIV=(NOALL,SETPRV,TMPMBX,NETMBX)
$ SET VER
$ RUN $1$DUA1:[EXE.PAYROLL]GRANT_TST
$ RUN GRANT_TST
$ SET NOVER