PCbridge: a inexpensive Ethernet Bridge
                             Vance Morrison


What is bridge?

    A bridge is a device that spans two or more networks (almost always
    ethernet), forwards packets between the networks so that it appears
    that the networks are a single network.  Bridges differ from repeaters
    because they gather information about where hosts on the networks are
    and ONLY forward messages when necessary.  Since local traffic stays
    local, a bridged network can handle more traffic than a single larger
    network.  Bridges differ from routers (like PCroute), because they
    only depend on the ethernet addressing scheme and not on the higher
    level protocol (IP, DECNET, SNA etc), that handles internetwork routing.

What is PCbridge?

    PCbridge is a simple program written for an IBM-PC that will turn
    a PC with appropriate interface cards into a ethernet bridge.   It
    has the capability to act as a standard 2 way ethernet-ethernet 
	or ethernet-starlan bridge as well as a remote bridge 
	(ethernet-serial-ethernet) or a n-way bridge.   With this software 
	it is possible to assemble a bridge for under $1000, that will 
	outperform bridges costing $2000 or more.

What does PCbridge Support?

    PCbridge supports

        Ethernet interfaces with the Western Digital WD8003E, WD8003EBT
            WD8013EBT cards.  

        Starlan cards with the WD8003S and WD8003SH cards.

        Serial Interfaces with the standard 8250 IBM COM ports at 
            baud rates up to 56.7K baud, as well as support for the
            newer 16550AF chips with built in FIFO buffers (these
            newer COM boards are HIGHLY recommended since they can
            reduce the interrupt overhead by a factor of 10).  COM
            boards with the 16550AF chips are now widely available
            from PC vendors.


What does PCbridge NOT support?

    Although it performs the  bridging function very well, it is not
    a 'smart' bridge.  In particular it does NOT include any spanning
    tree algorithm for detecting and breaking loops.    This does not
    mean PCbridge can't be used in a bridged network with loops, it simply
    means that other 'smarter' bridges must be used at strategic places
    that will perform this function.  In addition PCbridge does NOT support
    SNMP or any other network management protocol.   


How fast is PCbridge?

    Bridges have two metrics associated with them.  First is the number
of packets a second it can forward, and the other how many packets a second
it can filter.   The second metric is interesting because it can't be 
easily be measured directly, after all rock connected to two pieces of 
ethernet will filter (drop) as many packets per second as you like.  The
meaning of the second metric is to determine just how fast the router
can examine ethernet packets if it does not need to forward them.  

    To measure this I placed a counter in the main loop that was incremented
every time a packet was examined (from either ethernet segment).  Then I 
modified the code slightly so that the code ALWAYS thought it got a packet
that it should drop.  Thus by running the code for a time and determining
how many packets it examined I could come up with a very accurate filtering
rate.

    The forwarding rate was measured by measuring the packet delay.  
This actually tends to underestimate the packet throughput, but we will
use it as a rough guide.    All of these tests were done with the
WD8003E card.  If you are using the WD8013 card with its 16 bit data
path, you can expect the packet forwarding rate to almost double.
Unfortunately, I do not have test data for this card.

         Packet Filtering    Packet Forwarding (60byte)
            rate (PPS)          rate (PPS)
    -------------------------------------------------------------
    4.77Mhz XT      4080 PPS            1677 PPS
    10Mhz XT (est)  8000 PPS            3000 PPS
    16Mhz AT        26214 PPS           5832 PPS

While packet filtering is independent of packet size, packet forwarding
is dependent on the size of the packet.   The packets I used where the
smallest ethernet packet (60 bytes).  
        
For comparison purposes a low end Retix bridge costs $2000 (actually
more if you want thin ethernet) and has a forwarding rate of 6000 PPS
and a filtering rate of 10,000 PPS.   An 16Mhz AT with WD8013EBT cards
(costing about $1000) is likely to have forwarding rates of about 
10,000 PPS and  filtering rates of about 25,000 PPS.  Thus you will
get almost twice the performance for half the cost.

------------------------------------------------------------------------

Which ethernet card is for me?

   Note that all the WD80XX cards have on-board input buffers that can
keep up with the full 10Mbit/sec bit rate of ethernet.  The bridge
will ONLY start dropping packets when this input queue has filled. 
The queue sizes are as follows

        WD8003E         6.5K bytes
        WD8003EBT       30.5K bytes
        WD8013EBT       14.5K bytes

Note that may file serving programs (Novell and NFS for example) like
to send data in fast 8K blocks.  Because the WD8003E card has only a 6.5K
buffer, this will cause packets to be lost if the WD8003E card is used
in such an environment.    

The WD8013EBT has the additional advantage of having a 16bit data path.
Thus this card can transfer data to other cards twice as fast as the
WD8003X cards.   The only disadvantage to this card is that it can not
be used in a XT machine, an AT or better machine is needed.  

Thus the recommended configuration is a cheap AT clone with WD8013EBT
cards.  If an XT must be used, or packet forwarding is not a issue,
then WD8003EBT cards are the second choice.  Only if no file serving
traffic is expected (like in a remote bridge), is the WD8003E recommended.

Note that if you HAVE to run NFS though a bridge with WD8003E cards it
should be possible to ask NFS to send data in smaller 4K blocks. 
On UNIX systems this is done via the 'rsize' and 'wsize' parameters
in fstab.   Since this has to be done for every NFS hosts, this is
clearly a choice of last resort, but I thought I would mention it.

--------------------------------------------------------------------------


Disclaimer - 

    I have tested PCbridge quite a bit, but we do not use it here
    in a production environment.  Thus I cannot guarantee that it will
    work well for your particular situation.  It should though.

---------------------------------------------------------------------------

Questions, comments, and bug reports to:

    morrison@accuvax.nwu.edu

    Vance Morrison