ERSATZ-11 BETA VERSION 1.0
                            PDP-11 SYSTEM SIMULATOR
                           Release date: 14-Nov-1994
                       Copyright (C) 1994 by John Wilson
                              All rights reserved
        
             E11.EXE is a beta test version of a full system emulator
        for the PDP-11.  It runs on any AT-class machine with an 80186
        or better CPU, and requires around 350KB of free memory.  It is
        intended to boot and run any PDP-11 operating system (it has
        been tested with RT-11 (all flavors), RSX-11M, RSTS/E, 2.9BSD
        UNIX, Fuzzball, and XXDP+;  it seems to have some problems with
        IAS, and no attempt has been made to test DOS/BATCH, TSX+,
        MUMPS, or any flavor of UNIX other than 2.9BSD;  2.11BSD will
        definitely not work due to its need for "cadillac" hardware).

        Emulated configuration:

        * PDP-11/34a CPU with selectable extensions
        * FP11A floating point processor
        * 248KB main memory
        * RL11/RL01-02 disk drives (up to 4)
        * RK611/RK06-07 disk drives (up to 8)
        * RX211/RX02 or RX11/RX01 8" floppy (using image files and/or
          1.2MB floppies)
        * DL11 terminal ports;  console and up to 15 others (VT100,
          and/or uses COM ports and/or LPT ports)
        * LP11 printer ports;  up to 4 (same devices as DL11)
        * KW11L line clock (50/60 Hz, settable)
        
             The emulator speed depends on the application (changing MMU
        registers is an expensive operation so multiuser OSes tend to
        run more slowly than RT-11FB does, for example), but in general
        it runs noticeably above the speed of a real PDP-11/34a (with
        cache) on a 486-DX2/80.  Your mileage may vary.  It has
        successfully booted and run RT-11FB on a 4.77 MHz IBM PC with a
        V20 processor (80186-compatible), but it barely stayed ahead of
        the clock interrupts.
        
             The FP11 emulation requires a math coprocessor.  If the PC
        has none, then the emulated PDP-11 will have no FPP either.
        
             I consider this program to be a beta test release because
        there are still some reported bugs that I've been unable to
        duplicate, and there are many unfinished or unstarted features
        that I plan to add, most of which hinge on porting the program
        to run in 80386 protected mode so as to be able to implement
        22-bit addressing efficiently.  My apologies to anyone who wants
        to run it on an 80286 or earlier, the final version will most
        likely require a 386.  Besides the program is growing so rapidly
        that nothing has been left untouched long enough to be
        considered 100% tested.  However in my own experience the
        emulator has been very reliable, I wish I could say the same for
        my real PDP-11s.

        Known problems:

        * IAS doesn't work with the emulator for some reason.  I don't
          know why yet.

        Planned additions:

        * Network hardware.  Started but not yet finished.  The idea I'm
          toying with is having the init file say which protocol numbers
          the 11 needs to receive and then registering those with a packet
          driver, then simulating a DELUA which "hears" only those packet
          types.  That way it wouldn't interfere with other network
          software on the same PC.

        * MSCP disks.  Don't get me started on this one...  (DEC is
          still cagey about documentation even though all the competitors
          that they were trying to fool got their clones working years
          ago.)  It might be cute to simulate these using their own
          partitions on the hard disk, then write real DSRs for a few
          popular controllers (i.e.  bypassing DOS) so that disk I/O would
          be truly asynchronous (like real hardware), that would speed
          things up considerably, as well as stop the emulator from
          pausing emulation for a few seconds during drive spin-ups on
          "Green" PCs.  But remember, this section deliberately omitted.

        * Some kind of tape support.  My first goal will be to support
          QIC-40/QIC-80 drives with a format compatible with Linux's FTAPE
          package (which makes them act like 9-track magtapes).  Don't
          hold your breath though, I have no understanding at all of
          Reed-Solomon ECC and the QIC documents have a lot of holes in
          them anyway.  A longer range goal (although probably easier)
          will be supporting SCSI 9-track drives attached to the PC.  The
          main holdup there is that I don't have one.

        
             The system has been tested under the XXDP+ diagnostic
        monitor.  It passes the KD11EA diagnostics DFKAA, DFKAB, and
        DFKAC, and the FP11A diagnostics DFFPA, DFFPB, and DFFPC.  It
        fails all MMU diagnostics due to the absence of the maintenance
        mode.


        COMMANDS
        
             Ersatz-11 recognizes a number of keyboard commands.  These
        are entered at the "E11>" prompt, which appears when the PDP-11
        is halted but may be brought up at any time by pressing
        Alt-SysReq (or by pressing the BREAK key on a serial terminal if
        the console terminal (TT0:)  has been ASSIGNed to a COM port).
        Commands (and parameters and switches) may generally be
        shortened to any unique abbreviation.

        INITIALIZATION FILE
        
             When E11 is first started, it looks for a file named
        "E11.INI" first in the current directory, and then in the
        directory where E11.EXE is located (or, it searches the PATH if
        you're still running DOS V2.X).  If this file exists than a
        command is read from the file each time E11 would otherwise
        prompt for a user command;  input for the console DL11 still
        comes from the keyboard, so the init file may be used both to
        start up the system and to shut it down (E11 will continue after
        the BOOT command if you type Alt-SysReq).  If a line's first
        non-blank character is ';' or '!', it is treated as a comment.

        Typical E11.INI file:
        
        mount dl0: rt11.dsk
        ; uncomment the ASSIGN command to use a COM port for console I/O
        ; (baud rate must have been initialized from DOS using a MODE command)
        ;assign kb0: com3: /irq5
        boot/rt11 dl0:
        ; control returns to the next line when the user presses Alt-SysRq
        quit

        COMMAND DESCRIPTIONS
        ======= ============


        ASSIGN ddu:  Fn
        ASSIGN ddu:  COMn:  [/IRQn [/SHARE]]

        Assigns a physical PC device to emulate a particular DL11
        (TT0:-TT15:)  or LP11 port (LP0:-LP3:).  The first (and possibly
        only) argument after the PDP-11 device name may be either the
        name of a function key F1-F12, or a serial port COM1:-COM4:, or
        a line printer port LPT1:-LPT4:.

        If a function key is given, then the specified port is connected
        to a simulated VT100 which can be put up on the screen by
        pressing Alt and the specified function key (note that the
        screens assigned to F11 and F12 are not accessible if you still
        have the 84-key AT keyboard, sorry;  but look at the bright
        side, at least you get the keypad comma key).  When one screen
        is being displayed on the PC screen, the others (up to 11) are
        maintained invisibly in memory, so they will be up to date when
        you switch the display to them by pressing Alt and the function
        key for the screen you want.

        UNTESTED FEATURE:  If there are two video adapters on the PC
        (e.g.  an SVGA and a Hercules mono card), then one DL11/LP11
        pseudo VT100 may be displayed on each.  The Alt-function keys
        choose which of the 12 possible screens is displayed on the
        primary monitor, and the Ctrl-function keys choose which is on
        the secondary monitor.  Note that it is not possible to display
        the same port on both monitors at once.  I no longer have such a
        setup so the code is untested.

        If the name of a COM port is given, then the specified DL11/LP11
        port is connected to that port.  Any IRQ from IRQ0 to IRQ15 may
        be specified, or if the IRQ is omitted then IRQ4 is used for COM
        ports whose I/O base address is 300h or more, IRQ3 for 2FFh or
        less.  These defaults have been in use since XTs were the
        standard, and most multi I/O boards will be set up this way.
        However it's not uncommon with newer boards for COM3 to use IRQ5
        and COM4 to use IRQ2 (or IRQ9 really, which is effectively the
        same on an AT);  you will have to use the /IRQ5 and /IRQ2
        switches in this case.  The /SHARE switch (the /IRQn switch is
        required if /SHARE is given) means that the serial port has
        special IRQ sharing hardware (as documented in the IBM AT
        Technical Reference Manual) so that more than one device may use
        the same IRQ at once;  this hardware is relatively rare, so if
        you don't know whether you have it, you probably don't.  Note
        that without this hardware it's not possible for more than one
        device to be actively using the same IRQ at the same time;  so
        for example if you have a mouse attached to COM1 using IRQ4 and
        it has been initialized by MOUSE.COM, E11 will not be able to
        use COM3 if it also uses IRQ4.

        The baud rate, number of data bits, etc.  for a COM port should
        be set with a MODE command from DOS before Ersatz-11 is run.

        If the name of an LPT port is given, then the specified
        DL11/LP11 port is connected to that port.  /IRQn and /SHARE may
        be given as for COM ports;  the default IRQ for all LPT ports is
        IRQ7.  E11's LPT handler uses interrupts;  I've seen vague
        references to interrupts not working correctly with some LPT
        ports, or maybe it was with some printers, but having polled I/O
        as an option would be horribly slow (either printing speed or
        CPU emulation or both would suffer) so it's not supported.
        Interrupts work great with my brand-X LPT port and 13-year-old
        NEC Spinwriter.  Trouble is most likely if you have multiple LPT
        ports, since they may all try to drive IRQ7 at once.

        LPT output is passed transparently, so you'll need to make sure
        that your OS and printer agree on whether lines end in <CRLF> or
        just <LF>, and on whose responsibility it is to interpret tabs
        and form feeds.

        Note that it is possible to ASSIGN a TT:  port to a printer, or
        to ASSIGN an LP:  port to a screen.  Why you'd want to do this I
        don't know but who am I to stop you.  The reason for making them
        both use the same pool of devices was so that they could both
        access COM ports, since serial terminals and serial printers are
        both reasonable devices.  LP:  ports attached to COM ports or
        screens respond to XON/XOFF flow control.

        The ASSIGN command fails if the specified COM or LPT port
        doesn't exist, or if the specified (or default) IRQ is already
        in use and the /SHARE switch is not given, or if you're trying
        to steal TT0:'s device for some other port (there must always be
        a TT0:  since that's E11's console terminal).


        BOOT ddu:  [/switches]

        Boots the system from the specified disk.  The disk must have
        been mounted with the MOUNT command.  The optional switch is an
        OS name;  for now the only meaningful ones are /RT11 and /RSTS,
        /RSX is defined too but has no effect.  This has to do with the
        method used to pass time and date information to a newly booted
        monitor.  RT-11 ignores the time and date passed at 005000
        unless the NOP in the first word of the bootstrap is cleared to
        0 (HALT) and the bootstrap is entered at 000002.  RSTS believes
        the time and date at 001000 (in a different format from RT-11)
        regardless of whether its NOP was nuked, but later versions of
        RSTS save the first word of the bootstrap and execute it later
        (anyone know why?), so they will halt if the system was booted
        the RT-11 way.  Hence the need for the switch.  If you like
        typing the time and date manually (or your PC has no RTC) then
        don't worry about the switch.  I don't know enough about RSX or
        any other OS to set up the time/date for it, if that's even
        possible (although, simulating a made-up RTC device would be
        easy, to be read by a privileged program during OS startup;  but
        making an emulator emulate hardware that never existed and never
        will seems somehow like cheating to me).

        There is also a /HALT switch, which means to go as far as
        loading block 0 into core and setting up the registers, but to
        stop there.  This can be handy for debugging boot blocks.


        CALCULATE expr (& expr is a synonym)

        Calculates the value of a 32-bit octal expression and displays
        the result in octal, decimal, ASCII and radix-50.  The operators
        are */+-, unary +-, and (), with the usual precedence.  Numbers
        are either octal digit strings, or decimal if they contain 8 or
        9 or end in ".", or radix-50 triplets if preceded by "^R", or
        general register contents if the names R0-R5 are given (with a
        "'" suffix to indicate the other register set) or SP or PC, R$
        or PS means the process status word, and something of the form
        "'a" means the ASCII value of a.


        DEASSIGN ddu:

        Disables the specified DL11 port (TTn:)  or LP11 port (LPn:).
        Deassigning TT0:  is not allowed (either explicitly, or
        implicitly by ASSIGNing its PC device to another PDP-11 device).


        DEPOSIT addr val

        Deposits the word <val> at absolute 18-bit address <addr>, which
        is forced even.  An error message is returned if an attempt is
        made to access a nonexistent CSR in the I/O page.


        EXAMINE addr

        Examines the word at absolute 18-bit address <addr>, which is
        forced even.  An error message is returned if an attempt is made
        to access a nonexistent CSR in the I/O page.


        FPREGISTER [r v1 v2 [v3 v4]]

        Sets or displays the FPP registers.  r is the FP accumulator
        number, 0-5, and v1-v4 are two or four 16-bit octal words to
        write in the register (sorry, no decimal).  If no arguments are
        given then the octal contents of all six ACs are given, along
        with octal displays of the FPS, FEC, and FEA, and also a
        bit-by-bit display of FPS.


        GO [addr]

        Starts the machine at the specified address, or at the address
        currently in the program counter if none is given.


        HALT

        If the machine is running, halts it and displays the registers.
        Otherwise a no op.


        HELP [command]

        Explains use of Ersatz-11 commands.  Just type "HELP" for a
        list.


        INITIALIZE

        Initializes all emulated I/O devices, disables the MMU, sets the
        CPU mode to "kernel."


        LOG ddu:  [filename]

        Logs all output to the specified character device (TTn:  or
        LPn:)  in the specified file.  If no filename is specified, any
        existing log file for that device is closed.


        LIST [addr]

        Disassembles eight instructions starting at the specified 16-bit
        address (within the current I-space map) if it is given, or
        otherwise at the first address following the last one
        disassembled by the most recent LIST or REGISTER command.


        MOUNT devu:  path/filename.ext [/switches]

        Mounts the specified DOS file on the specified PDP-11 disk drive
        (DL0:-DL3:, DM0:-DM7:, or DY0:-DY1:);  that is, PDP-11 reads and
        writes to that drive access the specified file, which is a
        byte-by-byte image of a disk, which you presumably loaded from a
        real PDP-11 using Kermit or DECnet or some equivalent, or built
        using FLX.EXE or RT11.EXE or PUTR.COM.

        For DL:, the drive is set up to emulate an RL01 or RL02
        depending on the size of the file;  each drive is set
        separately, so you can have a mix of RL01s and RL02s.  The
        /RONLY switch has the same effect as pressing the WRITE PROT
        button on a real drive (/WPROTECT is a synonym).

        For DM:  things are similar to DL:, each of the 8 drives can be
        either an RK06 or RK07 depending on the file size.  /RONLY works
        as above.

        For DY:  (DX:  is a synonym), the drive is set up to emulate an
        RX01, RX02, or RX03 disk depending on the size of the file or
        whether the /SSSD, /SSDD etc.  switch was given.  The file size
        is also used to determine whether the file is a block-by-block
        image of the PDP-11 floppy starting at logical block 0 (such as
        one gotten by using Kermit to read the disk under a PDP-11 OS),
        in which case the interleave needs to be un-done since the
        PDP-11 device handler will re-do it;  or a sector-by-sector
        image starting at track 0, side 0, sector 1.  The latter format
        yields a slightly larger file because the PDP-11 floppy device
        handlers skip track 0 (something to do with proposed ANSI
        compatibility that never materialized as far as I know).

        A second option for DY:  is to give the name of a 1.2MB floppy
        drive instead of the name of a DOS image file, i.e.  A:  or B:.
        Accesses to that RX02 unit will be redirected to the specified
        floppy drive (and there's no need to re-MOUNT the drive when you
        change disks) using a 26-sector format equivalent to that of a
        real 8" disk drive.  In fact, if you somehow connect an 8" drive
        to your PC floppy controller then it should be able to handle
        RX01 media directly (I haven't had an opportunity to test this
        though).  DEC's MFM format is weird so RX02 disks wouldn't be
        compatible.  The RX211 "set density" command is implemented as a
        full format, so you can format the weird 1.2MB disks using
        FORMAT.SAV or SPEC%() or whatever you'd use on your real PDP-11.
        Two problems:  (1) On a 1.2MB 5.25" drive the index hole is in
        the same place for SS and DS media (8" drives use the index hole
        to tell them apart) so E11 decides whether to report the disk as
        double-sided by depending on the /SSxx or /DSxx switches to the
        MOUNT command (/SSDD is the default);  the program detects disk
        density changes like a real RX211 (well, more or less,
        occasionally it takes a few tries to notice a change because the
        PC controller doesn't have a "wrong density" error flag, it's
        not that simple with IBM-style MFM) but still needs to be told
        if the number of sides changes.  (2) Many, if not most, PC
        floppy controllers have broken single density modes (the PC BIOS
        is hard coded for double density so no one cares), so
        FORMAT/SINGLE or anything else to do with actual single-density
        media may not work on your PC.  FDC chips made by SMC are known
        OK (FDC37C65LJP for one, the kind that takes one 16/32MHz xtal
        and one 9.6MHz one), as are at least some by Goldstar.  In my
        testing Intel's 82077 can't write SD disks but seems to be able
        to read them with some retries;  according to the data sheets
        for the NS PC8477B (which is supposed to be compatible) this is
        because the chip requires an external pin (MFM) to be grounded
        to enable SD mode, and for normal AT use it would be reasonable
        to let it float high (required by RESET mode ID anyway) so I
        imagine that's what most designers do.

        *** IMPORTANT NOTE ***
        The simulator has no control over any caching of disk writes
        that DOS may do, so it is important that you QUIT out of the
        simulator to make sure all the pseudo-disk files get closed
        properly, rather than simply switching the computer off, after
        shutting down your PDP-11 OS.  Otherwise there is no guarantee
        that all data written to disk by the PDP-11 has really made it
        onto the DOS disk (in practice I've had no problems, but trouble
        is theoretically possible so you've been warned).  But, the
        RX211 1.2MB floppy emulation controls the hardware directly (in
        fact it even intercepts INT 13h to keep DOS's fingers out of
        things so you can't crash the machine by trying to MOUNT an
        image file located on a DOS floppy while 1.2MB floppy emulation
        is active) so as long as the PDP-11 is done with the disk it's
        OK to take it out of the drive.

        Also, the simulator has no control over "Green PC" BIOSes which
        spin down hard drives after a specified period of inactivity.
        When E11 accesses the drive after it's been shut down, the BIOS
        will pause several seconds while it spins the drive back up.
        During this period E11 is not running, so the simulated PDP-11
        may drop incoming characters (but maybe not, E11 maintains a
        small FIFO buffer on each line) and its clock will lose a few
        seconds.  If this is a problem you may have to disable this BIOS
        feature.  If anyone knows of a way for E11 to handle spinning
        the drive up asynchronously after a timeout, without confusing
        the BIOS, I'd love to hear about it, what little APM
        documentation I have appears to be wrong, at least from my
        testing (that and/or my BIOS is broken).  That way the PDP-11
        could keep running and it would just see a slow disk transfer
        once in a while.


        PROCEED [break]

        Continues PDP-11 execution at the address currently in the
        program counter.  If <break> is specified, then it is the
        virtual address of a single hard breakpoint, where the PDP-11 is
        guaranteed to stop if an instruction fetch is attempted starting
        at that address, regardless of what mode the computer is
        executing in, and regardless of whether the contents of that
        location have changed since the breakpoint was set.  This can be
        handy for tracing code that hasn't been loaded yet.  Note that
        hard breakpoints and single stepping with the STEP command
        interfere with the operation of the CPU T bit, so don't combine
        them with a debugger (or CPU traps diagnostic program) running
        on the PDP-11.


        QUIT

        Exit the simulator, closing all image and log files and
        resetting all devices that were in use.


        REGISTER [r val]

        If <r> and <val> are given, sets register <r> (0-7) in the
        current register set to contain <val>.  Otherwise displays the
        values of all eight registers, the condition codes, the current
        and previous processor modes, and the current interrupt priority
        level.  Note that the only way to set the PSW value is by
        depositing it into location 777776.


        SET CPU item [item...]

        This command changes the emulated CPU type, either by changing
        to a new model all at once, or on a feature-by-feature basis.
        SET CPU 34A sets the emulation to be 11/34a compatible, SET CPU
        35 sets it to be 11/35 compatible (mostly -- the 11/20-style
        weirdness with MOV SP,-(SP) pushing the decremented SP, etc.  is
        not emulated).  EIS and NOEIS tell whether the EIS instructions
        exist, FPP and NOFPP turn the FPP emulation on or off (it's
        permanently off if your PC has no 80x87), and MXPS and NOMXPS
        enable/disable the MFPS and MTPS instructions.

        There are many other items but they correspond to features that
        either don't exist yet (so even though they appear in SHOW CPU
        you get an error message when you try to turn them on), or
        haven't had serious testing.  If you want to try them please let
        me know how it turns out, I believe they work, but it wouldn't
        be fair to claim I'm sure, that's why this is a beta release.

        CPUERR    CPU error register.
        CSM       CSM instruction (requires SUPMODE to work).
        DSPACE    Split I/D space.
        DUALREGSET  Dual register set.
        MMTRAPS   11/45,55,70-style memory management traps, 3-bit ACF.
        PIRQ      11/45-style 7-level software interrupts.
        SPL       SPL instruction.
        SUPMODE   Supervisor mode.
        TSTSET    J-11 TSTSET, WRTLCK instructions.

        This gives you the ability to roll your own CPU, which may not
        correspond to any actual existing PDP-11 model.  This may annoy
        your OS, and changing CPU types while running will almost
        definitely startle it.  Anyway SHOW CPU will show you what
        you've done.  The list of configurable features will grow in
        future versions to include more actual PDP-11 models, this is
        just what I have now.


        SET DISPLAY NONE
        SET DISPLAY PORT n
        SET DISPLAY LPTn:

        If PORT is specified, specifies the octal 80x86 I/O address of a
        word port which when written as a word, sets the 16-bit display
        register.  Building the trivial hardware to support this is left
        as an exercise to the reader.

        If a PC LPT port name is given, it specifies a port which has a
        multiplexed LED board plugged into it, and E11 will refresh each
        half on alternate 60Hz (50Hz) clock ticks;  there's a little
        flicker but it works and requires no chips or power supply, just
        build your board so that the D0-D7 lines (pins 2-9 of the DB25)
        drive the anodes of the both the D0-7 and D8-15 LEDs (through
        the same set of eight 100 ohm resistors since only one set of
        LEDs will have their cathodes grounded at a time).  Then add two
        NPN switching transistors (2N3904 etc.)  with the emitters
        grounded (pin 25), the collectors connected to the cathodes of
        all 8 LEDs for that byte, and the bases connected through a 1K
        current limiting resistor to either /STROBE (pin 1) for the
        D0-D7 LEDs or /INIT (pin 16) for the D8-D15 LEDs.

        If NONE is specified, then the current DR value is available
        only from the SHOW DISPLAY command (the default condition).


        SET FLOPPY RX[2]11

        Sets the type of floppy controller that will be emulated.  This
        command is necessary because the RX11 and the RX211 use the same
        CSR and vector addresses, otherwise E11 could just emulate one
        of each.  The default is RX211 (with a so-called "RX03" drive);
        the RX11 is inferior in every way to the RX211 (and probably
        doesn't work with your floppy controller anyway so you'll be
        stuck with image files) so normally you wouldn't use this
        command, but if you're trying to boot something that expects an
        RX11 (e.g.  an RT-11 distribution with RX01 boot blocks) you'll
        need this command since the RX211 is not software-compatible
        with the RX11 (although it's very similar).


        SET HERZ {50 | 60}

        Sets the frequency of the KW11L line clock (startup default is
        60);  Ersatz-11 reprograms the PC timer chip for this rate to
        simulate line time clock interrupts, and then maintains a count
        in software so that it knows when to trigger BIOS 18.2 Hz
        interrupts (there is some jitter due to the BIOS interval being
        rounded down to the previous KW11L interrupt, but there is no
        cumulative error so the DOS clock is still correct when you exit
        out of E11).


        SET KEYBOARD [NO]SWAP

        SWAP sets the keyboard handler to exchange the functions of the
        Caps Lock and left Ctrl keys for people who (understandably)
        don't like the IBM Enhanced Keyboard.  NOSWAP sets the handler
        back so that the keys work as marked.


        SET [NO]SCOPE

        Sets whether the console terminal is a scope or a hardcopy
        terminal, for the purpose of handling rubout characters typed at
        the "E11>" prompt.  Mainly useful if the console is redirected
        to a COM port with a DECwriter (etc.)  plugged into it.


        SET SCROLL {HARD | SOFT}

        Selects the mechanism used for video scrolling.  HARD scrolling
        offers superior performance (it works by programming the video
        board(s) to change the start address of the screen each time a
        full-screen scroll is needed), but exposes a bug in the DOS box
        of a certain GUI system.  SOFT scrolling does things the slow
        obvious way, by copying the whole screen a line up on each line
        feed, and ought to work with anything.  HARD scrolling is the
        default;  you should try putting SET SCROLL SOFT in your E11.INI
        file if your display goes nuts a screen or so into each
        attempted E11 session.


        SET SWITCH n
        SET SWITCH PORT n

        If PORT is specified, specifies the octal 80x86 I/O address of a
        word port which when read as a word, gives the current 16-bit
        switch register value.  Otherwise (PORT not specified), sets the
        value of the emulated SR to the octal number n.


        SET TTn:  CSR=nnnnnn VECTOR=nnn

        Sets the octal CSR and/or vector addresses for the specified
        DL11 port (values will be saved for use when the port is created
        using ASSIGN if it doesn't currently exist, otherwise effect is
        immediate).


        SHOW CPU

        Shows emulated CPU type, along with breakdown of features.


        SHOW MMU [ {KERNEL | SUPERVISOR | USER} [INSTRUCTION | DATA] ]

        If the MMU is enabled, shows the current mapping for the
        specified space.  Defaults are kernel and instruction space.


        SHOW ddu:

        Shows the configuration of the specified device;  this is the
        function key or COM port, CSR and vector if it's a DL11 or LP11
        port, or the disk type and write protect flag for disks.


        STEP

        Executes a single instruction step and displays the updated
        registers.

        HISTORY:

        V0.8 BETA, 29-Mar-1994;  initial release.

        V0.9 BETA, 05-Jul-1994;  many bug fixes (mainly trap handling,
        MMU emulation, DIV instruction, and VT100 reverse video), added
        RX211 emulation, multiple DL11s, and 50 Hz KW11L mode.

        V1.0 BETA, 14-Nov-1994;  more bug fixes, added FP11A,
        RK611/RK06-07, LP11, D-space, and supervisor mode emulation.
        Also CALC, HELP, INIT, LOG, SET/SHOW CPU, SET DR LPTn:, SET
        SCROLL, SHOW MMU commands, VT100 graphics/underline, changed to
        .EXE file (ran out of space in unified code/data segment in .COM
        file).



        NOTES:

        This program is dedicated to RSTS V7.0-07 Digby's Bitpile.
        Ad Majorem Digby Gloriam.

        INTERRUPTS:
        The interrupt system ended up having to be a little weird, due
        to some shameful assumptions in DEC OSes (mainly RSX and RT-11
        SJ) about how many instructions are guaranteed to be executed
        after writing a command to a device CSR, before the device will
        complete the operation and interrupt.  Since MS-DOS doesn't
        support asynchronous I/O (unless you go to extremes which
        wouldn't have made sense in a CPU hog like an instruction set
        simulator), it's natural to have all emulated device I/O appear
        to the PDP-11 to be instantaneous (not really, the PC takes a
        break between PDP-11 instructions to do the transfer), with the
        completion interrupt occurring on the instruction following the
        one that started the transfer.  Unfortunately this catches some
        OS code with its pants down;  in my testing, RSX appeared to
        issue WAIT instructions for TTY output which was assumed not to
        have completed yet a few dozen instructions after writing a
        character to a DL11 (thus hanging the system), and similarly the
        RT-11 SJ (but not FB/XM) keyboard interrupt service routine runs
        with interrupts enabled on the assumption that another keyboard
        interrupt couldn't possibly happen before the current ISR
        finishes (when this does happen the ISR recurses and the
        characters are put in the buffer in reverse order, which was
        happening with VT100 keypad keys in E11).  My solution to these
        problems was to put in a queueing system, so that the interrupt
        (and in some cases the transfer itself) doesn't occur until a
        set number of instruction fetches (which in most cases I set on
        the order of hundreds) after the instruction that started the
        transfer.  This slightly slows down I/O, and at some point I may
        add commands to make each of the delays settable, for tuning in
        cases where my hard-coded delays turn out not to be enough, or
        cases of "clean" code which makes no assumptions in which case
        things can be sped up by setting the all delays to 1.  I'd be
        interested to see how these OSes handle really fast serial lines
        on actual slow PDP-11s.  All of this applies to disks too,
        although I haven't run into any cute problems yet of code that
        executes within a buffer that a disk is reading to and counts on
        the CPU's ability to "outrun" the disk and JMP out in time;  but
        just to be safe the disk code delays actually doing the transfer
        until it's about to post the interrupt anyway.  RK06/07 seek
        attentions are delayed still further beyond acknowledging the
        seek command so as not to confuse overlapped seek drivers;
        however you'll get faster results using a non-overlapped driver
        if one is supplied with your OS.  Since usually all your
        emulated disks are on one physical DOS disk with one head
        carriage, there's nothing to overlap anyway.

        KEYBOARD:
        The keypad layout may take a little getting used to but it's
        intended to be familiar if your fingers are already comfortable
        using KED or EDT on a real VT100;  just don't look at it.  The
        digits and '.' key work as marked in Num Lock mode (otherwise
        only the arrows work).  The keys around the top and right edges
        of the keypad are *not* as marked, but correspond to the
        PF1-PF4, hyphen, comma, and ENTER keys of the VT100 (the comma
        key is missing unless you have an 84-key AT keyboard;  Northgate
        Omnikey 102 keyboards have an = key where the VT100 comma
        belongs but unfortunately it transmits the same scan code as the
        =/+ key on the main keyboard so E11 can't use it as a comma).
        To get the normal function of the Num Lock key (and Esc, Scroll
        Lock, and Sys Req on an 84-key AT keyboard), press Alt, Ctrl, or
        Shift at the same time.  The keypad hyphen, comma, ENTER, and
        period keys are also available as F6, F8, F10, and F9 keys.

        DISK IMAGES:
        Getting a snapshot of a bootable disk for your OS into a huge
        DOS file is Your Problem, I don't want to get involved in
        pirating software from a company whose legal department is
        probably bigger than any *company* I've ever worked for.  BTW,
        my local (Albany, NY) DEC office has no conceptual problem with
        selling a real license for a PDP-11 that doesn't really exist.
        Anyway I used Kermit to slurp the disk images out of a real
        PDP-11, and I've heard of people using Process Software TCP/IP
        with a live PDP-11, or DECnet and Pathworks, or Mark Aitchison's
        RT11.EXE (a fine program) with an RX50 distribution kit.  Paul
        Koning (former RSTS developer) has written a very nice program
        named "flx" for manipulating files in RSTS disk images, among
        other things it can build a bootable disk given the files from
        [0,1].  It's available from FTP.UPDATE.UU.SE in
        pub/pdp11/rsts/utils/flx and is written in portable C, so it can
        be used with any emulator (or with real disk packs on a VAX).  A
        DOS executable is included with the sources.  I'm working on a
        separate utility program to manipulate DEC file systems, stay
        tuned if you care but don't hold your breath, it's gotten
        somewhat out of hand with frivolous features that have delayed
        my finishing the useful ones.

        *** WATCH OUT ***
        The RT-11 DL:  and DM:  device handlers expect to find a bad
        block replacement table in block 1 of a disk.  If something else
        is there (like the pack label in Files-11 and RDS 1.1 and later,
        or the MFD in RDS 0.0), they will replace blocks at random and
        you'll get a corrupted disk image (yes, I'm sure :-).  So either
        hack your Kermit (etc.)  to use the appropriate .SPFUN instead
        of .READ, or don't use RT-11 to read non-RT-11 disks.

        HOST SYSTEMS:
        "Why didn't you write a version to run on the {machine} under
        {OS}?"  The program is written entirely in 80x86 assembly
        language (over 21,000 lines);  porting the devices, debugger,
        interrupt system etc.  to another architecture would be
        straightforward but the instruction set processor depends
        heavily on similarities between the 80x86 and the PDP-11 (most
        notably byte order and the condition flags;  correcting the byte
        order and/or deriving condition flags "by hand" on another
        machine would be very inefficient).  The FP11 simulation
        likewise relies heavily on the 80x87 data formats.  Also the
        VT100 emulator gets pretty intimate with the video hardware.  So
        it seems a little unreasonable for you to ask me to spend months
        MORE for no pay, writing the whole thing over again for your
        machine, just to save you paying a couple of hundred bucks for
        some cheesy mono 486DLC machine if you don't already have one.
        Of course, if someone with a financial interest in keeping
        PDP-11 code alive at above full speed wants to donate an Alpha
        or PowerPC system to motivate me to port the whole mess to it,
        that's another story!

        Meanwhile, if what you want is a UNIX-based PDP-11 emulator in
        C, three (or more?)  have already been released, by Bob Supnik
        of DEC (J-11, in /pub/mbg/simulators on FTP.STD.COM), Eric
        Edwards of RIT (11/40?  /pub/csh/mag/pdp.tar.Z on
        FTP.CSH.RIT.EDU) and der Mouse of McGill (FP-less J-11?
        /pub/people/mouse/pdp11 on FTP.CIM.MCGILL.CA).  You'll need a
        faster machine to get the same results.

        SOURCES:
        At this time I am not making a public release of the source
        code, because it contains proprietary code from a possible
        forthcoming commercial product.  Also the program is changing
        rapidly and I like having all the bugs where I can see them.

        COPYRIGHT NOTICE:
        Ersatz-11 is Copyright (C) 1994 by John Wilson.  All rights
        reserved.  Distribution of this document and/or the E11.EXE
        executable file, in unmodified form, without charge, is allowed
        without restriction.  Anything else is strictly forbidden unless
        you contact me to work something out first.

        ACKNOWLEDGMENTS:
        That should cover most of the important stuff.  A lot of stuff
        has gone right since the initial beta release, mostly thanks to
        input either from people who have experience with PDP-11
        emulation (Bob Supnik at DEC and Alan Sieving at QED), or from
        people who have helped me debug Ersatz-11 with their
        configuration (many people, Frank Borger's (U.  Chicago) efforts
        with RT-11SJ and IAS have been particularly impressive, as have
        Paul Koning's (Chipcom) insights into RSTS).

        FEEDBACK:
        I would really appreciate continued feedback on the program,
        good and bad;  bad news is usually more useful (I'm very eager
        to fix bugs, but I have to find them first), but I'm always
        happy to hear that things work right too, especially if you've
        gotten it working with an OS that hasn't been tried before, or
        if you've found a novel way to bootstrap a PDP-11 OS onto your
        PC.  Also I'd be very interested in hearing suggestions for
        improvements (besides the obvious 22-bit addressing).

        AS ALWAYS, MAKE A BACKUP OF ANYTHING YOU'D REGRET LOSING BEFORE
        RUNNING THIS PROGRAM.  Yeah I know you won't (I didn't) but
        think about how you'll feel if something important gets
        destroyed...  Anyway once you're set up it's a nice change being
        able to throw a couple of dozen RL02 images on a QIC-80 tape for
        safekeeping, might as well do your other data the same favor.


        John Wilson
        11 Bank Street
        Troy, NY  12180
        USA
        +1 (518) 271-1982
        
        wilsonj@rpi.edu
        John_Wilson@MTS.RPI.EDU  (if RPI.EDU is in AFS never-never land)
        USERHA8G@RPITSMTS.BITNET (if *you're* in never-never land)